MANUAL ON DETAILED

TECHNICAL SPECIFICATIONS FOR

##### THE VDL MODE 4 DIGITAL LINK

PART II

ENGLISH ONLY

TABLE OF CONTENTS

1. SECTION  LINK LAYER PROTOCOLS AND SERVICES	8

1.1 GENERAL INFORMATION	8

1.1.1 Functionality	8

1.1.2 Services	8

1.1.2.1 Connection-oriented	8

1.1.2.2 Connectionless	8

1.1.3 Acronyms, abbreviations and parameter symbols	8

1.2 MAC SUBLAYER	15

1.2.1 MAC sublayer services	15

1.2.2 MAC sublayer parameters	16

1.2.2.1 Parameter M1 (number of slots per superframe)	16

1.2.2.2 Parameter M2inc and M2limit (MAC layer control parameters for network entry)	16

1.2.3 Time synchronization	17

1.2.3.1 Primary	17

1.2.3.2 Secondary	17

1.2.3.3 Alignment to UTC second	18

1.2.3.4 Tertiary	18

1.2.3.5 Data quality level	18

1.2.4 Slot idle/busy notification	18

1.2.4.1 Slot idle detection	18

1.2.4.2 Slot busy detection	18

1.2.4.3 Slot occupied detection	18

1.2.5 Transmission processing	19

1.2.6 Received transmission processing	19

1.3 VSS SUBLAYER	19

1.3.1 Services	19

1.3.1.1 Multiple access	19

1.3.1.2 Error detection	20

1.3.1.3 Channel congestion	20

1.3.2 Burst format	20

1.3.2.1 Version number	21

1.3.2.2 Source address	21

1.3.2.3 Message ID	22

1.3.2.4 Information field	23

1.3.2.5 Reservation fields	23

1.3.2.6 Autonomous/directed flag	23

1.3.3 VSS sublayer parameters	24

1.3.3.1 Parameter VS1 (number of ground quarantined slots)	25

1.3.3.2 Parameter VS2 (minimum CCI performance)	25

1.3.3.3 Parameter VS4 (quarantine slot re-use range)	25

1.3.3.4 Parameter VS5 (maximum burst length)	25

1.3.4 VSS quality of service parameters	25

1.3.4.1 Parameter Q1 (priority)	26

1.3.4.2 Parameters Q2a to Q2d (slot selection range constraint for level n)	27

1.3.4.3 Parameter Q3 (replace queued data)	27

1.3.4.4 Parameter Q4 (number of available slots)	27

1.3.4.5 Parameters Q5 (VSS retransmission parameters)	27

1.3.5 Received transmission processing	27

1.3.6 Reserved access protocol specification	28

1.3.6.1 Reservation table	28

1.3.6.2 Selecting slots for transmission or reservation	28

1.3.6.3 Reserved transmissions	31

1.3.6.4 Ground quarantine	31

1.3.6.5 Reservation conflicts	32

1.3.6.6 Transmission conflicts for mobile stations	33

1.3.7 Random access protocol specification	34

1.3.7.1 Random access parameters	34

1.3.7.2 Random access procedures	35

1.3.8 Fixed access protocol specification	36

1.3.8.1 Recommendation	36

1.3.9 Null reservation protocol specification	36

1.3.9.1 Null reservation burst format	36

1.3.10 Periodic broadcast protocol specification	37

1.3.10.1 Periodic broadcast reservation burst format	37

1.3.10.2 Periodic broadcast timers	37

1.3.10.3 Periodic broadcast parameters	38

1.3.10.4 Periodic broadcast reception procedures	38

1.3.10.5 Periodic broadcast transmission procedures	39

1.3.11 Incremental broadcast protocol specification	42

1.3.11.1 Incremental broadcast reservation burst format	42

1.3.11.2 Incremental broadcast parameters	43

1.3.11.3 Incremental broadcast reception procedures	44

1.3.11.4 Incremental broadcast transmission procedures	44

1.3.12 Combined periodic broadcast and incremental broadcast protocol specification	44

1.3.12.1 Combined periodic broadcast and incremental broadcast reservation burst	45

1.3.13 Big negative dither (BND) broadcast protocol specifications	45

1.3.13.1 BND reservation burst format	45

1.3.13.2 BND broadcast parameters	46

1.3.13.3 BND broadcast reception procedures	46

1.3.13.4 BND broadcast transmission procedures	46

1.3.14 Unicast request protocol specification	46

1.3.14.1 Unicast request reservation burst format	46

1.3.14.2 Unicast request parameters	47

1.3.14.3 Unicast request reception procedures	48

1.3.14.4 Unicast request transmission procedures	49

1.3.15 Information transfer request protocol specification	50

1.3.15.1 Information transfer request reservation burst format	50

1.3.15.2 Information transfer request parameters	51

1.3.15.3 Information transfer request reception procedures	52

1.3.15.4 Information transfer request transmission procedures	52

1.3.15.5 Information transfer request acknowledgement procedures	53

1.3.16 Directed request protocol specification	53

1.3.16.1 Directed request reservation burst format	53

1.3.16.2 Directed request parameters	58

1.3.16.3 Directed request reception procedures	58

1.3.16.4 Directed request transmission procedures	60

1.3.16.5 Directed request response procedures	61

1.3.17 Block reservation protocols specification	62

1.3.17.1 Superframe block reservation burst format	62

1.3.17.2 Second frame block reservation burst format	64

1.3.17.3 Superframe block reservation parameters	64

1.3.17.4 Superframe block reservation reception procedures	65

1.3.17.5 Second frame block reservation parameters	68

1.3.17.6 Second frame block reservation reception procedures	68

1.3.17.7 Superframe block reservation transmission procedures	69

1.3.17.8 Rebroadcast request superframe block reservation response procedures	70

1.3.17.9 Second frame block reservation transmission procedures	70

1.3.18 Response protocol specification	70

1.3.18.1 Response burst format	70

1.3.19 General request protocol specification	71

1.3.19.1 General request burst format	71

1.3.19.2 General request procedures	71

1.3.20 General response protocol specification	72

1.3.20.1 General response burst format	72

1.3.20.2 General response procedures	74

1.3.21 Retransmission procedures	74

1.4 DLS SUBLAYER	75

1.4.1 Services	75

1.4.1.1 Data transfer	75

1.4.1.2 DATA DLPDU duplicate suppression and sequencing	76

1.4.1.3 Error detection	76

1.4.1.4 Station identification	76

1.4.1.5 Broadcast addressing	76

1.4.1.6 DLS Priority	76

1.4.1.7 DLS link control DLPDUs	76

1.4.2 DLS protocol specification	77

1.4.2.1 State Variables	77

1.4.2.2 Station address encoding	77

1.4.2.3 DLS burst formats	79

1.4.3 DLS system parameters	81

1.4.3.1 Parameter TD1 (ZOCOP transmit reset timer)	82

1.4.3.2 Parameter TD2 (ZOCOP receive reset timer)	82

1.4.3.3 Parameter ND1 (maximum number of octets of any user data packet)	82

1.4.3.4 Parameter ND2 (maximum length of DLS transmission)	82

1.4.3.5 Parameter ND3 (maximum length of fragment)	82

1.4.4 DLS procedures	82

1.4.4.1 Broadcast	83

1.4.4.2 Setting of re-transmission parameter	83

1.4.4.3 Selection of user data packet for transmission	83

1.4.4.4 Selection of transmission procedures	85

1.4.4.5 Short transmission procedures	85

1.4.4.6 Long transmission procedures	87

1.4.4.7 DLS not supported	90

1.4.4.8 No link with sender	91

1.4.4.9 User data packet reception	91

1.4.4.10 Receipt of ACK DLPDU	91

1.4.4.11 Link reset	92

1.4.4.12 Linking DLS DLPDU transmissions	92

1.4.4.13 CTRL DLPDU	93

1.4.4.14 Procedures for air-air communication	93

1.5 LINK MANAGEMENT ENTITY SUBLAYER	94

1.5.1 Services	94

1.5.1.1 Link provision	94

1.5.1.2 Link change notifications	94

1.5.2 Synchronization burst format	94

1.5.2.1 Fixed and variable data fields	94

1.5.2.2 Fixed data field format	95

1.5.2.3 Variable data field format	99

1.5.2.4 Synchronization burst request	99

1.5.2.5 CTRL frame	99

1.5.2.6 Broadcast link management frame	100

1.5.3 Control (CTRL) parameter formats	101

1.5.3.1 Encoding	101

1.5.3.2 VDL Mode 4 parameter identification	101

1.5.3.3 General purpose information parameters	102

1.5.3.4 Mobile-initiated information parameters	105

1.5.3.5 Ground-initiated modification parameters	107

1.5.3.6 Ground-initiated information parameters	112

1.5.4 LME timers and parameters	117

1.5.4.1 Counter L1 (maximum number of missed reservations) and Timer TL3 (inter-miss timer)	118

1.5.4.2 Timer TL1 (maximum link overlap time)	118

1.5.4.3 Parameters TL2 (link initialization time)	118

1.5.5 LME procedures	118

1.5.5.1 Synchronization burst procedures	119

1.5.5.2 Peer entity contact Table (PECT)	120

1.5.5.3 Network entry protocol specifications	120

1.5.6 CTRL frame types and procedures	127

1.5.7 CTRL transmission procedures	131

1.5.7.1 Frequency management procedures	131

1.5.7.2 Link connectivity procedures	131

1.5.7.3 Ground station identification	131

1.5.7.4 Link establishment	132

1.5.7.5 Mobile-initiated handoff	132

1.5.7.6 Mobile-requested ground-initiated handoff	134

1.5.7.7 Ground-based initiated handoff	134

1.5.7.8 Ground-based requested mobile-initiated handoff	135

1.5.7.9 Ground-based requested broadcast handoff	136

1.5.7.10 Ground-based commanded autotune	136

2. SECTION  VDL MODE 4 MOBILE SUBNETWORK DEPENDENT CONVERGENCE FUNCTION (SNDCF)	138

3. SECTION  ADDITIONAL MATERIAL FOR ADS-B APPLICATIONS	139

3.1 INTRODUCTION	139

3.2 ACRONYMS, ABBREVIATIONS AND PARAMETER SYMBOLS	139

3.3 INFORMATION FIELD FORMATS	141

3.4 ADS-B REQUEST	154

3.4.1 ADS-B request format	154

3.4.2 Sleep mode	154

3.4.3 Automatic selection of variable information fields	155

3.5 DEFAULT ADS-B REPORTING	157

3.6 ADS-B PROCEDURES	158

3.7 CTRL PARAMETERS	159

3.7.1 Directory of service (DOS) message	159

3.7.2 Channel management CTRL Parameter	159

3.7.2.1 Header block encoding	160

3.7.2.2 Destination block encoding	163

3.7.2.3 Channel management parameter reception procedures	166

3.7.2.4 Cancellation of channel management CTRL command	168

3.7.2.5 Cancellation of autonomous streams	168

3.7.2.6 Transmission block encoding	169

3.7.2.7 Frequency block encoding	171

3.7.2.8 Transmission parameter block definition	171

3.7.2.9 Script block definition	172

4. SECTION  DEFINITIONS FOR COMPACT POSITION REPORTING	174

4.1 INTRODUCTION	174

4.2 PARAMETER SYMBOLS, DATA TYPES, CONSTANTS AND VARIABLES	174

4.2.1 Parameter symbols	174

4.2.2 Data Types	174

4.2.3 Constants	174

4.2.4 Variables	174

4.2.5 Functions	177

4.2.6 Patch constants	179

4.2.6.1 Transition table	179

4.2.6.2 Patch size functions	181

4.3 FIXED DATA FIELD POSITION ENCODING	181

4.3.1 General	181

4.3.2 Input parameters	181

4.3.3 Calculations	181

4.3.3.1 Latitiude	181

4.3.3.2 Longitude	181

4.4 FIXED DATA FIELD POSITION LOCAL DECODING	182

4.4.1 General	182

4.4.2 Input parameters	182

4.4.3 Calculations	182

4.4.3.1 Supporting Function	182

4.4.3.2 Latitude	182

4.4.3.3 Longitude	183

4.5 FIXED DATA FIELD POSITION GLOBAL DECODING	183

4.5.1 General	183

4.5.2 Input parameters	184

4.5.3 Transition level straddling	184

4.5.4 Calculations	184

4.5.4.1 Latitude	184

4.5.4.2 Longitude	184

4.6 INFORMATION FIELD OFFSET ENCODING	185

4.6.1 General	185

4.6.2 Input parameters	185

4.6.3 Calculations	185

4.6.3.1 Supporting functions	185

4.6.3.2 Latitude	185

4.6.3.3 Longitude	186

4.7 INFORMATION FIELD OFFSET DECODING	186

4.7.1 General	186

4.7.2 Input parameters	186

4.7.3 Calculations	187

4.7.3.1 Latitude	187

4.7.3.2 Longitude	187

4.8 PATCH ID ENCODING	188

4.8.1 General	188

4.8.2 Input parameters	188

4.8.3 Calculations	188

4.9 PATCH ID DECODING	188

4.9.1 General	188

4.9.2 Input parameters	188

4.9.3 Calculations	188

4.9.3.1 Latitude	188

4.9.3.2 Longitude	189

4.10 POSITION REPORT PROCESSING	189

4.10.1 Services	189

4.10.2 Position report parameters	189

4.10.2.1 Parameter TR1 (maximum age for use in global decode)	189

4.10.2.2 Parameter TR2 (maximum time between global updates)	189

4.10.3 Position report processing procedures	189

4.10.3.1 Position report processing state machine	190

4.10.3.2 Position report processing state machine transitions	190

4.10.3.3 State machine transitions for transition level straddling	192

SECTION  LINK LAYER PROTOCOLS AND SERVICES

GENERAL INFORMATION

Functionality

Note.— The VHF digital link (VDL) Mode 4 link layer is divided into four sublayers:

a)	media access control (MAC) sublayer requiring the use of time division multiple access (TDMA);

b)	a VDL Mode 4 specific services (VSS) sublayer providing communication using a flexible burst format and associated transmission and reservation protocols over the MAC sublayer;

c)	a data link service (DLS) sublayer providing connection-oriented and broadcast services over the VSS sublayer;

d)	a link management entity (LME) which establishes and maintains connections.

Services

Connection-oriented

The VDL link layer shall provide a reliable point-to-point service using a connection-oriented DLS sublayer.

Connectionless

The VDL link layer shall provide an unacknowledged broadcast service using a connectionless DLS sublayer.

Acronyms, abbreviations and parameter symbols

Note 1.—  The following terms relating to VDL Mode 4 are used in this document as they are defined below.

Autotune Function.  This function, performed by the Link Management Entity, allows a ground VDL Mode 4 station to command an aircraft to change the operating characteristics of synchronization burst transmissions.

# Burst length.  The number of slots across which the VDL Mode 4 burst is transmitted.

Delayed Burst.  A VDL Mode 4 burst that begins sufficiently after the beginning of a slot so that the transmitting VDL Mode 4 station is confident that no other VDL Mode 4 station that it could receive from and is within the guard range is transmitting in the slot.  The delayed VDL Mode 4 burst terminates by the end of the slot in which it began (its length is shortened to ensure completion by the nominal time).

Primary Time Source.  The normal operation timing mode in which a VDL Mode 4 station maintains time synchronization to Universal Coordinated Time (UTC) second.

Secondary Time Source.  A timing source used in a failure mode, which applies when the primary time source fails, in which a VDL Mode 4 station maintains time synchronization to UTC second.

VDL Mode 4 Station Address.  A 27-bit identifier used to uniquely identify a VDL Mode 4 station.

Note 2.— A combination of the 24-bit ICAO aircraft address plus 3 additional bits may be used to identify aircraft.

Superframe.  A group of slots that span a period of one minute.  The start of the current superframe is aligned with the start of the slot that is currently being used for transmission.  The next superframe starts one minute after the current slot.

Synchronization burst (or “sync” burst). A VDL Mode 4 burst which announces, as a minimum, existence and position.

Tertiary Time Source.  A timing source used in a failure mode, which applies when the primary and secondary time sources fail, in which a VDL Mode 4 station maintains time synchronization to an estimate of the mean slot start times of a set of VDL Mode 4 stations.

Note  3.— The following acronyms and abbreviations are introduced in this Section as they are defined below. Other acronyms, abbreviations and parameter symbols have been listed in previous sections of these SARPs.

| Acronym | Description |
| --- | --- |
| A/A AVLC | Air/Air Aviation VHF link control |
| A/G | Air/Ground |
| ATS | Air Traffic Services |
| BND | Big negative dither |
| CPR | Compact position reporting |
| CRC | Cyclic redundancy check |
| DLPDU | Data Link Protocol Data Unit |
| DLS | Data Link Service |
| DM | Disconnected mode (frame) |
| DME | Distance measuring equipment |
| DOS | Directory of Service |
| FRMR | Frame reject (frame) |
| GBAS | Ground based augmentation system |
| GNSS | Global navigation satellite system |
| GSIF | Ground station information frame |
| hex | Hexadecimal |
| HPL | Horizontal protection limit |
| IA5 | The character set defined in ISO 646 Table 5 |
| ICAO | International Civil Aviation Organisation |
| INFO | Information (frame) |
| ISO | International Standardization Organization |
| LME | Link Management Entity |
| N/A | Not Applicable |
| NPA | Non-precision approach |
| NSCOP | Network Setup Connection Oriented Protocol |
| PECT | Peer entity contact table |
| QoS | Quality of service |
| RNP | Required navigation performance |
| RR | Receive ready (frame) |
| RTS | Request to send (burst) |
| SBAS | Spaced-based augmentation system |
| SNDCF | Subnetwork Dependent Convergence Function |
| SPS | Standard positioning service |
| SREJ | Selective reject (frame) |
| SZOM | Start Zero Overhead Mode (frame) |
| TCP | Trajectory Change Point |
| UA | Unnumbered acknowledge |
| UI | Unnumbered information (frame) |
| UN | United Nations |
| VME | VDL Mode 4 Management Entity |
| WGS | World geodetic system |
| ZOCOP | Zero Overhead Connection-Oriented Protocol |

Note 4.— The following are the symbols for parameters, timers, and counters that are introduced in this Section as they are defined below.

Table 1-1. Parameters, timers and counters for link layer protocols and services

| Parameter | Name | Section or table defined in |
| --- | --- | --- |
| CG1 | CG1 filter | Table 1-94 |
| CG1_decay | Decay rate for CG1 filter | Table 1-92 |
| CG1_inc | Digital filter increment when a synchronization burst from a previously unknown station is detected | Table 1-92 |
| CG1_limit | Digital filter threshold which triggers network entry due to station being “exposed” | Table 1-92 |
| CG1_plea | Minimum pool size of peer stations for Plea | Table 1-92 |
| CG1_range | Range limit used in digital filter for “exposure” determination | Table 1-92 |
| CG1_reach | Maximum unreachability time | Table 1-92 |
| L1 | Maximum number of missed reservations | 1.5.4.1 |
| M1 | Number of slots per superframe | 1.2.2.1 |
| M2inc | Filter increment for receiver blocking check | 1.2.2.2 |
| M2limit | Filter threshold for receive blocking check (network entry) | 1.2.2.2 |
| ND1 | Maximum number of octets in any user data packet | Table 1-58 |
| ND2 | Maximum length of DLS transmission | Table 1-58 |
| ND3 | Maximum length of fragment | Table 1-58 |
| P | Persistence | 1.3.7.1.2 |
| Q1 | Priority | 1.3.4.1 |
| Q2a – d | Slot selection range constraint for level n | 1.3.4.2 |
| Q3 | Replace queued data | 1.3.4.3 |
| Q4 | Number of available slots | 1.3.4.4 |
| Q5 | VSS retransmission parameters | 1.3.4.5 |
| Q5min | VSS retransmission parameters | 1.3.4.5 |
| Q5max | VSS retransmission parameters | 1.3.4.5 |
| Q5mult | VSS retransmission parameters | 1.3.4.5 |
| Q5exp | VSS retransmission parameters | 1.3.4.5 |
| Q5num | VSS retransmission parameters | 1.3.4.5 |
| Q5wait | VSS retransmission parameters | 1.3.4.5 |
| TD1 | ZOCOP link transmit reset timer | Table 1-58 |
| TD2 | ZOCOP link receive reset timer | Table 1-58 |
| TL1 | Maximum link overlap time | Table 1-88 |
| TL2 | Link initialization time | Table 1-88 |
| TL3 | Inter-miss timer | Table 1-88 |
| TG6 | Maximum delay for plea response | Table 1-92 |
| TG7 | Minimum time delay for CG1 filter | Table 1-92 |
| TM2 | Channel busy timer | 1.3.7.1.1 |
| TV11 | Reservation hold time | 1.3.10.2.1 |
| TV11min | Reservation hold timer minimum value | 1.3.10.3.1 |
| TV11max | Reservation hold timer maximum value | 1.3.10.3.1 |
| TV61 | Second frame block reservation timeout | 1.3.17.5.1 |
| V11 | Nominal periodic rate | 1.3.10.3.2 |
| V12 | Periodic dither range | 1.3.10.3.3 |
| V21 | Nominal incremental period | 1.3.11.2.1 |
| V22 | Maximum incremental dither range | 1.3.11.2.2 |
| V32 | Minimum response delay | 1.3.14.2.1 |
| V33 | Maximum response delay | 1.3.14.2.2 |
| V34 | Source/destination control | 1.3.14.2.3 |
| V35 | Broadcast control | 1.3.14.2.4 |
| V36 | Length of reserved block | 1.3.14.2.5 |
| V42 | Length of information transfer | 1.3.15.2.1 |
| V43 | Minimum information transfer delay | 1.3.15.2.2 |
| V44 | Maximum information transfer delay | 1.3.15.2.3 |
| V45 | Minimum response delay | 1.3.15.2.4 |
| V46 | Maximum response delay | 1.3.15.2.5 |
| V52 | Minimum response delay | 1.3.16.2.1 |
| V61 | Superframe block start offset | 1.3.17.3.1 |
| V62 | Superframe block length | 1.3.17.3.2 |
| V63 | Superframe block repeat rate | 1.3.17.3.3 |
| V64 | Superframe block re-broadcast request | 1.3.17.3.4 |
| V65 | Superframe block re-broadcast offset | 1.3.17.3.5 |
| V66 | Second frame block size | 1.3.17.5.2 |
| V67 | Second frame block repeat rate | 1.3.17.5.3 |
| VS1 | Number of ground quarantined slots | 1.3.3.1 |
| VS2 | Minimum co-channel interference (CCI) performance | 1.3.3.2 |
| VS3 | Maximum number of access attempts | 1.3.7.1.3 |
| VS4 | Quarantine slot re-use range | 1.3.3.3 |
| VS5 | Maximum burst length | Table 1-8 |

Note  5.— The following are the symbols for subfields and variables defined in this section.

Table 1-2. Symbols and variables for link layer protocols and services

| Parameter | Name | Section or table defined in |
| --- | --- | --- |
| a | application | Table 1-85 |
| ai | additional service information | Table 1-85 |
| aj | Additional slot j | Table 1-35 |
| a/d | Autonomous/directed flag | 1.5.5.1, Table 1-6b |
| anum | application number | Table 1-85 |
| ao | Acknowledgement offset | Table 1-30 |
| A_slot | Acknowledgement slot | 1.3.15.4.3 |
| balt | Base altitude | Table 1-66 |
| bd | Backoff delay | Table 1-53 |
| b/g | Baro/geo altitude | Table 1-66 |
| bl | Burst length | 1.3.5 |
| blg | Block length | Table 1-41 |
| bo | Block offset | Table 1-41 |
| br | Block repeat rate | Table 1-41 |
| bs | Block start | Table 1-41 |
| bt | Block timeout | Table 1-41 |
| c/r | Command/response status bit | 1.4.2.2.2 |
| cprf | CPR format even/odd | Table 1-66 |
| Ct_slot | Current transmission slot | 1.3.10.5.2 |
| d | Destination address | Table 1-27 |
| da | Data age | Table 1-66 |
| do | Directed offset | Table 1-35 |
| dt | Directed timeout | Table 1-35 |
| ent | Entry number | Table 1-85 |
| eo | Easterly offset parameter | 1.5.3.6.5 |
| erid | Extended reservation ID | Table 1-7 |
| err | Error type | Table 1-53 |
| f | Frequency | Table 1-30 |
| Ft_slot | Future transmission slot | 1.3.10.5.6 |
| Gsc | GSC flag | Table 1-85 |
| IB | Initialise bit | 1.4.2.3.7 |
| Id | Information field identity | Table 1-66 |
| id1, id2, id3… | ID extension | Table 1-66 |
| in | Information field | 1.4.2.2.1, Table 1-66 |
| io | Incremental offset | Table 1-21 |
| lat | Latitude | Table 1-66 |
| lg | Length | Table 1-27 |
| lon | Longitude | Table 1-66 |
| M | More bit | 1.4.2.3.4 |
| m2 | Measure of the uncertainty of the reservation data | 1.2.2.2 |
| mi | Message ID | 1.3.2.3 |
| nd | Negative dither | Table 1-25 |
| neg | Negotiation subfield | 1.4.2.3.8 |
| no | Northerly offset parameter | 1.5.3.6.5, Table 1-83 |
| nr | Nominal update rate | Table 1-33 |
| N_slot | Nominal slot | 1.3.10.5.1 |
| nucp | Position navigation uncertainty category | Table 1-66 |
| off | Offset to first reserved slot | Table 1-35 |
| ok | Confirm/failure flag | Table 1-53 |
| or | Override flag | Table 1-35 |
| po | Periodic offset | Table 1-16 |
| pr | Priority | Table 1-26 |
| Pr_flag | Plea response flag | 1.3.16.1 |
| prm | VSS user specific parameter | Table 1-51 |
| pt | Periodic timeout | Table 1-16 |
| rcvr | Receiver control | Table 1-35 |
| rd | Reservation data | Table 1-5 |
| re | Response expected | Table 1-71g |
| res | Reserved bit | Table 1-53 |
| rid | Reservation ID | 1.3.2.5 |
| r-mi | Requested message ID | Table 1-51 |
| ro | Response offset | Table 1-27 |
| roff | Re-broadcast offset | Table 1-41 |
| rrr | CTRL retransmission number | 1.5.3.3.3 |
| R_slot | Reserved slot | 1.3.11.4.2 |
| retrans | Number of times that a burst has been transmitted | 1.3.21 |
| S | Source address | 1.3.2.2 |
| Sss | CTRL sequence number | 1.5.3.3.3 |
| s_avail | Slot availability | 1.3.10.5.3 |
| sdf | Source/destination flag | Table 1-27 |
| si | Service information | Table 1-85 |
| sit | Service information type | Table 1-85 |
| sz | Size | Table 1-43 |
| T | Toggle bit | 1.4.2.3.3 |
| Tt | Value of Toggle bit for (current) transmitted DLPDUs | 1.4.2.1 |
| Tr | Value of Toggle bit for last received DLPDU | 1.4.2.1 |
| tc | TCP change flag | Table 1-66 |
| tfom | Time figure of merit | Table 1-66 |
| trmt | Transmit control | Table 1-35 |
| t_slot | Transmission slot | 1.3.11.4.1 |
| vc | Vertex count | Table 1-31 |
| Ver | Version number | 1.3.2.1 |
| vt | Timeout | Table 1-43 |

All division operations, unless otherwise stated, shall be integer divisions. An implied truncation shall occur after the division.

In the tables included in this document to illustrate the format of bursts, the following order is implied:

a) bit order in each burst subfield shall be indicated by subscript numbers. Bit 1 shall indicate the least significant bit; and

b) bits shall be transmitted octet by octet, starting with the first octet in each table, and within each octet the rightmost bit (as shown in the tables) shall be transmitted first.

MAC SUBLAYER

The MAC sublayer shall acquire the shared communication path so as to provide the services defined in Section 1.2.1.

Note.— This function should be “transparent” to higher functional layers, meaning that the way in which supporting communications resources are utilized to achieve this should not be visible to the higher layers and sublayers (e.g. the VSS and DLS).

MAC sublayer services

Note.— The MAC sublayer provides

a)	TDMA media access;

b)	time synchronization of the start of each time slot in the channel (Section 1.2.3);

c)	transmission (Section 1.2.5) and reception (Section 1.2.6) processing.

The MAC sublayer shall accept from the physical layer a continuous indication of channel idle/busy status (see Section 1.2.4). The MAC sublayer shall accept from the VSS sublayer a burst for transmission, accompanied by the time to transmit it. The MAC sublayer shall provide to the VSS sublayer the received burst  data, slot busy/idle status, and the status of bursts sent for transmission.

MAC sublayer parameters

MAC service system parameters shall be as described in Table 1-3.

Table 1-3. MAC service system parameters

| Symbol | Parameter Name | Minimum | Maximum | Default | Increment |
| --- | --- | --- | --- | --- | --- |
| M1 | Number of slots per superframe | 60 slots | 15360 slots | 4500 slots | 60 slots |
| M2inc | Filter increment for receiver blocking check | 1 | 256 | 2 | 1 |
| M2limit | Filter threshold for receive blocking check (network entry) | 1 | 65536 | 160 | 1 |

Parameter M1 (number of slots per superframe)

The parameter M1 shall be the number of available slots per superframe. A superframe shall span a period of 60 seconds.

Note.— M1/60 slots spans a time interval of 1 second. The M1 increment forces M1/60 to be an integer. This simplifies the protocol since a slot counter (or equivalent) can be started at the boundary between any two consecutive UTC seconds.

Parameter M2inc and M2limit (MAC layer control parameters for network entry)

Note 1.— For a station that is able to make reservations on a channel as defined in Section 1.3.6.1, the need to execute a network entry procedure, as defined in Section 1.5.6.3, as a result of temporary loss of receiving function on the channel due to known cosite transmissions, is controlled by the m2 filter.

An m2 filter shall be maintained by a station for each active channel as a measure of the uncertainty of the reservation data. Each m2 filter shall be controlled by parameters M2inc and M2limit, which define the parameters of the following algorithm in which m2 is updated after every slot:

m2k+1	= m2k + M2inc	if receiver function on the channel is blocked by own station transmission on another channel,

e.g. through a common antenna;

= max((m2k - 1), 0) 	if receiver function is not blocked.

If m2 >= M2limit, m2 shall be reset to 0 and the station shall execute a network entry procedure in accordance with Section 1.5.6.3.

Note 2.— The objective is to force re-entry when the reservation table  may have been corrupted by lack of recent reservation data, without requiring re-entry as a result of minor gaps in reception as may be caused by limited and isolated transmissions on other channels. Parameters M2limit and M2inc can be reset by ground station command on a per channel basis.

Time synchronization

Note.— Time synchronization is described as set out in the following table:

Table 1-4. Operating modes and time synchronization

| Operating mode | Synchronization mode | Data quality level | Synchronization |
| --- | --- | --- | --- |
| Normal | Primary | Certified | UTC |
|  | Primary | Non-certified | UTC |
| Failure | Secondary | Non-certified | UTC |
|  | Tertiary | Non-certified | Non-UTC |

Primary

Under normal operating conditions, a station shall maintain time synchronization such that the start of each successive group of M1/60 slots is synchronized with the start of any Universal Coordinated Time (UTC) second to within a two-sigma value of 400 ns.

Note.— This is defined as the primary time source.

Secondary

A station shall be capable of maintaining  time synchronization such that the start of each successive group of M1/60 slots is synchronized with the start of any UTC second to within a two-sigma value of 15 microseconds.

Note 1.— This is defined as the secondary time source.

Note 2.— One method is to synchronize to slot boundaries defined by a station declaring primary time.

Only when the primary source fails shall secondary time be used.

A station using secondary time shall revert to primary time whenever primary time is available.

Note 3.— Secondary time is regarded as a failure mode.

Alignment to UTC second

For stations maintaining primary or secondary time, the start of each successive group of M1/60 slots shall be aligned with a UTC second.

Tertiary

A station shall be capable of maintaining time synchronization to an estimate of the mean slot start times of a set of stations to within a two-sigma value of 20 microseconds.

Note 1.— This is defined as the tertiary time source.

When a mixture of secondary and tertiary time sources is available, the station shall derive time from the secondary time source(s) and exclude the tertiary time source(s).

Only when both the primary and secondary sources fail shall tertiary time be used.

A station using tertiary time shall: a) revert to primary time whenever primary time is available or b) revert to secondary time whenever secondary time is available and primary time is not available.

Note 2.— Tertiary time is regarded as a failure mode.

Data quality level

The certified quality level shall indicate that timing and position information provided by the station can be used by other stations as a means of deriving position information.

When a station is deriving position information from the transmissions of other stations it shall only use data from stations declaring the certified quality level.

Secondary and tertiary timing levels shall not indicate the certified quality level.

Note.— Certification of stations for use as “pseudolites” to support secondary navigation, will be under control of an authority, such as an aviation administration.

Slot idle/busy notification

Slot idle detection

A station shall consider the slot idle if the channel idle/busy status (see VDL SARPs Section 6.9.5.3) is idle at the start of the slot.

Slot busy detection

A station shall consider the slot busy if the channel idle/busy status (see VDL SARPs Section 6.9.5.3) is busy at the start of the slot.

Slot occupied detection

A slot shall be considered occupied if the channel is considered to be continuously busy for a period of at least 5 msec during the slot.

Note.— The slot occupied detection is used to monitor the operations of peer stations, including the L1 counter. This is different from the channel idle/busy state, which affects in part the station’s ability to make a random transmission.

Transmission processing

Bursts received from the MAC sublayer shall be forwarded to the physical layer, together with the time for transmission.

With the exception of certain delayed bursts, a station shall begin transmissions only at the beginning of the slot boundary as determined by its local clock. Delayed bursts shall begin 4 msec after the beginning of the slot boundary, if the channel is idle at that point.

Note.— The delay allows time for any other station to begin transmitter ramp-up, for the signal to travel the propagation distance, and for the channel busy detector to determine the appearance of a signal. A delayed burst can fit in a single slot, and preserve nominal propagation guard time, even if transmission begins late. The delay could be somewhat shorter but no longer; the 4 msec value was selected to ease design and ensure robustness of the channel busy detector.

Received transmission processing

Bursts with an invalid cyclic redundancy code (CRC) shall be discarded. Bursts with valid CRCs shall be forwarded to the VSS sublayer, along with the received time of transmission and signal quality parameters.

VSS SUBLAYER

Note 1.— There is one VSS sublayer entity for each VDL Mode 4 channel accessed by the station. The VSS sublayer provides service to the VDL Mode 4 management entity (VME) as well as the link management entities (LME) associated with other VDL Mode 4 peer systems, their associated DLEs and the DLS. The VSS is served by the MAC associated with its particular VDL Mode 4 channel.

Note 2.— This Section describes the services that bursts can provide and some example protocols and procedures, which may be amended, extended, or ignored by any specific burst application.

Note 3.— Other protocols may be defined for unique applications; however, it is expected that most bursts will use one of the below defined protocols. Regardless of this, the various reservation fields for the protocols defined below cannot be redefined.

Services

Multiple access

Note.— The VSS sublayer implements protocols to allow all stations the opportunity to transmit while providing for high system throughput, low transit delays, and low probability of collisions. These protocols include:

a)	reserved access (see Section 1.3.6):

1)	null reservation (see Section 1.3.9);

2)	periodic broadcast (see Section 1.3.10);

3)	incremental broadcast (see Section 1.3.11);

4)	combined periodic and incremental broadcast (see Section 1.3.12);

5)	big negative dither broadcast (see Section 1.3.13);

6)	unicast request (see Section 1.3.14);

7)	information transfer request (see Section 1.3.15);

8)	directed request (see Section 1.3.16);

9)	block reservation (see Section 1.3.17);

10)	response (see Section 1.3.18).

b)	random access (see Section 1.3.7); and

c)	fixed access (see Section 1.3.8).

The designation of “reserved access”, “random access” and “fixed access” apply to the protocols in the transmitting station, and not to any message indicator or flag in the transmitted frame or burst.

Error detection

The VSS sublayer shall compute a 16-bit CRC according to ISO 3309 to facilitate detection by the MAC sublayer (see Section 1.2.6) of data corruption during transmission.

Channel congestion

The VSS sublayer shall notify the LME sublayer whenever channel congestion is detected (see Section 1.3.7.1.1).

Burst format

VSS bursts shall conform to ISO 3309 frame structure except as specified in Table 1-5.

Note 1.- The maximum burst length is defined in Section 1.3.3.4.

Note 2.- A burst occupying a single slot has 24 octets of data. Thus, assigning 8 bits for bit stuffing and 2 octets for the flags, a maximum single-slot burst has a value of ‘n’ equal to 21. Note that a burst can be up toVS5 slots in length. Bursts can consist of a single block of data between two flags, as illustrated in Table 1-5, or can consist of a number of blocks of data with each block separated from the next by a flag.

Table 1-5. Burst format

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Flag | - | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 |
| Autonomous/directed flag (a/d), reservation ID (rid), version number (ver) | 1 | s27 | s26 | s25 | ver3 | ver2 | ver1 | rid | a/d |
| Source address (s) | 2 | s24 | s23 | s22 | s21 | s20 | s19 | s18 | s17 |
|  | 3 | s16 | s15 | s14 | s13 | s12 | s11 | s10 | s9 |
|  | 4 | s8 | s7 | s6 | s5 | s4 | s3 | s2 | s1 |
| Message ID (mi) | 5 | ink | mik | . . . . . . | mi4 | mi3 | mi2 | mi1 |
| Information | 6 |  |  |  |  |  |  |  |  |
|  | 7 - n-5 |  |  | . . . . . . . . |  |  |
|  | n-4 |  |  |  |  |  |  |  |  |
| Reservation data (rd) | n-3 |  | in1 | rdk | . . . . . . |  |  |
| Extended reservation ID (erid) | n-2 | eridk | . . . . . | erid1 |  |  | rd1 |
| CRC (c) | n-1 | c9 | c10 | c11 | c12 | c13 | c14 | c15 | c16 |
|  | n | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 |
| Flag | - | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 |

|  | . . . . . . . . |  | Denotes variable length field |
| --- | --- | --- | --- |

Note 3.—  ATN applications are supported by compressed frame bursts (see Section 1.4.2.2.2).

Note 4.— The lengths of the message ID and information fields depend on the message type being used.

Note 5.— The lengths of the extended reservation ID and reservation fields depend on the reservation protocol being used. The reservation field may also be subdivided into further fields, depending on the reservation protocol.

Version number

The version number (ver) subfield shall indicate the version of VDL Mode 4 supported by the station. It shall be set to 000binary on transmit. If the station receives a burst in which the version number is non-zero, it shall inform the VSS user that a non-zero version number has been received and ignore the rest of the burst.

Source address

The source address (s) of the transmitting station shall be encoded in the 27-bit field as described in Table 1-5. The address format shall be as described in Section 1.4.2.2.

Message ID

The message ID (mi) of the burst shall be encoded in the variable length field as defined in Table 1-5. The first four bits of the burst message ID field shall be as defined in Table 1-6a.

Table 1-6a. Message ID assignment

| Message ID field | Assigned burst type | VSS user |
| --- | --- | --- |
| Mi7 | mi6 | mi5 | mi4 | mi3 | mi2 | mi1 |  |  |
| x | x | x | x | x | 0 | 0 | Autonomous synchronization burst (see 1.5.6.1) | LME |
| x | x | x | x | x | 1 | 0 | Directed synchronization burst (see 1.5.6.1) | LME |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | General request burst | Defined by r-mi |
| 0 | 0 | 0 | 0 | 1 | 0 | 1 | No operation |  |
| 0 | 0 | 0 | 1 | 0 | 0 | 1 | Reserved for future use |  |
| 0 | 0 | 0 | 1 | 1 | 0 | 1 | Reserved for future use |  |
| 0 | 0 | 1 | 0 | 0 | 0 | 1 | General response burst | Defined by r-mi |
| 0 | 0 | 1 | 0 | 1 | 0 | 1 |  |  |
|  |  |  | to |  | 0 | 1 | Reserved for future use |  |
| 0 | 0 | 1 | 1 | 1 | 0 | 1 |  |  |
| 0 | 1 | 0 | 0 | 0 | 0 | 1 | Reserved for future use |  |
| 0 | 1 | 0 | 0 | 1 | 0 | 1 |  |  |
| 0 | 1 | 0 | 1 | 0 | 0 | 1 | Reserved for future use |  |
| 0 | 1 | 0 | 1 | 1 | 0 | 1 |  |  |
| 0 | 1 | 1 | 0 | 0 | 0 | 1 | DLS burst | DLS |
| 0 | 1 | 1 | 0 | 1 | 0 | 1 | Reserved for future use |  |
| 0 | 1 | 1 | 1 | 0 | 0 | 1 | Reserved for future use |  |
| 0 | 1 | 1 | 1 | 1 | 0 | 1 | Reserved for future use |  |
| 1 | 0 | 0 | 0 | 0 | 0 | 1 | Reserved for future use |  |
| 1 | 0 | 0 | 0 | 1 | 0 | 1 | Network entry burst | VSS |
| 1 | 0 | 0 | 1 | 0 | 0 | 1 | Bursts defined in ADS-B application standards | ADS-B application |
| 1 | 0 | 0 | 1 | 1 | 0 | 1 |  |  |
|  |  |  | to |  | 0 | 1 | Reserved for future use |  |
| 1 | 1 | 1 | 1 | 1 | 0 | 1 |  |  |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |  |
|  |  |  | to |  | 1 | 1 | Reserved for future use |  |
| 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |  |

Note.— Bits denoted as x are available for use within the information field.

The message ID shall define the VSS user which is responsible for handling the message, following completion of processing required within the VSS.

Information field

The optional information field (in) shall contain VSS user defined data.

Note.— The content of the information field is generally a matter for definition by applications using VDL Mode 4. General request and general response message formats are specified in Sections 1.3.19 and 1.3.20 respectively.

Reservation fields

The reservation ID (rid) of the burst shall be encoded in the 1-bit field as defined in Table 1-5. If the reservation ID equals 1, this shall indicate that the reservation type is either a null reservation (see Section 1.3.9), a periodic broadcast reservation (see Section 1.3.10) or a combined periodic broadcast and incremental broadcast reservation (see Section 1.3.12) and that there is no extended reservation ID (erid); otherwise, the extended reservation ID field shall indicate other reservation types as defined in Table 1-7.

Note 1.— The rid (and erid if present) subfield defines the interpretation of the reservation data (rd) field.

Autonomous/directed flag

The autonomous/directed (a/d) flag shall be encoded as defined in Table 1-6b if the message ID (see Table 1-6a) indicates that the burst is a synchronisation burst.  Otherwise it shall be reserved for future definition and set equal to 1.

Table 1-6b.  Autonomous/directed flag encoding

| Subfield | Range | Encoding | Notes |
| --- | --- | --- | --- |
| Autonomous/directed (a/d) | Boolean | 0 = autonomous slot selection (including directed rate), 1 = directed slot selection or ground station transmission | Identifies whether the synchronization burst is an autonomous or directed burst |

Table 1-7. Extended reservation ID field (erid)

| Extended reservation ID field (erid) | Reservation type |
| --- | --- |
| Octet n-2 |  |
| Bit 8 | Bit 7 | Bit 6 | Bit 5 | Bit 4 |  |
| 0 | 0 | 0 | 0 | 0 | Response burst (no reservation) |
| 0 | 0 | 0 | 0 | 1 | Big negative dither (BND) reservation |
| 0 | 0 | 0 | 1 | 0 | Superframe block reservation |
| 0 | 0 | 0 | 1 | 1 | Second frame block reservation |
| 0 | 0 | 1 | 0 | x | Unicast request reservation |
| 0 | 0 | 1 | 1 | 0 | Reserved for future allocation |
| To |  |
| 0 | 1 | 0 | 0 | 1 |  |
| 0 | 1 | 0 | 1 | 0 | Information transfer request reservation |
| 0 | 1 | 0 | 1 | 1 | Reserved for future allocation |
| 0 | 1 | 1 | 0 | 0 | Directed request reservation |
| 0 | 1 | 1 | 0 | 1 | Reserved for future allocation |
| To |  |
| 0 | 1 | 1 | 1 | 1 |  |
| 1 | 0 | x | X | x | Incremental broadcast reservation |
| 1 | 1 | 0 | 0 | 0 | Reserved for future allocation |
| To |  |
| 1 | 1 | 1 | 1 | 1 |  |

Note 2.— Bits denoted x are available for use within the reservation data (rd) field.

VSS sublayer parameters

VSS service system parameters shall be as described in Table 1-8.

Table 1-8. VSS sublayer parameters

| Symbol | Parameter name | Minimum | Maximum | GFSK default | Increment |
| --- | --- | --- | --- | --- | --- |
| VS1 | Number of ground quarantined slots | 0 slots | 15 slots | 4 slots | 1 slot |
| VS2 | Minimum CCI performance | P2 dB | 60 dB | 12 dB | 1 dB |
| VS4 | Quarantine slot re-use range | 0 | 1000 nmi | 300 nmi | 10 nmi |
| VS5 | Maximum burst length | 1 slot | 16 slots | 10 slots | 1 slot |

Note.— P2 is defined in VDL SARPS Section 6.9.5.5.2.2.

Parameter VS1 (number of ground quarantined slots)

The parameter VS1 shall define the number of ground quarantined slots (see Section 1.3.6.4).

Parameter VS2 (minimum CCI performance)

The parameter VS2 shall be used to control the CCI conditions by which a station may transmit given that another station has reserved the same slot. In the case where a station X and Y transmit in the same slot and station Y’s transmission is directed to another station Z, CCI conditions shall be fulfilled if the ratio defined below:

is greater than VS2.

Parameter VS4 (quarantine slot re-use range)

The parameter VS4 shall be used to control the range at which a quarantined slot may be re-used by a distant station (see Section 1.3.6.4).

Parameter VS5 (maximum burst length)

The parameter VS5 shall define the maximum burst length in slots including flags and zero bits inserted for transparency.

VSS quality of service parameters

Every burst processed by the VSS sublayer for transmission shall be associated with the parameters defined in Table 1-9.

Table 1-9. VSS quality of service system parameters

| Symbol | Parameter Name | Minimum | Maximum | Default | Increment |
| --- | --- | --- | --- | --- | --- |
| Q1 | Priority | 0 | 15 | 11 | 1 |
| Q2a | Slot selection range constraint for level 1 | 0 | 1000 nmi | 150 nmi | 1 nmi |
| Q2b | Slot selection range constraint for level 2 | 0 | 1000 nmi | 150 nmi | 1 nmi |
| Q2c | Slot selection range constraint for level 3 | 0 | 1000 nmi | 0 nmi | 1 nmi |
| Q2d | Slot selection range constraint for level 4 | 0 | 1000 nmi | 300 nmi | 1 nmi |
| Q3 | Replace queued data | FALSE | TRUE | FALSE | -- |
| Q4 | Number of available slots | 1 | 20 | 3 | 1 |
| Q5min | VSS retransmission parameters | minimum | 0 s | 20 s | 0 | 1 ms |
| Q5max |  | maximum | 1 s | 20 s | 5 s | 1 ms |
| Q5mult |  | multiplier | 1 | 2.5 | 1 | 0.01 |
| Q5exp |  | exponent | 1 | 2.5 | 1.5 | 0.01 |
| Q5num |  | number of attempts | 1 | 15 | 4 | 1 |
| Q5wait |  | maximum time to wait for a reply | 1 s | 120 s | 60 s | 1 s |

Parameter Q1 (priority)

The parameter Q1 shall be the priority of the transmission and shall be as defined in Table 1-10.

Table 1-10. Priority levels

| Message categories |  | Q1 |
| --- | --- | --- |
| Network/systems management |  | 14 |
| Distress communications |  | 13 |
| Urgent communications |  | 12 |
| High priority flight safety messages |  | 11 |
| Normal priority flight safety messages |  | 10 |
| Meteorological communications |  | 9 |
| Flight regularity communications |  | 8 |
| Aeronautical information service messages |  | 7 |
| Network/systems administration |  | 6 |
| Aeronautical administrative messages |  | 5 |
| Unassigned |  | 4 |
| Urgent priority administrative and UN charter communications |  | 3 |
| High priority administrative and state/government communications |  | 2 |
| Normal priority administrative |  | 1 |
| Low priority administrative |  | 0 |

Note.- this duplicates the ATN network priority numbering scheme. Q1 = 15 is reserved for future use.

Parameters Q2a to Q2d (slot selection range constraint for level n)

The parameters Q2a to Q2d shall be used to impose range constraints on the slot selection process for levels 1 to 4 defined by Table 1-11.

Parameter Q3 (replace queued data)

The parameter Q3 shall be a Boolean switch that shall be used to control queuing of repeated bursts on a congested channel. If Q3 = TRUE, then a new data field shall replace a queued data field of the same type. Otherwise, both the old and new data fields shall be transmitted.

Note.— Thus, if a channel is busy and, e.g., a synchronization burst containing ADS-B data cannot be transmitted, then a second synchronization burst (although with potentially different data) will overwrite the first burst.

Parameter Q4 (number of available slots)

The parameter Q4 shall be used to control the number of slots added to the available slot list during the slot selection process (see Section 1.3.6.2).

Parameters Q5 (VSS retransmission parameters)

The parameters Q5min, Q5max, Q5mult, Q5exp, Q5num and Q5wait shall control the retransmission of bursts for which an expected response has not been received (see Section 1.3.21).

Received transmission processing

A station shall be capable of recognizing and processing all possible reservation types as defined in Sections 1.3.9 through 1.3.18. When a station receives a burst with an unrecognized reservation type, it shall discard the burst without updating the reservation table.

When a station receives a known reservation type with an invalid subfield, or a known reservation type with valid subfields but an invalid combination, it shall reserve the slots indicated by the valid sub-fields; however, the station shall not transmit a response, nor shall the burst be passed to a VSS user.

When a station receives a burst with a known reservation type and a non-zero reserved subfield, it shall ignore the data in the reserved subfield.

The current slot for a burst shall be the slot in which the received transmission begins. The burst length (bl) shall be the number of slots across which the burst is transmitted.

Note.— Current slot and burst length are used throughout the text in protocol definitions. In the text, unless otherwise stated, references to particular slot numbers (e.g. for calculating the position of new reservations) are relative to the current slot which is taken to be slot 0. If a transmission extends across a slot boundary, it is considered to occupy the slots on both sides of the boundary for reservation purposes.

Valid bursts shall be forwarded to the appropriate VSS user, along with the time of receipt of the transmission. The received signal quality (see VDL SARPS Section 6.9.5.1.5.1) and the time of receipt of the bursts shall be passed to the VME. If the appropriate VSS user cannot be identified (i.e., the message ID is reserved or that functionality is not implemented) and the burst contains one or more reservations for the receiving station only, then the station shall transmit a general failure (see Section 1.3.20) with an error type of 00 hex or 80 hex (i.e., unsupported function) in the first slot of each of the reservations.

Reserved access protocol specification

Note.— Procedures for processing bursts containing specific reservation types are described in Sections 1.3.9 through 1.3.18.

Reservation table

A station shall maintain a table of all reservations in the next 4*M1 + 128 slots. For each reserved slot, the reservation Table entry shall consist of the 27-bit address of the intended transmitter, the 27-bit address of the destination (if any) and the type of reservation made. For periodic broadcast reservations (see Section 1.3.10) and directed request reservations (see Section 1.3.16), the reservation table shall also include pointers to all other reserved slots associated with the same reservation stream.

The reservation table shall be updated before the end of the first slot after the end of the burst.

With the exception of delayed bursts (see Sections 1.2.5, 1.5.6.3.3.1 and 1.5.6.3.4), and cases where a station has been directed to transmit by another station, a station shall wait for at least M1 slots after starting to listen to a channel before starting to transmit or reserve slots.

Note 1.— This allows sufficient time to build up the reservation table data.

Note 2.— A reservation table is for specification purposes only and the implementer is free to choose the method by which the reservation information is stored and processed. A station is required to record all reservations for a slot for possible use in slot selection algorithms because several stations may intentionally share a slot.

Note 3.— There may be more than one reservation associated with a particular slot.

Selecting slots for transmission or reservation

A station shall select slots for transmission or for reservation for later transmissions using the algorithm specified below.

Note.— When the channel is low to moderately loaded, the station will be able to select unreserved slots for transmission (level 0 in Table 1-11). When the channel is congested, the station is able to use slots that have been reserved by other stations by applying rules defined below (levels 1 to 4 in Table 1-11).

The VSS user shall specify one or more groups of quality of service parameters Q1, Q2a, Q2b, Q2c, Q2d and Q4 for slot selection. The station shall attempt to select slots using the first group of quality of service parameters. If slot selection is unsuccessful, the station shall use the next group and continue with successive groups until a slot has been selected. If, having used all groups of quality of service parameters, no slot has been selected, the VSS user shall be informed that slot selection has been unsuccessful.

Specification of candidate slots

The VSS user shall specify a range of candidate slots for slot selection.

Note.— The method for specifying candidate slots is protocol dependent (see Sections 1.3.9 to 1.3.18).

Derivation of a list of available slots

Slot selection criteria

A list of available slots shall be chosen from the candidate slots using the following rules:

a)	all unreserved slots shall be added to the list of available slots (shown as level 0 in Table 1-11).

b)	if, having completed stage a), the number of available slots is less than Q4, further available slots shall be selected from slots that have been previously reserved by other stations. The station shall initially select from slots which obey conditions specified as level 1 in Table 1-11 until Q4 available slots have been chosen. If, having applied level 1 conditions, the number of available slots is still less than Q4, slot selection shall continue using level 2 conditions. The process shall continue using subsequent levels until Q4 slots have been selected or until all levels have been applied. At each level, selection shall start with slots reserved by the most distant station and proceed in decreasing range order.

Table 1-11. Slot selection criteria

|  | Selection conditions |
| --- | --- |
| Selection priority | Planned transmission by station A | Previously reserved transmission by station B | Minimum distance between station A and station B |
| Level 0 | Any | Unreserved | Not applicable |
| Level 1 | Broadcast or CCI protected communication with station C | CCI protected communication with station D | Q2a |
| Level 2 | Broadcast or CCI protected communication with station C | Broadcast | Q2b |
| Level 3 | Broadcast or CCI protected communication with station C | Broadcast or CCI protected communication with station D | Q2c |
| Level 4 | Broadcast or CCI protected communication with station C | Any transmission | Q2d |

In Table 1-11, the following definitions and specifications shall apply:

| Station A | The station attempting to select a slot. |
| --- | --- |
| Station B | A station that has previously reserved a slot. |
| Station C | A station to which station A wishes to address a point-to-point communication. |
| Station D | A station for which station B has reserved a slot for point-to-point communication. |
| CCI protected | A point-to-point communication between two stations which fulfils the CCI conditions as defined in Section 1.3.3.2 and is therefore protected if a third station simultaneously transmits in the same slot. |

Note 1.— The decision criterion in Table 1-11 is the distance between station A and station B; however, the requirement to check for CCI protected communications requires station A to also examine the distance relationship between station B and station C, and station A and station D, if known. It is possible to disable the selection process at any of the levels in Table 1-11 by setting the appropriate range constraint (Q2a to d) large (1000 nmi).

Note 2.— For certain applications Q2d could be set to zero so that a slot can always be chosen even if this is at the expense of another application.

Recommendation

In selecting the list of available slots at level 0, priority should be given to candidate slots which are not reserved for transmission on any channel monitored by the station, and which also do not violate quarantine constraints (see Section 1.3.6.4) on the desired transmit channel.

Recommendation

A mobile station should exclude from consideration any slots which have been previously reserved for a point-to-point transmission, on any channel, where it is the intended destination.

1.3.6.2.2.4	Additional considerations for slot selection for transmission

Note 1.- It is assumed that ground stations will have the capability to transmit in all the active channels in the region they serve. However, mobile stations, especially with a single transmitter, will not be able to transmit in the same slot in different channels.

A mobile station A, when selecting the list of available slots for transmission in a channel for itself or another mobile station B, shall exclude from consideration the specific slots, which the station A knows are reserved for transmission for the intended station (either A or B) in other channels monitored by A.

Note 2.-If the selecting station is a ground station, then the station can select a conflicting slot if the ground station expects to overide the existing reservation. Procedures to resolve transmission conflict for mobile stations are described in section 1.3.6.6

Additional constraints applying to global signalling channels

On channels designated as global signalling channels (GSCs) (see VDL SARPs Section 6.9.2.2.1), mobile stations maintaining primary or secondary time shall exclude the first V66 (see Section 1.3.17.5.2) slots of every UTC second. The first V66 slots after every UTC second shall comprise the VLMC and shall be allocated for ground station use only.

Selection of slots from available slots

If, having completed the derivation of a list of available slots, the number of available slots is zero, no slot shall be selected and the VSS user shall be informed that slot selection was unsuccessful. If the number of available slots is greater than or equal to 1, a slot shall be chosen from the list of available slots such that the probability of choosing a given slot is the same as the probability of choosing any other slot.

Selection of slots for burst lengths greater than 1

For burst lengths greater than 1, the process specified in Section 1.3.6.2.2 shall be applied to continuous blocks of slots of length equal to the burst length. A block of slots shall be regarded as available at a particular level number (see Table 1-11) if all slots within the block are available at the same or lower level number. The procedure described in Section 1.3.6.2.4 shall then be used to select one of the available blocks.

Limits on selection of reserved slots

A station which has selected a slot that was reserved by another station, shall not select another slot reserved by that station within M1 - 1 slots after the selected slot.

Reserved transmissions

When a station has a burst to transmit for which it has a reservation, it shall transmit the scheduled data in the reserved slots, except as noted below.

Unavailable data

If the data for a burst for which a slot was reserved is unavailable when it is time to transmit, then the station shall send a general failure (see Section 1.3.20).

Reservation no longer valid

A station shall check that a reservation is valid according to the procedures of Section 1.3.6.5 before transmitting.

Ground quarantine

Establishment of ground quarantine

With the exception of a delayed burst (see Sections 1.2.5, 1.5.6.3.3.1 and 1.5.6.3.4), a mobile station, A, shall not reserve a slot or transmit on the slot boundary of the VS1 slots after a slot which has been reserved by a ground station, B, using a periodic broadcast reservation (see Section 1.3.10) or which has been reserved by a mobile, C, using a synchronization burst with the autonomous/directed bit set to 1 (see Section 1.3.2.6) and a periodic broadcast reservation field, unless the station (B or C) that has reserved the slot is at a range greater than VS4 from station A, in which case station A shall consider the slot to be unreserved.

Note 1.— The periodic broadcast reservation would be used to place a reservation for subsequent transmissions by the ground station. The directed request reservation would be used to reserve slots for broadcast by mobile stations and these mobiles will subsequently use periodic broadcast reservations and directed synchronization bursts to maintain the directed reservation (see Section 1.3.16.5).

Note 2.— Quarantine as defined in Section 1.3.6.4.1 does not apply to a delayed burst. If no normal transmission is detected (i.e., no transmission starting on the slot boundary), the slot may be used for a delayed burst regardless of its perceived quarantine status. This is to allow the ground system to provide opportunities for network entry unimpeded by other traffic. Note, however, that delayed bursts must not be made when ground quarantine is established using a block message (see Section 1.3.6.4.3).

Maintenance of ground quarantine after cancellation of a directed request broadcast

If a station receives a periodic broadcast burst with the periodic offset (po) subfield set to 0 and the periodic timeout (pt) subfield set to 0 (see Section 1.3.10.5.9), then it shall maintain ground quarantine as described in Section 1.3.6.4.1 for the current slot and for M1 slots after the current slot if it had previously contained a reservation associated with the same stream (see Section 1.3.10.4). Ground quarantine behaviour for any other slots associated with the same stream shall be cancelled.

Note.— This applies to the cancellation of a stream that was set up using a directed request and also to the cancellation of a ground station's periodic broadcast stream.

Ground quarantine established by block message

A mobile station, A, shall not reserve a slot or transmit in slots which have been reserved by a ground station, B, or a mobile station, C, using a block reservation (see Section 1.3.17), unless the station (B or C) that has reserved the slot is at a range greater than VS4 from station A, in which case station A shall consider the slot to be unreserved.

Note.— It is not possible to transmit a delayed burst in a reserved block.

Reservation conflicts

Note.— The following rules determine the action that a station takes in the event of detecting a reservation conflict. This is a normal event which is expected to occur as a result of slot re-use under CCI protection. In the event of a conflict, generally the slot selection criteria are re-applied to determine whether the slot could still have been selected in the knowledge of the new conflicting reservation. Generally, a station required to transmit in a slot that was reserved for it by another station will always transmit, since it cannot be assumed to have possession of the necessary information to determine the optimum action.

If a station, A, receives a burst containing a reservation from another station, B, for a slot which has already been reserved for station A to transmit, then station A shall take the following action:

a)	if the conflicting reservation from station B also requires station A to transmit, then station A shall transmit (i) the response with the higher priority (as determined by Q1), or (ii) the first requested transmission in the case of equal priority, or else;

b)	if station A no longer requires to transmit in the existing reservation, or does not have the necessary information to transfer, then it shall not transmit in the slot, or else;

c)	if the existing reservation for station A to transmit was made by a station other than A (i.e. by a unicast request (sdf = 0), information transfer, or directed request reservation), then A shall transmit in the slot in accordance with the existing reservation, or else;

d)	if the existing reservation for station A to transmit was made by A itself, then A shall apply the procedure described in 1.3.6.2.2 to determine whether, in the knowledge of the reservation made by station B, the slot is available at any level 1, 2, 3 or 4, using the same values of Q2 and other parameters as originally used to select the slot. If the slot is determined to be available by this process, then A shall transmit according to its existing reservation. If the slot is no longer available, the actions specified in Table 1-12 shall be performed.

Table 1-12. Action in the event of reservation conflict

| Protocol for A’s existing reservation (made by A) | Protocol for B’s conflicting reservation | Action by A |
| --- | --- | --- |
| Slots reserved by station A using ground quarantine (see Section 1.3.6.4) | Any | Transmit according to existing reservation. |
| Periodic broadcast | Incremental broadcast, big negative dither unicast request, or information transfer | Transmit according to existing reservation. |
| Periodic broadcast | Periodic broadcast (autonomous/directed), directed request, slots reserved by ground quarantine (see Section 1.3.6.4) | If the conflict occurs later than A’s next transmission in the stream, then select a new transmission slot and reduce the value of TV11 so as to cause the stream to dither to the new slot prior to the conflict; otherwise, do not transmit in the former slot, and re-establish the stream in a new slot. |
| Incremental broadcast or big negative dither | Any | Do not transmit in the existing reservation, and make the transmission in an alternative slot by random access (Section 1.3.7). |
| Unicast request (sdf = 1), or information transfer | Any | Do not transmit in the existing reservation, and apply the retransmission procedures (Section 1.3.21). |

Transmission conflicts for mobile stations

Note.- The following rules describe the action that a mobile station will take when it is detecting that it is requested to transmit simultaneously in the same slot in different channels.

If a mobile station is requested to transmit in the same slot in different channels, then the station shall take the following action:

- If there is only one transmission with the highest priority among the required transmissions, then the station shall transmit this highest priority transmission, or else;

- If there is only one ground initiated transmission among the transmissions with the same highest priority, then the station shall transmit this ground initiated transmission, or else;

- If there is more than one ground initiated transmission among the transmissions with the same highest priority, then the station shall transmit the last requested of these ground initiated transmission, or else;

- If there are no ground initiated transmissions among the transmissions with the same highest priority, then the station shall transmit the first requested transmission.

Random access protocol specification

The station shall implement a non-adaptive p-persistent algorithm to allow equitably all stations the opportunity to transmit while maximizing system throughput, minimizing transit delays, and minimizing collisions.

Note.— Transmissions which use the random access procedures may be used to place reservations for future transmissions using the reserved access procedures (Section 1.3.6) or they may be “one-off” transmissions which place no reservations and which will conform to either the null reservation burst format (Section 1.3.9.1) or the response protocol burst format (Section 1.3.18.1)

Random access parameters

Table 1-13. Random access VSS system parameters

| Symbol | Parameter name | Minimum | Maximum | Recommended default | Increment |
| --- | --- | --- | --- | --- | --- |
| TM2 | Channel busy timer | 25 slots | 9000 slots | 1500 slots | 20 slots |
| p | Persistence | 1/256 | 1 | 64/256 | 1/256 |
| VS3 | Maximum number of access attempts | 1 | 65535 | 24 | 1 |

Timer TM2 (channel busy timer)

Timer TM2 indicates the number of slots (TM2) that a sublayer shall wait after receiving a request to transmit. This timer shall be started if it is not already running, when the VSS sublayer receives a request for random transmission. Upon a successful random transmission access attempt, the timer shall be cleared if the random transmit queue is empty and reset if it is not empty. When the timer expires, the VSS user shall be informed that the channel is congested.

Parameter p (persistence)

Parameter p shall be the probability that the station will transmit on any random access attempt.

Counter VS3 (maximum number of access attempts)

Counter VS3 shall be used to limit the maximum number of random access attempts (VS3) that a station will make for any transmission request. This counter shall be cleared upon system initialization, Timer TM2 expiring, or a successful access attempt. The counter shall be incremented after every unsuccessful random access attempt. When the counter reaches the maximum number of random access attempts, authorization to transmit shall be granted as soon as the channel is available.

Random access procedures

Random access procedures for transmissions starting on a slot boundary

When the station has one or more bursts to transmit for which it does not have a reservation, it shall use the p-persistent algorithm as defined  below:

a)	access attempts shall only be made and transmission shall only begin on a slot boundary of available slots. A station shall regard a slot or block of slots as available for a random transmission if it conforms to the criteria of any of Levels 0 through 2 in Table 1-11 using default or VSS user-supplied quality of service parameters; and

b)	transmission shall not begin if the station has not previously made or received a reservation for the prior slot, and the slot is busy as defined in Section 1.2.4 at the slot boundary.

If the station is unable to select a slot, this shall be regarded as an unsuccessful random access attempt.

If the station is able to select a slot, then the station shall transmit on the slot boundary with probability p (defined in section 1.3.7.1.2).

Note.— Consider the case where a station intends to apply a p-persistent algorithm for random transmission at the start of slot k. If the prior slot (k-1) is reserved and slot k is unreserved or effectively unreserved, the station may be confident that the transmission in slot (k-1) will terminate and garble will not occur. However, if slot (k-1) is unreserved (according to the reservation table  of the station) but nonetheless busy, the station has no way of knowing whether the transmission will terminate or continue. So in this case, a physical layer measurement is necessary to ensure that the transmission has terminated. Since the measurement process takes finite time, an apparently unreserved transmission which ends close to the end of slot (k-1) may forestall a random transmission in slot k. This is unavoidable.

Random access procedures for delayed transmissions

Delayed transmissions shall use a p-persistent algorithm as defined  below:

- transmissions shall be delayed relative to the slot boundary in accordance with Section 1.2.5; and

- a station shall not start a transmission if the channel is busy, as defined in Section 1.2.4, at the intended (delayed) start time.

If the station is unable to select a slot, this shall be regarded as an unsuccessful random access attempt.

If the station is able to select a slot, then the station shall transmit on the slot boundary with probability p (defined in section 1.3.7.1.2).

Recommendation

When possible, a station should use the reserved access protocols described in Section 1.3.6 to reserve slots for new transmissions by adding reservation fields to transmissions for which slots have already been reserved. The random access protocol should be used only if there is no suitable  opportunity to reserve a slot.

Recommendation

When possible, if there has been no previous reservation, a ground station should use ground quarantined slots (see Section 1.3.6.4) for transmission. The random access protocol should be used only if there is no suitable  opportunity to use ground quarantined slots.

Transmit queue management

There shall be a single queue for all random transmissions which do not have reserved slots for transmission. This queue shall be sorted in priority order, with a higher value of Q1 being transmitted before a lower value of Q1. If Q3 is TRUE, then the queue shall be searched to determine if a burst of the same type has been queued.

Fixed access protocol specification

A ground station shall be capable of being pre-programmed either to not transmit in certain slots with times expressed in UTC or to transmit specific transmissions in specific slots with starting times expressed in UTC (without necessarily announcing a reservation).

Recommendation

The user should specify the use of an appropriate reservation protocol to protect future fixed transmissions.

Note 1.— The user will be able to specify a time or slot for a particular transmission and can also specify a reservation protocol to protect the next fixed transmission. For example, the user could specify a certain ground transmission at a certain time and then specify the use of the periodic reservation block to reserve the same slot in the next minute.

Note 2.— The ground infrastructure service provider is able to use this protocol together with the blocking reservation protocol (see Section 1.3.17.7.1) to organise a series of coordinated reserved slots for ground transmissions.

Null reservation protocol specification

Null reservation burst format

A reservation ID (rid) = 1 and a reservation data (rd) field in accordance with Table 1-14 shall indicate a null reservation. In this case, the information field shall extend up to the last 10 bits prior to the CRC.

Table 1-14. Null reservation bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| reservation data (rd) field | n-3 | x | x | x | x | x | x | 0 | 0 |
|  | n-2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

Note.— Bits denoted x are available for use within the information field.

Periodic broadcast protocol specification

Note.— The periodic broadcast protocol is intended for those VSS users transmitting one or more times per superframe for a number of superframes. A sequence of reserved slots linked by a periodic reservation is known as a “stream”. A periodic broadcast reservation burst reserves a slot in the next superframe for its own stream (i.e., a VSS user transmitting 3 times a minute has 3 streams).

Periodic broadcast reservation burst format

A reservation ID (rid) = 1 and a reservation field in accordance with Table 1-15 shall indicate a periodic broadcast reservation. In this case, the information field shall extend up to the last 10 bits prior to the CRC.

Table 1-15. Periodic broadcast reservation bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| periodic timeout (pt) | n-3 | x | x | x | x | x | x | pt2 | pt1 |
| periodic offset (po) | n-2 | po8 | po7 | po6 | po5 | po4 | po3 | po2 | po1 |

Note 1.— Bits denoted x are available for use within the information field.

Note 2.— If the reservation field is all zeros, then a null reservation is being made (see Section 1.3.9). In the case of pt = 3, a combined periodic broadcast and incremental broadcast is indicated, in which case the periodic offset (po) subfield is replaced by the incremental offset (io) subfield, as described in Section 1.3.12. When io = 0 binary, only a periodic reservation is made.

The subfields shall be as defined in Table 1-16.

Table 1-16. Periodic broadcast reservation field encoding

| Subfield | Range | Encoding | Definitions |
| --- | --- | --- | --- |
| periodic offset (po) | -127 to +127 | two’s complement math po = -128 is invalid | po identifies a slot relative to the first slot of the transmission in a future superframe |
| periodic timeout (pt) | 0 to 3 |  | pt is the number of superframes in the future for which a reservation is being made. |

Periodic broadcast timers

Timer TV11 (reservation hold timer)

The timer TV11 shall control the number of successive superframes which will use the same slot for transmission (see Section 1.3.10.5) before moving to a new slot. There shall be one TV11 timer for each slot used for periodic broadcasts.

Periodic broadcast parameters

The periodic broadcast protocol shall implement the system parameters defined in Table 1-17.

Table 1-17. Periodic broadcast VSS system parameters

| Symbol | Parameter name | Minimum | Maximum | Recommended default | Increment |
| --- | --- | --- | --- | --- | --- |
| TV11min | Reservation hold timer minimum value | 0 superframes | 15 superframes | 4 superframes | 1 superframe |
| TV11max | Reservation hold timer maximum value | 1 superframe | 16 superframes | 8 superframes | 1 superframe |
| V11 | Nominal periodic rate | 1 per superframe | 60 per superframe | 1 per superframe | 1 per superframe |
| V12 | Periodic dither range | (2/M1)*V11 | 1.00 | 0.10 | 0.01 |

TV11min shall be less than or equal to TV11max.

The VSS user shall provide any of the parameters TV11min, TV11max, V11, V12 and quality of service parameters (Q2a to Q2d and Q4) for which the default values are not desired.

Parameters TV11min and TV11max (reservation hold timer minimum and maximum values)

Parameters TV11min and TV11max shall be used to determine the start value for the TV11 timer, consistent with the procedure defined in Section 1.3.10.5.4.

Parameter V11 (nominal periodic rate)

The parameter V11 shall be the number of times per superframe that a VSS user will transmit a burst.

Parameter V12 (periodic dither range)

The parameter V12 shall define the range for candidate slots on either side of the nominal slot (see Section 1.3.10.5.1) from which the station shall choose a slot or group of slots to be reserved for transmission once the TV11 timer expires. V12 shall be specified as a fraction of the nominal periodic rate.

Note.— The selected slot may be chosen from a range between the nominal slot -truncate((V12/2)*(M1/V11)) and the nominal slot +truncate((V12/2)*(M1/V11)) or, if this range is greater than +/- 127, a range between nominal slot - 127 and the nominal slot + 127.

Periodic broadcast reception procedures

Upon receipt of a burst containing a periodic broadcast reservation, the station shall update its reservation table  and carry out the actions as specified in Table 1-18. All reservations associated with a single periodic broadcast reservation burst shall be known as a stream.

Table 1-18. Action on receipt of periodic broadcast reservation burst

| Periodic offset (po) | Periodic timeout (pt) | Action |
| --- | --- | --- |
| 0 | 0 | No reservation. Note 1.— reservation format is the same as null reservation (see Section 1.3.9) |
| Any except 0 | 0, 1 or 2 | Reserve the following slots for the source to broadcast: if pt = 1 or 2 then for j = 1 to pt, the slots equal to (j * M1) through (bl - 1 + (j * M1)) after the first slot of the received burst AND for j = pt + 1 to 4, the slots equal to (po + (j * M1)) through (bl - 1 + (po + (j * M1))) slots after the first slot of the received burst |
| 0 | 1 or 2 | Reserve the following slots for the source to broadcast: for j = 1 to pt, the slots equal to (j * M1) through (bl - 1 + (j * M1)) after the first slot of the received burst |
| Any | 3 | Reserve the following slots for the source to broadcast: for j = 1 to 4, the slots equal to (j * M1) through (bl - 1 + (j * M1)) after the first slot of the received burst Note 2.— The interpretation of the periodic offset subfield in the case of periodic timeout = 3 and io ≠ 0 binary is described in Section 1.3.12. |

The actions defined in Table 1-18 shall cancel any previous reservations for the same stream.

If a station was expecting to receive a transmission from a peer station containing a periodic broadcast reservation, but receives a transmission from the peer station containing an incremental reservation (see Section 1.3.11) or a unicast request with the source/destination flag set equal to 1 (see Section 1.3.14), the station shall cancel the periodic broadcast reservation stream for the peer station.

Periodic broadcast transmission procedures

Selection of nominal slots

When operating without any directed slot reservations (see Section 1.3.16.1.1) for a given VSS User application which requires periodic broadcast transmissions, a station shall select nominal slots (n_slot) which form a periodic sequence in time, considering all frequencies used, with a variation of no more than +/- 1 slot as required to accommodate the constraints imposed by the nominal reporting rate for the application and the slot rate on the channel.

When operating with a mixture of directed slot reservations (see Section 1.3.16.1.1), autonomous and directed rate reservations (see Section 1.3.16.1.1) for a given VSS User application which requires periodic broadcast transmissions, a station shall select nominal slots (n_slot) for the autonomous or directed rate which form a periodic sequence in time, considering all frequencies used, with a variation of no more than +/- 1 slot as required to accommodate the constraints imposed by the nominal reporting rate for the application and the slot rate on the channel.

Note 1.— For an application that requires periodic broadcast transmissions on multiple frequency channels, for which no directed-slot reservations have been received, the aggregate of all required transmissions should be used when calculating the nominal rate. Example 1: Two frequencies with a required update rate of once per 10 seconds on each frequency. In this case, nominal slots should be interleaved and equally-spaced to achieve an aggregate nominal rate of once per 5 seconds (i.e. considering the two channels together). Example 2: two frequencies with a required update rate of once per 15 seconds on frequency F1 and once per 5 seconds on frequency F2. In this case, the aggregate nominal rate should be once per 3.75 seconds with three successive nominal slots on F2 spaced 3.75 seconds apart, followed by a 7.5 second gap centred on a nominal slot for F1, followed by another three successive nominal slots on F2 etc.

Note 2.— A station may shift equally all the nominal slots associated with an application's autonomous or directed rate reservations forward or backward in time, so as to enhance the likelihood of finding appropriate transmission slots for the application as a whole (i.e. within the dither bands surrounding each nominal slot).

Note 3.— A station may shift individual slots or sets of slots as required to satisfy the needs of this section. This may be required, for example, if the application adds a new frequency or if the nominal rate on one of the existing frequencies is changed in real time (i.e. with a directed rate request).

Note 4.— This paragraph is relevant for transmissions using periodic reservations. It does not apply to transmissions using other reservation types, or random transmissions. For example, transmissions made using random and incremental protocols are excluded.

Selection of slots for a periodic broadcast transmission

If there is no existing periodic reservation for the VSS user, the station shall select a current transmission slot (ct_slot) corresponding to each nominal slot by inspection of the reservation table  data, using the following procedure:

The station shall use the slot selection procedure specified in Section 1.3.6.2 using all slots that are within truncate((V12/2)*(M1/V11))) of n_slot and within 127 slots of n_slot, as candidate slots and the parameter settings defined in Table 1-19.

Table 1-19. Periodic broadcast QoS parameters

| Symbol | Parameter name | Default |
| --- | --- | --- |
| Q2a | Slot selection range constraint for level 1 | 300 nmi |
| Q2b | Slot selection range constraint for level 2 | 300 nmi |
| Q2c | Slot selection range constraint for level 3 | 1000 nmi |
| Q2d | Slot selection range constraint for level 4 | 1000 nmi |
| Q4 | Number of available slots | 3 |

Note 1.— The station first tries to find unreserved slots in the range V12 * M1/V11 on either side of the nominal slot.

If slot selection is unsuccessful, the station shall re-apply this slot selection, using the same candidate slots and VSS user supplied quality of service parameters.

Note 2.— If the first stage is unsuccessful, the station can use previously reserved slots of the most distant users (assuming that the quality of service parameters supplied by the VSS user allow this).

Calculation of slot availability

After selection of a new current transmission slot, the station shall compute the slot availability (s_avail), indicating how many consecutive superframes are available until the equivalent slot is reserved by another user. The value of s_avail shall indicate the slot (ct_slot + s_avail * M1) which is reserved by another user and shall range from 1 (for a slot that is reserved in the next superframe) to 4 (for slots that currently have no reservation for at least 3 superframes). The calculation of s_avail shall use the following rules:

a)	if the current transmission slot has not been previously reserved, s_avail shall be the number of superframes that are left before the equivalent slot is reserved;

b)	if the current transmission slot has been previously reserved by a station, s_avail shall be the number of superframes that are left before the equivalent slot is reserved by a different user.

Transmission in a new slot

If there is no prior reservation or if the station is using for the first time a slot for which there has been a prior reservation, the station shall start the timer TV11 at a value equal to s_avail, if s_avail = 1,2 or 3, and otherwise equal to a random value uniformly chosen between TV11min and TV11max.

Note.— The reservation for the new slot is maintained for TV11 superframes unless s_avail indicates that only 1, 2 or 3 superframes are available before another station has placed a reservation.

Transmission for TV11 greater than 3

If the TV11 timer is greater than 3 and there is no requirement to associate the current transmission with an incremental reservation, the station shall transmit a burst containing a periodic broadcast reservation in the current transmission slot with io = 0 and pt = 3. After transmission, the timer TV11 shall be decremented by one and the current transmission slot shall be incremented by M1.

Reservation of a new slot for TV11 equal to 1,2, or 3

If the TV11 timer is equal to 1,2 or 3 and if the VSS user requires that periodic broadcast reservations are maintained after the current transmission slot reservation expires, the station shall reserve a future transmission slot (ft_slot) for subsequent transmissions. If a future transmission slot has already been selected, there shall be no further slot selection. Otherwise, selection of ft_slot shall be carried out using the procedure set out in Section 1.3.10.5.2 using all slots  that are within truncate((V12/2)*(M1/V11))) of n_slot and within 127 slots of n_slot and within 127 slots of ct_slot,  except slot (ct_slot + TV11 * M1), as candidate slots.

Note.— This process selects a new slot to which the periodic broadcast transmission will move in TV11 superframes after the current transmission slot. This new slot will occupy a different position in the superframe to the current transmission slot.

Transmission for TV11 equal to 1, 2 or 3

If the TV11 timer is equal to 1,2 or 3 the station shall transmit a burst containing a periodic broadcast reservation in the current transmission slot with po = (ft_slot - ct_slot) and pt = TV11-1.

If a future transmission slot has not been selected and the VSS user does not require the reservation to be maintained, the value of the po shall be set to 0.

After transmission, the timer TV11 shall be decremented and the current transmission slot set equal to ct_slot + M1.

TV11 equal to 0

If the TV11 timer is equal to 0, and the VSS user requires a reservation to be maintained, then if a new slot has not been selected for further periodic broadcasts, the station shall select a new current transmission slot using the procedures set out in Section 1.3.10.5.2. If a new slot has been selected for further periodic broadcasts, the station shall set the current transmission slot equal to the future transmission slot.

The station shall start to transmit in the new current transmission slot carrying out the procedures set out in Sections 1.3.10.5.3 to 1.3.10.5.8.

If the VSS user does not require a reservation to be maintained, no further action shall be taken.

Reservation cancellation

A station wishing to cancel a stream of reservations for its own transmissions, in the absence of a reservation conflict, shall transmit a periodic broadcast reservation burst with po = 0 and pt = 0 in the next reserved slot and the timer TV11 shall be cleared. A station receiving such a burst shall clear all reservations known to be associated with the stream.

Note 1.— Because all existing reservations for a stream are cancelled on receipt of a periodic reservation burst and are replaced according to the reservation information contained in the burst (see Section 1.3.10.4), this action has the effect of cancelling the whole stream.

Note 2.— Reservation conflicts are mediated in accordance with Section 1.3.6.5, and the requirement to transmit a reservation cancellation (i.e. po = 0 and pt = 0) does not apply if the transmission would be disallowed by the considerations of that section.

Incremental broadcast protocol specification

Note.— The incremental broadcast protocol is intended for those VSS users which are transmitting multiple times per minute, but only for a minute or two. A burst reserves a number of slots for a time later in the same superframe. The number of slots reserved is equal to the burst length (see Section 1.3.5) of the burst containing the reservation.

Incremental broadcast reservation burst format

A reservation ID (rid) = 0 with extended reservation ID and reservation fields set in accordance with Table 1-20 shall indicate an incremental broadcast reservation. In this case, the information field shall extend up to the last 10 bits prior to the CRC.

Table 1-20. Incremental broadcast reservation bit encoding

| Description | Octet | Bit Number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
|  | n-3 | x | x | x | x | x | x | io8 | io7 |
| incremental offset (io) | n-2 | 1 | 0 | io6 | io5 | io4 | io3 | io2 | io1 |

Note.— Bits denoted x are available for use within the information field.

The subfields shall be as defined in Table 1-21.

Table 1-21. Incremental broadcast reservation field encoding

| Subfield | Range | Encoding | Definitions |
| --- | --- | --- | --- |
| Incremental offset (io) | 0 to 255 | (See Section 1.3.11.4) | io identifies a slot relative to the first slot of the transmission |

Incremental broadcast parameters

The incremental broadcast protocol shall implement the system parameters defined in Table 1-22.

Table 1-22. Incremental broadcast VSS system parameters

| Symbol | Parameter name | Minimum | Maximum | Recommended default | Increment |
| --- | --- | --- | --- | --- | --- |
| V21 | Nominal incremental period | 960/M1 sec | 60480/M1 sec | 1.0 sec | 0.1 sec |
| V22 | Maximum incremental dither range | 720/(V21* M1) | MIN(1.001-240/(V21*M1), 61200/(V21*M1) – 0.999) | MIN(0.75, maximum allowed value of V22) | 0.001 |

The VSS user shall provide any of the parameters V21, V22 and quality of service parameters (Q2a to Q2d and Q4) for which the default values are not desired.

Note.— The maximum value of V21 is set by the maximum allowed value of the incremental offset subfield. The minimum value of V21 and V22 is set to ensure that there are at least 5 candidate slots from which to choose a slot to be reserved.

Parameter V21 (nominal incremental period)

The parameter V21 shall be the nominal time after the first slot of the incremental broadcast transmission that a VSS user will transmit a burst.

Parameter V22 (maximum incremental dither range)

The parameter V22 shall define the range for candidate slots on either side of the nominal slot from which the station shall choose a slot or group of slots to be reserved for transmission. V22 shall be specified as a fraction of the nominal incremental period.

Note.— The selected slot may be chosen from a time range between V21 +/- V22*V21.

Incremental broadcast reception procedures

Upon receipt of a burst containing an incremental broadcast reservation, a station shall reserve the slot equal to (4 * io) through (bl - 1 + 4 * io) after the first slot of the received burst for the source to broadcast.

When a burst contains an incremental broadcast reservation with io = 0, then no incremental reservation shall be placed.

Incremental broadcast transmission procedures

Selection of the transmission slot for the incremental broadcast reservation

If no slot or group of consecutive slots, has been reserved for transmission of an incremental reservation, and if the incremental reservation is not to be combined with a periodic broadcast reservation (see Section 1.3.12), the station shall select a slot or group of consecutive slots using the random access procedures (see Section 1.3.7).

The transmission slot (t_slot) shall be the first slot of the incremental broadcast transmission.

Selection of the reserved slot for the incremental broadcast reservation

The station shall choose a slot or group of consecutive slots to reserve using the slot selection procedure specified in Section 1.3.6.2:

a)	using VSS user supplied quality of service parameters; and

b)	candidate slots in the range (V21*M1/60 - V22 * V21*M1/60) through (V21*M1/60 + V22*V21*M1/60 + bl -1) such that the chosen slot, or the first slot in the chosen group of slots, is an exact modulo 4 difference from t_slot.

The reserved slot (r_slot) shall be the chosen slot or the first slot in the chosen group of slots.

Incremental broadcast burst transmission

The station shall transmit an incremental broadcast burst in the transmission slot with the value of io set to (r_slot - t_slot)/ 4.

Combined periodic broadcast and incremental broadcast protocol specification

Note.— The periodic broadcast reservation (see Section 1.3.10) can be combined with an incremental broadcast reservation (see Section 1.3.11) when the periodic broadcast timer (TV11) is greater than 3, enabling the station to reserve a fourth slot up to 1020 slots in the future (as well as three slots in the subsequent superframes). A station may therefore use the opportunity presented by a combined periodic broadcast and incremental broadcast to reserve a slot for a different VSS user which happens to be in the random access queue or to improve net entry performance (see Section 1.5.6.3.5) by reserving both in the next superframe (periodic broadcast) and this superframe (incremental broadcast).

Combined periodic broadcast and incremental broadcast reservation burst

A reservation ID (rid) = 1 and a reservation field in accordance with Table 1-23 shall indicate a combined periodic broadcast and incremental broadcast reservation. In this case, the information field shall extend up to the last 10 bits prior to the CRC. The periodic timeout (pt) subfield shall be set to 3. The incremental offset (io) subfield shall be as defined in Section 1.3.11.1.

Table 1-23. Combined periodic/incremental broadcast reservation bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| periodic timeout (pt) = 3 | n-3 | x | x | x | x | x | x | 1 | 1 |
| incremental offset (io) | n-2 | io8 | io7 | io6 | io5 | io4 | io3 | io2 | io1 |

Note.— Bits denoted x are available for use within the information field.

All other parameters and procedures shall be as specified in Sections 1.3.10 and 1.3.11.

Big negative dither (BND) broadcast protocol specifications

Note.— The BND can be used by a VDL Mode 4 station intending to enter a VDL Mode 4 channel/network (i.e. begin transmitting synchronization bursts on an autonomous basis), in cases where the station has listened to the channel for a few seconds but has not yet built a complete reservation table, and either: 1) it has fewer current reservations for synchronization bursts than required; or 2) it has a sufficient number of reservations, but one or more of them is about to expire (pt = 0), and the station wishes to initiate or continue periodic streams using the reservation opportunities presented by these existing reservations. The BND can be transmitted in a normal or delayed burst. The BND can also be used in the context of a normal stream of synchronization bursts, to meander a stream outside the existing maximum dither range (e.g. when the flow channel must be adjusted).

BND reservation burst format

A reservation ID (rid) = 0, an extended reservation ID (erid) = 00001binary, and reservation data set in accordance with Table 1-24 shall indicate a Big Negative Dither (BND).

Table 1-24. BND broadcast reservation bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| negative dither (nd) | n-3 | x | x | x | x | x | x | nd5 | nd4 |
| extended reservation ID (erid) | n-2 | 0 | 0 | 0 | 0 | 1 | nd3 | nd2 | nd1 |

Note.— Bits denoted x are not used by this reservation type and shall be available for use within the information field.

The subfields shall be as defined in Table 1-25.

Table 1-25. BND broadcast reservation parameters

| Subfield | Range | Encoding | Definitions |
| --- | --- | --- | --- |
| negative dither (nd) | 0 to 31 |  | nd identifies a slot relative to and earlier than the current slot + M1 - 128 slots. |

BND broadcast parameters

There are no BND parameters.

BND broadcast reception procedures

Upon receipt of a burst containing a BND broadcast reservation, a station shall reserve the slots from (M1- 128 - (4 * nd)) through (M1 - 128 - (4 * nd) + (bl - 1)) after the first slot of the received burst for the source to broadcast.

Note.— This reservation type allows a station to place a reservation for a future transmission, in a slot which is likely to be unreserved (see associated transmission procedures).

BND broadcast transmission procedures

A station shall not transmit a BND reservation until it has listened to a channel for at least 254 slots and can select a slot for transmission from among those slots addressable by the BND reservation using the slot selection procedures defined in Section 1.3.6.2 and VSS user supplied quality of service parameters, Q2 and Q4.

Unicast request protocol specification

Note.— This protocol is intended for a VSS user which requires a response from a peer VSS user.

Unicast request reservation burst format

A reservation ID (rid) = 0 with an extended reservation ID and reservation fields set in accordance with Table 1-26 shall indicate a unicast request reservation.

Table 1-26. Unicast request reservation bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| destination address (d) | n-8 | d24 | d23 | d22 | d21 | d20 | d19 | d18 | d17 |
|  | n-7 | d16 | d15 | d14 | d13 | d12 | d11 | d10 | d9 |
|  | n-6 | d8 | d7 | d6 | d5 | d4 | d3 | d2 | d1 |
| source/destination flag (sdf) | n-5 | ro12 | ro11 | ro10 | ro9 | sdf | d27 | d26 | d25 |
| response offset (ro) | n-4 | ro8 | ro7 | ro6 | ro5 | ro4 | ro3 | ro2 | ro1 |
| length (lg) | n-3 | lg8 | lg7 | lg6 | lg5 | lg4 | lg3 | lg2 | lg1 |
| priority (pr) | n-2 | 0 | 0 | 1 | 0 | pr4 | pr3 | pr2 | pr1 |

The subfields and associated actions shall be as defined in Table 1-27. Bits 25, 26 and 27 of the destination address (d) subfield shall be the address type field. In the case that the address type field is equal to 7, bits 1 through 24 of the destination subfield (d) shall be absent and the information field shall extend up to the last four octets prior to the CRC. Otherwise, the information field shall extend up to the last seven octets prior to the CRC and the burst shall include  all of the destination subfield (d).

Table 1-27. Unicast request reservation field encoding

| Subfield | Range | Encoding / Actions | Definitions |
| --- | --- | --- | --- |
| response offset (ro) | 0 to 4095 |  | ro identifies a slot relative to the first slot of the transmission |
| destination address (d) | 0 to 227-1 | (See Section 1.4.2.1) | d is the 27-bit address of the destination station. |
| source/destination flag (sdf) | Boolean | If sdf = 0, reserve the response slot for the destination station to transmit. If sdf = 1, reserve the response slot for the source station to transmit. | sdf indicates which station will respond in the reserved response slot. Note that the source station is the station placing the reservation. |
| length (lg) | 0 to 255 |  | lg is one less than the number of slots that are reserved for the response |
| priority (pr) | 0 to 15 | See Table 1-10 |  |

Unicast request parameters

The unicast request protocol shall implement the system parameters as defined in Table 1-28.

Table 1-28. Unicast request VSS system parameters

| Symbol | Parameter name | Minimum | Maximum | Recommended default | Increment |
| --- | --- | --- | --- | --- | --- |
| V32 | Minimum response delay | 2 slot | 500 slots | 20 slots | 1 slot |
| V33 | Maximum response delay | 2 slot | 4095 slots | 1000 slots | 1 slot |
| V34 | Source/destination control | 0 | 1 | 0 | 1 |
| V35 | Broadcast control | 0 | 1 | 0 | 1 |
| V36 | Length of reserved block | 1 slot | 256 slots | N/A | 1 slot |

The VSS user shall provide the destination address and any of the parameters V32, V33, V34, V35, V36 and Quality of Service parameters (Q2a to Q2d, Q4 and Q5) for which the default values are not desired.

Parameter V32 (minimum response delay)

Parameter V32 shall be the minimum delay, measured in slot intervals, that a station will provide to a responder in order to ensure that the responder can generate the response before its reserved slot.

Note.— V32*60/M1 is the maximum time that a station is provided with to generate a response to the request.

Parameter V33 (maximum response delay)

Parameter V33 shall be the maximum delay, measured in slot intervals, that a station will provide to a responder in order to ensure timely delivery in case a retransmission is required.

Parameter V34 (source/destination control)

Parameter V34 shall control whether the unicast reservation protocol is used to reserve a slot for the destination station to transmit a response to the source (V34 = 0) or for the source station to transmit a response to the destination (V34 = 1). If the broadcast control parameter (V35 = 1), the value of V34 shall be ignored.

Note.— If the destination subfield is omitted (V35 = 1), then the reservation is for the source to broadcast and the value of V34 has no meaning.

Parameter V35 (broadcast control)

Parameter V35 shall control whether the lowest 24 bits of the destination subfield (d) are included in the reservation. If V35 = 0, then the lowest 24 bits of the destination subfield shall be included and the reservation will be for the station to transmit to or receive from a peer station. Otherwise the lowest 24 bits of the destination subfield shall be omitted, the address type field shall be set to 7 and the reservation will be for the station to make a broadcast transmission.

Parameter V36 (length of reserved block)

Parameter V36 shall be the number of reserved slots required for the unicast reservation protocol response.

Unicast request reception procedures

Upon receipt of a burst containing a unicast request reservation, a station shall reserve all of the slots from (1 + ro) through (1 + ro + lg) after the first slot of the received burst for:

a)	the destination to transmit a response to the source (if sdf = 0 and address type field (  7);

b)	or for the source to transmit a response to the destination (if sdf = 1 and address type field ( 7); and

c)	or for the source to make a broadcast transmission (if address type field = 7).

Unicast request transmission procedures

Selection of the transmission slot for the unicast request reservation

If no slot has been reserved for transmission of a unicast reservation, the station shall select a slot using the random access procedures (see Section 1.3.7)

The transmission slot (t_slot) shall be the slot containing the unicast request reservation transmission.

Selection of the reserved slot for the response

A block of slots of length V36 to be reserved for the response (address type field ( 7) or broadcast transmission (address type field = 7) shall be selected using the slot selection procedure specified in Section 1.3.6.2, using VSS user supplied quality of service parameters, and candidate slots in the range V32 to V33 after the transmitted burst.

The reserved slot (r_slot) shall be the chosen slot or the first slot in the chosen group of slots.

Unicast request burst transmission

A station sending a unicast request burst to its peer (V35 = 0) shall include the unicast request reservation field. It shall set the destination (d) subfield to the destination of the burst, the response offset (ro) subfield to a value of (r_slot - t_slot -1), the length (lg) subfield equal to (V36 – 1), the priority (pr) subfield equal to the priority of the burst to be transmitted as defined by Q1 and the source/destination flag (sdf) to V34.

A station sending a unicast request burst to reserve a slot for a subsequent broadcast (V35 = 1) shall include the unicast request reservation field. It shall set the response offset (ro) subfield to a value of (r_slot - t_slot - 1), the length (lg) subfield equal to (V36 – 1), the priority (pr) subfield equal to the priority of the burst to be transmitted as defined by Q1 and the address type field equal to 7.

Retransmission after no response

In the case of address type subfield ( 7 and sdf = 0, if a response is not received by the end of the reserved response slot(s), then the station shall retransmit the unicast burst according to the procedures of Section 1.3.21.

Slot selection criteria for unicast request with sdf = 1

A station applying the slot selection criteria of Section 1.3.6.2.2.1 shall exclude any slot reserved by another station using the unicast request protocol with sdf = 1.

Note. – use of the unicast request protocol with sdf = 1 allows a station placing the reservation to transmit to a different destination than the destination included in the reservation field.  One use for this is for a station completing a data transfer to one station by sending an acknowledgement to the destination contained in the unicast reservation field to simultaneously  place a reservation for a later transmission that starts  a new data transfer to a different destination. However, because the destination address for the new station is not known by any other station it is not possible to apply CCI criteria.  Hence the slot must be excluded from slot selection.

Information transfer request protocol specification

Note.— This protocol is intended for a VSS user which requires a peer VSS user to send a response of length, lg. The protocol also allows the requesting VSS user to place a reservation for an acknowledgement by the requesting VSS user to the response field.

Information transfer request reservation burst format

A reservation ID (rid) = 0 with extended reservation ID (erid) = 01010binary and reservation fields set in accordance with Table 1-29 shall indicate an information transfer request reservation. In this case, the information field shall extend up to the last nine octets prior to the CRC.

Table 1-29. Information transfer request reservation bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| acknowledgement offset (ao) | n-10 | res | ao7 | ao6 | ao5 | ao4 | ao3 | ao2 | ao1 |
| length (lg) | n-9 | lg8 | lg7 | lg6 | lg5 | lg4 | lg3 | lg2 | lg1 |
| response offset (ro) | n-8 | ro8 | ro7 | ro6 | ro5 | ro4 | ro3 | ro2 | ro1 |
|  | n-7 | ro12 | ro11 | ro10 | ro9 | f12 | f11 | f10 | f9 |
| frequency (f) destination address (d) | n-6 | f8 | f7 | f6 | f5 | f4 | f3 | f2 | f1 |
|  | n-5 | d24 | d23 | d22 | d21 | d20 | d19 | d18 | d17 |
|  | n-4 | d16 | d15 | d14 | d13 | d12 | d11 | d10 | d9 |
|  | n-3 | d8 | d7 | d6 | d5 | d4 | d3 | d2 | d1 |
|  | n-2 | 0 | 1 | 0 | 1 | 0 | d27 | d26 | d25 |

The subfields shall be as defined in Table 1-30.

Table 1-30. Information transfer reservation field encoding

| Subfield | Range | Encoding |
| --- | --- | --- |
| response offset (ro) | See Table 1-27 |  |
| length (lg) | See Table 1-27 | lg is one less than the number of slots that are reserved for the response |
| acknowledgement offset (ao) | 0 to 127 |  | ao identifies a slot relative to the end of the block of slots reserved by the response offset and length subfields |
| response offset (ro) | See Table 1-27 | ro identifies a slot relative to the first slot of the transmission |
| destination address (d) | See Section 1.4.2.1 | d is be the 27-bit address of the destination station for which the block of slots is being reserved. |
| frequency (f) | bit 12: frequency band indicator: 0: VHF band 108 — 136.975 MHz 1: reserved for future allocation bits 1 to 11: frequency allocation for bit 12 = 0: 1 to 1160 per frequency band in 25kHz increments. 1161 to 2047 reserved for future allocation. 1 indicates bottom of band. f = 001 hex = 108.000 MHz f = 000 hex if the subfield is to be ignored | The frequency subfield (f) identifies the frequency on which the reservation is to be made for the response. (See Section 1.3.15.5) |

Information transfer request parameters

The information transfer request protocol shall implement the system parameters defined in Table 1-31.

Table 1-31. Information transfer request VSS system parameters

| Symbol | Parameter name | Minimum | Maximum | Recommended default | Increment |
| --- | --- | --- | --- | --- | --- |
| V42 | Length of information transfer | 1 slot | 256 slots | N/A (depends on information to be transmitted) | 1 slot |
| V43 | Minimum information transfer delay | 2 slot | 500 slots | 20 slots | 1 slot |
| V44 | Maximum information transfer delay | 2 slot | 2047 slots | 1000 slots | 1 slot |
| V45 | Minimum response delay | 2 slot | 500 slots | 20 slots | 1 slot |
| V46 | Maximum response delay | 2 slot | 2047 slots | 1000 slots | 1 slot |

The VSS user shall provide the destination address and any of the parameters V42, V43, V44, V45, V46 and quality of service parameters (Q2a to Q2d and Q4) for which the default values are not desired.

Parameter V42 (length of information transfer)

Parameter V42 shall be the number of slots required for information transfer.

Parameter V43 (minimum information transfer delay)

Parameter V43 shall be the minimum delay, measured in slot intervals, that a station will provide to a responder in order to ensure that the responder can generate the required information for transfer before its reserved slots.

Note.— V43*60/M1 is the maximum time that a station is provided with to generate a response to the request.

Parameter V44 (maximum information.transfer delay)

Parameter V44 shall be the maximum delay, measured in slot intervals, that a station will provide to a responder in order to ensure timely delivery in case a retransmission is required.

Parameter V45 (minimum response delay)

Parameter V45 shall be the minimum delay, measured in slot intervals after the information transfer that the requesting station will require in order to generate an acknowledgement to the information transfer in order to ensure that the requesting station can generate the acknowledgement before its reserved slot.

Note.— V45*60/M1 is the maximum time that a station is provided with to generate an acknowledgement to the information transfer.

Parameter V46 (maximum response delay)

Parameter V46 shall be the maximum delay, measured in slot intervals after the information transfer that the requesting station will require in order to ensure timely delivery of the acknowledgement in case a retransmission is required.

Information transfer request reception procedures

Upon receipt of a burst containing an information transfer request reservation, a station shall reserve on the specified frequency all of the slots from (1 + ro) through (1 + ro + lg) after the first slot of the received burst for the destination to transmit one or more information frames to the source. Also, the slot equal to (2+ ro + lg + ao) after the first slot of the received burst shall be reserved for the source to transmit an acknowledgement to the destination.

Information transfer request transmission procedures

Selection of the transmission slot for the information transfer request reservation

If no slot has been reserved for transmission of an information transfer request reservation, the station shall select a slot using the random access procedures (see Section 1.3.7).

The transmission slot (t_slot) shall be the slot containing the information transfer request reservation transmission.

Selection of the reserved slots for the response

A block of slots of length V42 to be reserved for the response shall be selected using the slot selection procedure specified in Section 1.3.6.2, using VSS user supplied quality of service parameters, and candidate slots in the range V43 to V44 after the transmitted burst.

The reserved slot (r_slot) shall be the chosen slot or the first slot in the chosen group of slots.

Selection of the reserved slot for the acknowledgement

The acknowledgement slot (a_slot) shall be selected using the slot selection procedure specified in Section 1.3.6.2, using VSS user supplied quality of service parameters, and candidate slots in the range V45 to V46 after the end of the slot or group of slots reserved for the response.

Information transfer request burst transmission

A station sending an information transfer request burst to its peer shall include the information transfer request reservation field. It shall set the destination (d) subfield to the destination of the burst, the response offset (ro) subfield to a value of (r_slot - t_slot -1), the length (lg) subfield equal to (V42-1), the frequency (f) subfield set to the channel on which information transfer is required and the acknowledgement offset (ao) subfield set to a value of (a_slot - r_slot - lg - 1).

Action after no response

If a response is not received by the reserved information transfer slots, then the station shall inform the VSS user that no response has been received and carry out the actions defined by the VSS user.

Note.- For example, if the information transfer protocol is being used as part of DLS long transmission procedure, the defined action is to send a NACK in the slot reserved for the acknowledgement

Information transfer request acknowledgement procedures

The acknowledgement shall be on the same frequency as the information transfer reservation burst that was used to reserve a slot for the acknowledgement.

Directed request protocol specification

Note.— This protocol is intended for a VSS user which is responding to a plea for slot reservations (rapid network entry), or which requires periodic broadcast responses from a peer VSS user. Both of these scenarios involve reservations calculated and declared for use by the peer station. In addition, this protocol allows a VSS user to request that a peer VSS user autonomously transmit at a  specified rate.

Directed request reservation burst format

A reservation ID (rid) = 0, an extended reservation ID (erid) = 01100binary, and reservation fields set in accordance with Table 1-32 shall indicate a directed request reservation. The length of the reservation field shall be determined by the value of the plea response flag (pr_flag). For the case of pr_flag = 1, the information field shall extend up to the last fourteen octets prior to the CRC. For the case of pr_flag = 0, the information field shall extend up to the last ten octets prior to the CRC. The nominal update rate (nr) field shall be encoded in accordance with Table 1-33. The 27-bit destination address (d) shall be the 27-bit address of the destination station for whom reservations are being created.

Note.— The directed request reservation burst may be used for a plea response, autotune, or other directed request application.

Table 1-32. Directed request reservation bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Identification of additional Reservation data | n-15 |  |  |  |  |  |  |  |  |
|  | n-14 |  |  |  |  |  |  |  |  |
|  | n-13 |  |  |  |  |  |  |  |  |
|  | n-12 |  |  |  |  |  |  |  |  |
|  | n-11 |  | per tables 1-34, 1-36 through 1-37 |  |  |
|  | n-10 |  |  |  |  |  |  |  |  |
|  | n-9 |  |  |  |  |  |  |  |  |
|  | n-8 |  |  |  |  |  |  |  |  |
|  | n-7 |  |  |  |  |  |  |  |  |
| Nominal update rate (nr); Plea response flag (pr_flag) | n-6 |  |  |  | pr_flag | nr4 | nr3 | nr2 | nr1 |
| Destination address (d) | n-5 | d24 | d23 | d22 | d21 | d20 | d19 | d18 | d17 |
|  | n-4 | d16 | d15 | d14 | d13 | d12 | d11 | d10 | d9 |
|  | n-3 | d8 | d7 | d6 | d5 | d4 | d3 | d2 | d1 |
| Extended reservation ID (erid) | n-2 | 0 | 1 | 1 | 0 | 0 | d27 | d26 | d25 |

Table 1-33. Nominal update rate encoding

| Encoded data | Nominal update rate (transmissions per minute) |
| --- | --- |
| nr4 | nr3 | nr2 | nr1 | nr |
| 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 0 | 1 | 2 |
| 0 | 0 | 1 | 0 | 3 |
| 0 | 0 | 1 | 1 | 4 |
| 0 | 1 | 0 | 0 | 5 |
| 0 | 1 | 0 | 1 | 6 |
| 0 | 1 | 1 | 0 | 8 |
| 0 | 1 | 1 | 1 | Invalid |
| 1 | 0 | 0 | 0 | 10 |
| 1 | 0 | 0 | 1 | 12 |
| 1 | 0 | 1 | 0 | 15 |
| 1 | 0 | 1 | 1 | 20 |
| 1 | 1 | 0 | 0 | 30 |
| 1 | 1 | 0 | 1 | 60 |
| 1 | 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | Special |

Autotune reservation burst format

A directed request reservation burst with pr_flag = 0 shall indicate an autotune reservation. Additional reservation data shall be set in accordance with Table 1-34 with subfields defined in accordance with Table 1-35.

A reservation with do = 0, rcvr = 00binary and f ( current frequency is invalid and shall be handled as per Section 1.3.5.

Table 1-34. Encoding of additional data in autotune reservation burst

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Directed timeout (dt) | n-11 | dt4 | dt3 | dt2 | dt1 | f12 | f11 | f10 | f9 |
| Frequency (f) | n-10 | f8 | f7 | F6 | f5 | f4 | f3 | f2 | f1 |
| Length (lg) | n-9 | lg8 | lg7 | lg6 | lg5 | lg4 | lg3 | lg2 | lg1 |
| Transmit control (trmt) | n-8 | res | res | trmt | do13 | do12 | do11 | do10 | do9 |
| Directed offset (do) | n-7 | do8 | do7 | do6 | do5 | do4 | do3 | do2 | do1 |
| Override flag (or); receiver control (rcvr); nominal update rate (nr); pr_flag = 0 | n-6 | or | rcvr2 | rcvr1 | 0 | nr4 | nr3 | nr2 | nr1 |

Table 1-35. Directed request reservation field encoding

| Subfield | Range | Encoding | Definitions |
| --- | --- | --- | --- |
| length (lg) | 0 to 255 | See Table 1-27 | lg is one less than the number of slots that are reserved |
| Directed timeout (dt) | 0 to 15 | A value of 15 cancels the reservation | dt = the number of planned future transmissions reserved in slots spaced M1 slots apart |
| Nominal rate (nr) | 0 to 60 | See Table 1-33 When pr_flag = 0, nr = special is invalid | See Table 1-33 |
| Override flag (or) | 0 to 1 | See Section 1.3.16.3.1 | or indicates whether the current directed request reservation burst overrides all previous directed request reservations issued by the station on the indicated frequency |
| Receiver control (rcvr) | 0 to 3 | 00 = Station must continue to monitor the current frequency; 01 = Station must monitor the indicated frequency; 10= Autonomous decision; 11 = Station must continue to monitor the current frequency and also the indicated frequency | Defines handling of receiver tuned to frequency used to receive this burst. |
| Transmit control (trmt) | 0 to 1 | 0 = cancel transmissions on the current frequency (see 1.3.10.5.9) 1 = continue transmission on the current frequency (see 1.3.16.5.3) |  |
| Directed offset (do) | 0 or 2 to 213 – 1 | do = 1: invalid | do = 0 implies directed rate reservation. do >1 implies directed slot reservation. For do>1, do = the first slot in which to transmit. |
| offset to first reserved slot (off) | 2 to 29-1 | off = 0,1: invalid | off = the first slot in which to transmit (for plea response) |
| Additional slots (aj) | 1 to 2k-1 (k=6,12) | aj = 20 hex and nr special: invalid Note: k is the number of bits in each aj. k=6 for nr “special”, and k=12 for nr = “special”. j is the number of additional slots | For nr “special”, aj is encoded as two’s complement offset about a nominal slot defined by the offset to the first slot, and the nominal rate. For nr = special, a is encoded as a binary increment from the previously-reserved slot. aj refers to the additional slot |
| Frequency (f) | See 1.4.1.2 | See Table 1-30 | Defines new frequency for transmissions of required data. |
| plea response flag (pr_flag) | See 1.3.16.1 |  |

Plea response burst format

A directed request reservation with pr_flag = 1 shall indicate a network entry plea response. In this case, the reservation data not previously defined shall be encoded as indicated in Tables 1-36 and 1-37 with subfields set in accordance with Table 1-35, and shall consist of: a) the offset to a first reserved slot; and b) offsets to an additional n reserved slots as appropriate. Additional reserved slots shall be encoded as follows: slots 1 to n shall be encoded in additional slots a1 to an; additional slots an+1 to aN, where N is the maximum number of additional slots that can be accommodated in the formats defined by Tables 1-36 and 1-37, shall be set to zero.

Note 1. – In the format defined by table 1-36, up to 11 additional slots can be accommodated with offsets encoded using 6 bits.  In the format defined by table 1-37, up to 5 additional slots can be accommodated with offsets encoded using 12 bits.

Note 2.— This protocol is intended as a response for a VSS user which has no knowledge of the reservation table  and must be given a large number of reservations in a single transmission. It is primarily intended as a response to a plea for help during rapid network entry (e.g., when a peer station asks for help in setting-up a sequence of streams for synchronization bursts). However, it may be transmitted by the destination station to give itself quickly a large number of reservations.

Table 1-36. Encoding of additional data with nr (“special”

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| additional slots (aj) | n-15 | a11,6 | a11,5 | a8,6 | a8,5 | a8,4 | a8,3 | a8,2 | a8,1 |
|  | n-14 | a11,4 | a11,3 | a7,6 | a7,5 | a7,4 | a7,3 | a7,2 | a7,1 |
|  | n-13 | a11,2 | a11,1 | a6,6 | a6,5 | a6,4 | a6,3 | a6,2 | a6,1 |
|  | n-12 | a10,6 | a10,5 | a5,6 | a5,5 | a5,4 | a5,3 | a5,2 | a5,1 |
|  | n-11 | a10,4 | a10,3 | a4,6 | a4,5 | a4,4 | a4,3 | a4,2 | a4,1 |
|  | n-10 | a10,2 | a10,1 | a3,6 | a3,5 | a3,4 | a3,3 | a3,2 | a3,1 |
|  | n-9 | a9,6 | a9,5 | a2,6 | a2,5 | a2,4 | a2,3 | a2,2 | a2,1 |
|  | n-8 | a9,4 | a9,3 | a1,6 | a1,5 | a1,4 | a1,3 | a1,2 | a1,1 |
| offset to first reserved slot (off) | n-7 | a9,2 | a9,1 | off9 | off8 | off7 | off6 | off5 | off4 |
| nominal rate(nr); pr_flag = 1 | n-6 | off3 | off2 | off1 | 1 | nr4 | nr3 | nr2 | nr1 |

Table 1-37. Encoding of additional data for nr = ‘special’

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| additional slots (aj) | n-15 | res | res | res | res | a5,12 | a5,11 | a5,10 | a5,9 |
|  | n-14 | a5,8 | a5,7 | a5,6 | a5,5 | a5,4 | a5,3 | a5,2 | a5,1 |
|  | n-13 | a4,8 | a4,7 | a4,6 | a4,5 | a4,4 | a4,3 | a4,2 | a4,1 |
|  | n-12 | a4,12 | a4,11 | a4,10 | a4,9 | a3,12 | a3,11 | a3,10 | a3,9 |
|  | n-11 | a3,8 | a3,7 | a3,6 | a3,5 | a3,4 | a3,3 | a3,2 | a3,1 |
|  | n-10 | a2,8 | a2,7 | a2,6 | a2,5 | a2,4 | a2,3 | a2,2 | a2,1 |
|  | n-9 | a2,12 | a2,11 | a2,10 | a2,9 | a1,12 | a1,11 | a1,10 | a1,9 |
|  | n-8 | a1,8 | a1,7 | a1,6 | a1,5 | a1,4 | a1,3 | a1,2 | a1,1 |
| offset to first reserved slot (off) | n-7 | res | res | off9 | off8 | off7 | off6 | off5 | off4 |
| nominal rate (nr); pr_flag = 1 | n-6 | off3 | off2 | off1 | 1 | 1 | 1 | 1 | 1 |

Directed request parameters

The directed request protocol shall implement the system parameters defined in Table 1-38.

Table 1-38. Directed request VSS system parameters

| Symbol | Parameter Name | Minimum | Maximum | Recommended default | Increment |
| --- | --- | --- | --- | --- | --- |
| V52 | Minimum response delay | 1 slot | 500 slots | 20 slots | 1 slot |

The VSS user shall provide the destination address and any of the parameters  V52 and quality of service parameters (Q2a to Q2d, Q4 and Q5) for which the default values are not desired.

Parameter V52 (minimum response delay)

Parameter V52 shall be the minimum time that a station will provide to a responder in order to ensure timely delivery in case a retransmission is required.

Directed request reception procedures

Autotune reception procedures

Upon receipt of a burst containing an autotune reservation (pr_flag = 0), the station shall update its reservation table  and carry out the actions as specified in Table 1-39.

Table 1-39. Action on receipt of an autotune reservation burst

| Directed offset (do) | Directed timeout (dt) | Action |
| --- | --- | --- |
| 0 | any | See 1.3.16.5.2. |
| 1 | any | Invalid |
| 1 < do < M1 | dt < 15 | Reserve the following slots for the destination to broadcast: for j equal to 0 to 3 and k equal to 0 to nr - 1, the slots equal to truncate (do + (k * M1/nr) + j * M1) through (lg + truncate (do + (k * M1/nr) + j * M1)) after the first slot of the received burst |
| 1 < do < M1 | dt = 15 | Reserve the following slots for the destination to broadcast: for k equal to 0 to nr - 1, the slots equal to truncate (do + (k * M1/nr)) through (lg + truncate (do + (k * M1/nr))) after the first slot of the received burst |
| do > M1-1 | any | Invalid |

If the override (or) flag is set to 1, the destination station shall cancel all previously placed autotune reservations made by the source station on frequency f (see Section 1.3.10.5.9), otherwise it shall retain them.

Note 1.— In the case of dt = 15, slots are reserved in the current superframe for the destination to transmit periodic broadcast reservation bursts with po = 0 and pt = 0. These bursts have the effect of cancelling the directed reservations for each slot (see Sections 1.3.16.4.4 and 1.3.16.5.4).

Note 2.— Only the destination station cancels previously placed reservations (e.g. due to a directed request with the override bit set). Other stations wait until the destination station announces its intent before updating their reservation table.

The burst is invalid, and shall be handled as per Section 1.3.5, if the frequency subfield is equal to 000 hex, or fails to map to a known frequency, or indicates a frequency on which the transmitter cannot transmit.

Plea response reception procedures

Upon receipt of a burst containing a plea response reservation (pr_flag = 1), a station shall reserve the slots equal to ‘off’ after the first slot of the received burst and the series of slots rj for the destination to broadcast.

If nr ( ‘special’, then rj shall be:

rj = (off + truncate (j * M1/nr) + aj) for j = 1 to N,

where N is the maximum number of additional slots defined in the additional slots subfield (see Section 1.3.16.1.2),

If nr = ‘special’, then rj shall be defined as:

rj =(off + m=1j am) for j = 1 to N

Note.— Burst length is not included in the plea response, so these reservations are for single slots only.

Directed request transmission procedures

Recommendation

Note.— Selection of slots for directed request transmission can use the general procedures set out in Section 1.3.6.2 or use fixed transmission procedures (1.3.8). Since it is expected that the autotune reservation protocol will be used only by ground stations, the fixed transmission procedures are recommended, implemented in a manner that takes advantage of ground quarantining (see Section 1.3.6.4) and causes the formation of contiguous groups of ground directed slots.

The directed request protocol with pr_flag = 0 (autotune reservation) should only be used by ground stations and should use fixed transmission procedures to select slots for transmission of the autotune reservation burst and to form contiguous blocks of directed reservations.

The transmitting station should ensure that, if two users are allocated the same slots, they are sufficiently separated and on divergent paths such that the possible loss of communications between them is not significant.

Autotune transmission procedures

A station sending an autotune reservation (pr_flag = 0) to its peer shall set the destination (d) subfield to the destination of the burst, the frequency (f) subfield to the frequency on which the responder is to transmit, the directed offset (do) subfield to either 0 (for a directed rate reservation), or the offset from the first slot of the autotune reservation burst to the first slot in which to transmit (for a directed slot reservation), the nominal rate (nr) subfield to the number of times per M1 slots that a response is requested using the encoding defined in Table 1-33, and the directed timeout (dt) subfield to the span of dt*M1 slots over which the destination is to transmit. The value of the directed offset (do) subfield shall be greater than V52.

Retransmission after no response

There shall be no automatic retransmission of plea response bursts (pr_flag = 1). For autotune reservation bursts (pr_flag = 0), if a response is not received in the first directed slot after the autotune burst was transmitted, then the station shall retransmit the autotune reservation burst according to the procedures of Section 1.3.21.

Cancellation of autotune reservation

A station shall cancel an autotune reservation (pr_flag = 0) by transmitting an autotune reservation field with the directed timeout subfield set to 15. It is to set the destination subfield to the destination of the burst, the frequency subfield to the frequency on which the responder has previously been directed to broadcast, the directed offset (do) to the offset from the first slot of the autotune reservation burst to the first slot for which a reservation is to be cancelled and the nominal rate subfield to the number of slots per M1 slots for which a reservation shall be cancelled.

Note.— The settings of the directed offset and nominal rate subfields are the same as the original settings used to place the reservations. Hence this form of the autotune reservation can be used to exactly cancel a previous reservation. This protocol can also be used to cancel a subset of the reports established by the original autotune command. For example, if the directed reporting rate is 12/minute, a cancellation with nominal rate subfield set to 6/minute would leave a net reporting rate of 6/minute.

Plea response transmission procedures

A station transmitting a plea response (pr_flag = 1) shall set the destination (d) to the destination of the burst, the offset (off) subfield to the offset from the first slot of the reservation burst to the first slot in which to transmit, and the nominal rate (nr) subfield to the nominal number of times per M1 slots that a synchronization burst is to be sent on the frequency used for transmission. The value of the offset (off) subfield shall be greater than V52. A station shall ensure that the slots selected in the transmission satisfy the nominal update rate requirements and all of the requirements of Section 1.3.6.2. A station shall check to determine if a previous plea response had been sent to the mobile making the plea (i.e. the destination ID for this plea response), and if so, it shall begin the list of reserved slots with the remaining (future) reservations from the earlier plea response.

Note.— When the plea response can not encode sufficient reservations for a full 60 seconds, the destination station may issue a subsequent plea as the initial set of  reservations is consumed.

Directed request response procedures

Response to an autotune reservation with do > 1

On receipt of an autotune reservation transmission (pr_flag = 0) with the directed offset subfield (do) greater than 1, the responder station indicated by the destination address shall set the TV11 timer (see Section 1.3.10.2.1) equal to the value of the directed timeout (dt) subfield for each of the slots indicated in the autotune reservation transmission. The responder station shall transmit in each of the reserved slots. Each response burst shall contain the periodic broadcast reservation field with the periodic offset (po) subfield set to 0 and the periodic timeout (pt) subfield set to min(3, TV11-1). After transmission, the timer TV11 shall be decremented. When TV11 reaches zero, the responder shall not transmit a response to the directed request. Upon cessation of directed transmissions, the responder shall resume default autonomous behaviour on the GSCs, reserving new slots as required.

Note 1.— For example, when a station completes its series of directed synchronization burst transmissions on a local channel, it will resume autonomous synchronization bursts on the GSCs. This behaviour allows a ground station to implicitly hand-off a mobile as the mobile departs a defined airspace, and also ensures appropriate behaviour if the mobile unexpectedly flies out-of-coverage or the ground station fails.

Note 2.— When a station is no longer required to transmit a response to the directed request, it will revert to the autonomous mode as described in Section 1.5.6.1.2.

Recommendation

To simplify and ease the transition from a) directed slot  operations on local channels, to b) directed rate or autonomous mode operations on another channel, ground stations should attempt to autotune mobile stations (using a directed slot reservation) to the new channel, for a period of at least 60 seconds, prior to release. The mobile station should then use the BND reservation to continue the stream while it is building the reservation table  and operating under ground control.

Response to an autotune reservation with do  = 0.

If the directed offset subfield is equal to 0, the responder station shall operate autonomously using the periodic broadcast procedures with the nominal periodic rate (V11) set to nr in the autotune reservation transmission for the next dt*M1 slots, with the first two bits of the message ID field set to “00”. Upon cessation of directed transmissions, the responder shall resume default autonomous behaviour on the GSCs, reserving new slots as required.

Note 1.— For example, when a station completes its series of directed synchronization burst transmissions on a local channel, it will resume autonomous synchronization bursts on the GSCs. This behaviour allows a ground station to implicitly hand-off a mobile as the mobile departs a defined airspace, and also ensures appropriate behaviour if the mobile unexpectedly flies out-of-coverage or the ground station fails.

Note 2.— When a station is no longer required to transmit a response to the directed request, it will revert to the autonomous mode as described in Section 1.5.6.1.2.

Cancellation of autonomous periodic broadcasts

If trmt = 0 and if the responder was transmitting autonomously the VSS user data for which a directed request reservation was received, then it shall cancel its existing reservations in accordance with paragraph 1.3.10.5.9, and operate in accordance with the parameters of the directed request. If trmt = 1 and if the responder was transmitting autonomously on the channel on which a directed request reservation was received, then it shall maintain its autonomous transmissions on the channel.

Cancellation of directed request broadcasts

If the responder receives a directed request reservation burst with the directed timeout subfield set to 15, then it shall cancel its existing reservations in accordance with paragraph 1.3.10.5.9.

Response if unable to support directed request

If the responder is unable to support the directed request it shall transmit a general failure (see section 1.3.20.1) with error type 05 hex.  If there are insufficient receiver resources to meet the request it shall set bit 1 of the parameter sub-field to 1.  All other bits in the parameter sub-field shall be set to 0.

Recommendation

If possible, a responder sending a general failure should use slots reserved by the ground station on the channel indicated in the directed request.  Otherwise, the station should use the combined periodic/incremental reservation protocol to place the transmission on the channel on which the directed request was received.

Block reservation protocols specification

Note.— These protocols are intended for a VSS ground station which requires to reserve a block of slots for its own use. The superframe block reservation protocol establishes a series of blocks of slots in which no other station is allowed to place a reservation or to transmit. The second frame block reservation protocol establishes a block at the beginning of each UTC second. Network entry transmissions are also prohibited (see 1.3.6.4.3) in both types of blocks. The superframe block reservation protocol provides a facility for re-broadcasting of the block reservation by a mobile.

Superframe block reservation burst format

A reservation ID (rid) = 0, an extended reservation ID (erid) = 110, and reservation fields set in accordance with Table 1-40, with subfields defined in accordance with Table 1-41, shall indicate a superframe block reservation. The information field shall extend up to the last nine octets prior to the CRC. A burst containing a superframe block reservation shall not exceed twenty-one octets (not including the CRC).

Table 1-40. Superframe block reservation bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| destination address (d) | n-10 | d24 | d23 | d22 | d21 | d20 | d19 | d18 | d17 |
|  | n-9 | d16 | d15 | d14 | d13 | d12 | d11 | d10 | d9 |
|  | n-8 | d8 | d7 | d6 | d5 | d4 | d3 | d2 | d1 |
| block length (blg) | n-7 | blg5 | blg4 | blg3 | blg2 | blg1 | d27 | d26 | d25 |
| re-broadcast offset (roff) | n-6 | roff8 | roff7 | roff6 | roff5 | roff4 | roff3 | roff2 | roff1 |
| block repeat rate (br) | n-5 | res | res | res | res | br4 | br3 | br2 | br1 |
| block start (bs) | n-4 | bs8 | bs7 | bs6 | bs5 | bs4 | bs3 | bs2 | bs1 |
| block offset (bo) | n-3 | bo8 | bo7 | bo6 | bo5 | bo4 | bo3 | bo2 | bo1 |
| extended reservation ID (erid), block timeout (bt) | n-2 | 0 | 0 | 0 | 1 | 0 | res | bt2 | bt1 |

Table 1-41. Superframe reservation field encoding

| Subfield | Range | Encoding | Definitions |
| --- | --- | --- | --- |
| block timeout (bt) | 0 to 3 |  | bt * M1 = the number of slots for which the block reservation should be maintained |
| block repeat rate (br) | 1 to 60 | See Table 1-33. Codes 0111, 1110 and 1111 are invalid | Defines the number of blocks per minute |
| re-broadcast offset (roff) | 2 to 255 | bs = 0,1 invalid | roff indicates the slot in which the re-broadcast transmission should be made |
| block start (bs) | 2 to 255 | bs = 0,1 invalid | bs identifies a slot relative to the transmission slot which is the first slot of the first reserved block |
| block offset (bo) | –127 to +127 | Two’s complement math | bo identifies an offset of each reserved block at a future time defined by bt * M1 |
| block length (blg) | 0 to 31 |  | blg is one less than the number of slots reserved for the block |
| destination address (d) | See Table 1-27 | Ignored if ro = bs and octets n – 10 through n – 8 available for use within the information field. | d is the 27-bit address of the destination station which is required to re-broadcast the blocking message |

Second frame block reservation burst format

A reservation ID (rid) = 0, an extended reservation ID (erid) = 00011, and reservation fields set in accordance with Table 1-42, with subfields defined in accordance with Table 1-43, shall indicate a second frame block reservation. The information field shall extend up to the last two octets prior to the CRC.

Table 1-42. Second frame block reservation bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| timeout (vt) | n – 3 | vt6 | vt5 | vt4 | vt3 | vt2 | vt1 | sz5 | sz4 |
| size (sz) | n – 2 | 0 | 0 | 0 | 1 | 1 | sz3 | sz2 | sz1 |

Table 1-43. Second frame block reservation field encoding

| Subfield | Range | Definitions |
| --- | --- | --- |
| size (sz) | 0 to 31 | Number of slots to block after the start of each UTC second. |
| timeout (vt) | 1 to 60 | Value of TV61 |

Superframe block reservation parameters

The superframe block reservation protocol shall implement the system parameters defined in Table 1-44.

Table 1-44. Superframe block reservation VSS system parameters

| Symbol | Parameter name | Minimum | Maximum | Default | Increment |
| --- | --- | --- | --- | --- | --- |
| V61 | Superframe block start offset | 2 | 255 | 20 | 1 |
| V62 | Superframe block length | 1 | 32 | 3 | 1 |
| V63 | Superframe block repeat rate | 1 | 60 | 5 | See Table 1-33 for allowed values |
| V64 | Superframe block re-broadcast request | No | Yes | No | - |
| V65 | Superframe block re-broadcast offset | 2 | 255 | 10 | 1 |

For each superframe block reservation, the VSS user shall provide one or more sets of parameters consisting of:

a)	the time of the required superframe block ground transmission;

b)	the parameters V61 and V65 for which the default values are not desired;

c)	quality of service parameters (Q2a to Q2d, Q4 and Q5) for which the default values are not desired.

The station shall use the first set of parameters to calculate the position and subfield settings for the first ground station transmission as specified in Section 1.3.17.7.1 and then use each following set to move the position of the reserved blocks. Where possible, the station shall pre-announce that a block is to move using the block offset subfield as defined in Section 1.3.17.7.1.

Parameter V61 (superframe block start offset)

Parameter V61 shall be the offset to the start of the first reserved block from the slot containing the ground transmission.

Parameter V62 (superframe block length)

Parameter V62 shall be the length in slots of each reserved block.

Parameter V63 (superframe block repeat rate)

Parameter V63 shall be number of reserved slots per M1 slots encoded as defined in Table 1-33.

Parameter V64 (superframe block re-broadcast request)

Parameter V64 shall determine whether the superframe block reservation request is to be re-broadcast by a mobile using the procedures defined in Section 1.3.17.7.2.

Parameter V65 (superframe block re-broadcast offset)

Parameter V65 shall be the offset to the slot containing the re-broadcast from the slot containing the ground transmission.

Superframe block reservation reception procedures

Upon receipt of a burst containing a superframe block reservation, the station shall update its reservation table  and carry out the actions as specified in Tables 1-45 and 1-46.

Note.— The actions defined in Table 1-45 establish a series of reserved blocks of slots.

Table 1-45. Actions on receipt of a superframe block reservation burst

| Block start (bs) | Block offset (bo) | Block timeout (bt) | Action |
| --- | --- | --- | --- |
| bs < 2 | Any | Any | Invalid |
| bs ( 2 | Any except 0 | 0, 1, 2 | Reserve the following slots for the source or a mobile directed by the source to broadcast: if bt = 1 or 2 then for j equal to 0 to bt and k equal to 0 to br – 1, the slots equal to truncate (bs + (k * M1 / br) + j * M1) through (blg + truncate (bs + (k * M1 / br) + j * M1)) after the first slot of the received burst AND for j equal to bt + 1 to 3 and k equal to 0 to br – 1, the slots equal to truncate (bs + bo + (k * M1 / br) + j * M1) through (blg + truncate (bs + bo + (k * M1 / br) + j * M1)) after the first slot of the received burst |
| bs ( 2 | 0 | 0, 1 or 2 | Reserve the following slots for the source or a mobile directed by the source to broadcast: for j equal to 0 to bt and k equal to 0 to br – 1, the slots equal to truncate (bs + (k * M1 / br) + j * M1) through (blg + truncate (bs + (k * M1 / br) + j * M1)) after the first slot of the received burst Thereafter, terminate the reservations. |
| bs ( 2 | Any | 3 | Reserve the following slots for the source or a mobile directed by the source to broadcast: for j equal to 0 to bt and k equal to 0 to br - 1, the slots equal to truncate (bs + (k * M1 / br) + j * M1) through (blg + truncate (bs + (k * M1 / br) + j * M1)) after the first slot of the received burst |

Note.— The actions in Table 1-46 reserve the slot used by the station to provide a superframe block reservation in subsequent superframes.

Table 1-46. Further actions on receipt of a superframe block reservation burst

| Block offset (bo) | Block timeout (bt) | Action |
| --- | --- | --- |
| Any except 0 | 0, 1, 2 | Reserve the following slots for the source to broadcast: if bt = 1 or 2 then for j equal to 1 to bt, the slot equal to (j * M1) after the first slot of the received burst AND for j equal to bt + 1 to 3, the slot equal to (bo + j * M1) after the first slot of the received burst |
| 0 | 0, 1 or 2 | Reserve the following slots for the source to broadcast: for j equal to 1 to bt, the slot equal to (j * M1) after the first slot of the received burst Thereafter, terminate the reservations. |
| Any | 3 | Reserve the following slots for the destination to broadcast: for j equal to 1 to bt, the slot equal to (j * M1) after the first slot of the received burst |

If the re-broadcast offset (roff) is not equal to the block start (bs), the station shall carry out the actions specified in Table 1-47.

Note.— The actions in Table 1-47 are carried out if a ground station wishes to re-broadcast the block message via a mobile.

Table 1-47. Action on receipt of a superframe block reservation burst if roff is not equal to bs

| Re-broadcast offset (roff) | Block offset (bo) | Block timeout (bt) | Action |
| --- | --- | --- | --- |
| roff < 2 | Any | Any | Invalid |
| roff ( 2 | Any except 0 | 0, 1, 2 | Reserve the following slots for the destination to broadcast: if bt = 1 or 2 then for j equal to 0 to bt, the slot equal to (roff + j * M1) after the first slot of the received burst AND for j equal to bt + 1 to 3, the slot equal to (roff + bo + j * M1) after the first slot of the received burst |
| roff ( 2 | 0 | 0, 1 or 2 | Reserve the following slots for the destination to broadcast: for j equal to 0 to bt, the slot equal to (roff + j * M1) after the first slot of the received burst Thereafter, terminate the reservations. |
| roff ( 2 | Any | 3 | Reserve the following slots for the destination to broadcast: for j equal to 0 to bt, the slot equal to (roff + j * M1) after the first slot of the received burst |

Second frame block reservation parameters

The VSS user shall provide a value for the parameter TV61, defined in Table 1-48, for which the default values are not desired.

Table 1-48. Second frame block reservation parameters

| Symbol | Parameter Name | Minimum | Maximum | Default | Increment |
| --- | --- | --- | --- | --- | --- |
| TV61 | Second frame block reservation timeout | 1 superframe | 60 superframes | 4 superframes | 1 superframe |
| V66 | Second frame block size | 0 | 31 | 8 | 1 |
| V67 | Second frame block repeat rate | 0 | 60 | 3 | See Table 1-33 for allowed values |

For each second frame block reservation, the VSS user shall provide one or more sets of parameters consisting of the parameters V66 and V67 for which the default values are not desired and quality of service parameters (Q2a to Q2d, Q4 and Q5) for which the default values are not desired.

Timer TV61 (second frame block reservation timeout)

The timer TV61 shall control the time which a second frame block reservation is valid. When timer TV61 times out the mobile station shall return to the initial state defined in Table 1-48.

Parameter V66 (second frame block size)

Parameter V66 shall be the size of the second frame block.

Parameter V67 (second frame block repeat rate)

Parameter V67 shall be number of times per M1 slots that a second frame reservation transmission is repeated encoded as defined in Table 1-33.

Second frame block reservation reception procedures

Upon receipt of a burst containing a second frame block reservation, the station shall update its reservation table by reserving the first sz slots of every UTC second and set the timer TV61.

Superframe block reservation transmission procedures

Recommendation

Note.— Selection of slots for superframe block transmission can use the general procedures set out in Section 1.3.6.2 or use fixed transmission procedures (see Section 1.3.8). Since it is expected that the superframe block reservation protocol will be used only by ground stations, the fixed transmission procedures are recommended.

The superframe block reservation protocol should only be used by ground stations and should use fixed transmission procedures to select slots for transmission of the superframe block reservation bursts. The superframe block reservation should only be used by a mobile under ground direction as the result of a prior superframe block reservation burst issued by a ground station with the re-broadcast offset (roff) subfield not equal to the block start (bs) subfield.

Procedures for establishment of reserved blocks of slots

A station shall establish reserved blocks of slots by broadcasting a superframe block reservation. The station shall set the block start (bs) subfield to the offset from the first slot of the transmitted burst to the first slot of the first reserved block of slots as defined by parameter V61, the block repeat rate (br) subfield to the number of blocks per M1 slots defined by V63 using the encoding defined in Table 1-33, the block length (blg) equal to one less than V62  and the block timeout (bt) subfield to the span of bt*M1 slots over which the reservations defined by bs and br are to be maintained. If the value of bt is equal to 0, 1 or 2, the value of the block offset (bo) subfield shall be set to 0 if it is intended that the superframe block reservation will terminate after bt*M1 slots, or the offset from the first slot of the first reserved block if it is intended that the block reservation will move after bt*M1 slots. The value of bt shall not be set to –128.

Cancellation of reserved blocks of slots

A station shall cancel a superframe block reservation by transmitting a superframe block reservation field with bt equal to 0, 1 or 2 and bo equal to 0, in which case the superframe block reservation will be cancelled after M1 * bt + bs slots. It shall set the block start (bs) to the offset from the first slot of the transmitted burst to the first slot of the first block for which a reservation is to be cancelled as defined by parameter V61, the block length (blg) equal to one less than V62 and the block repeat rate (br) subfield to the number of blocks per M1 slots defined by parameter V63 for which a superframe block reservation is to be cancelled, using the encoding defined in Table 1-33.

Note.— The settings of the block start and block repeat rate subfields are the same as the original settings used to place the reservations.

Procedures to request re-broadcasting of a superframe block reservation

To request that a station, B, re-broadcast the superframe block reservation, station A shall transmit a superframe block reservation. Station A shall set the destination (d) to the address of station B and set the re-broadcast offset (roff) subfield to the offset from the first slot of the reservation burst to the first slot in which B should transmit. The value of the re-broadcast offset (roff) subfield shall be less than the value of the block start (bs) subfield.

If no re-broadcast of the superframe block message is required, the ground station shall set the re-broadcast offset (roff) subfield equal to the block start (bs) subfield and shall not include a destination (d) subfield.

Note.— The ground station establishes a reservation for station B to respond with the re-broadcasted superframe block message.

Rebroadcast request superframe block reservation response procedures

On receipt of a superframe block reservation directed to itself, station B shall transmit a superframe block reservation in the directed slot. The station shall set the block repeat rate (br), block offset (bo) and block timeout (bt) subfields to the values contained in the received burst. The station shall set the block start (bs) so as to indicate the same first slot of the first block as was directed in the received superframe block reservation, calculated relative to the first slot of the transmission. The station shall set the re-broadcast offset (roff) subfield equal to the block start (bs) subfield and shall not include a destination subfield.

Second frame block reservation transmission procedures

Recommendation

A ground station infrastructure which needs to maintain a virtual link management channel (VLMC) should not set the size (sz) subfield to zero.

Note.— The second frame block reservation protocol is used to extend or reduce the VLMC.

Procedures for establishment of reserved blocks of slots

When a ground station wishes to modify the length of the reserved blocks of slots in each second, it shall broadcast a second frame block reservation, V67 times per M1 slots. The station shall set the block size (sz) subfield to the desired number of slots after the start of each UTC second as defined by parameter V66.

Response protocol specification

Response burst format

A reservation ID (rid) = 0 with extended reservation ID (erid) = 00000binary and reservation fields set in accordance with Table 1-49 shall indicate a response burst. In the case that the address type field (see Section 1.3.14.1) is equal to 7, bits 1 through 24 of the destination subfield (d) shall be absent and the information field shall extend up to the last one octet prior to the CRC. Otherwise, the information field shall extend up to the last four octets prior to the CRC and the destination subfield (d) shall be the 27-bit address of the destination station (for which the response is addressed). No reservation shall be made as a result of receiving a response burst.

Table 1-49. Response burst reservation bit encoding

| Description | Octet | Bit Number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| destination address (d) | n-5 | d24 | d23 | d22 | d21 | d20 | d19 | d18 | d17 |
|  | n-4 | d16 | d15 | d14 | d13 | d12 | d11 | d10 | d9 |
|  | n-3 | d8 | d7 | d6 | d5 | d4 | d3 | d2 | d1 |
| reservation ID | n-2 | 0 | 0 | 0 | 0 | 0 | d27 | d26 | d25 |

The VSS user shall provide the destination address.

Note 1.— In the typical application, the response will be broadcast; however, some applications might require a unicast response.

Note 2.— The response burst with the address type field set equal to 7 is intended as an alternative to the null reservation type defined in Section 1.3.9.

General request protocol specification

General request burst format

To request a peer station to transmit a particular burst, a station shall send the burst described in Table 1-50 to the desired destination station. VSS user-specific parameters shall be encoded starting in the octet following the most significant (high order) bit of the r-mi field. Unused bits (x) shall be filled with 0 on transmit and shall be ignored on receive.

The values of the subfields shall be computed as defined in Table 1-51.

Table 1-50. General request bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
|  | 5 | r-mi1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| requested message ID (r-mi) | 6 | x | r-min | . . . . . . | r-mi2 |
| VSS user specific parameter (prm) | 7 | prm18 | prm17 | prm16 | prm15 | prm14 | prm13 | prm12 | prm11 |
|  | 8 | prm28 | prm27 | prm26 | prm25 | prm24 | prm23 | prm22 | prm21 |
|  | 9 | prm38 | prm37 | prm36 | prm35 | prm34 | prm33 | prm32 | prm31 |

|  | . . . . . . . . |  | Denotes variable length field |
| --- | --- | --- | --- |

Table 1-51. General request field encoding

| Subfield | Range | Encoding | Notes |
| --- | --- | --- | --- |
| requested message ID (r-mi) | (See Section 1.3.2.3) |  |
| VSS user specific parameter (prm) |  |  | defined by the VSS user |

The requested message ID (r-mi) shall define the VSS user, in accordance with Table 1-6a, which is responsible for handling the request.

General request procedures

Requester action

For a VSS user to request that a peer VSS user transmit (either broadcast or unicast request response) certain information, the VSS user shall transmit a general request burst with the requested ID (r-mi) field set to the desired response. The unicast request reservation field shall be used if a single response is required from a single station. The directed request reservation field shall be used if multiple responses are required from a single station.

Responder action

The addressed responder(s) shall respond in the indicated slots with the requested bursts except for the conditions specified in Section 1.3.6.5.

Exceptional cases

If the requested function is not supported, the responder shall send a general failure (see Section 1.3.20) with the ok bit set to 0, the requested ID (r-mi) field set to the requested VSS user, the backoff delay (bd) set to FF hex, and the error type (err) set to 00 hex (if that ground station does not support the requested function but other ground stations in the same system could support it).

If the requested function is supported, but there has been no response in time for transmission in the reserved slot, then the responder shall transmit a general failure (see Section 1.3.20) with the ok bit set to 0, the requested ID and extended ID fields set to the requested VSS user, the backoff delay set to an estimate of when the data will be available, and the error type set to either 7E hex or FE hex. Ground stations shall use 7E hex to indicate that mobile stations might get a quicker response via a different ground station. A ground station not capable of responding because of network problems shall use the error type of either 03 hex if no response can be expected or 04 hex if a response can be expected but will be delayed.

General response protocol specification

General response burst format

A station shall transmit a general response burst (either a general failure or general confirm) as defined in Table 1-52 with the parameters defined in Table 1-53 in response to certain requests from another station as described below. The requested message ID (r-mi) shall indicate the identity of the peer VSS user to which a response is being generated. The general response burst shall include one of the following reservation fields: unicast request reservation, information transfer request or response. The destination subfield contained in the reservation field shall indicate which VSS user is being responded to.

Table 1-52. General response bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Confirm/failure flag (ok) | 5 | ok | 0 | 0 | 1 | 0 | 0 | 0 | 1 |
| Requested message ID (r-mi) | 6 | res | r-mik | . . . | r-mi1 |
| Reserved bit (res) | 7 | res | res | res | res | res | res | res | res |
| Backoff delay (bd) | 8 | bd8 | bd7 | bd6 | bd5 | bd4 | bd3 | bd2 | bd1 |
| error type (err) | 9 | err8 | err7 | err6 | err5 | err4 | err3 | err2 | err1 |
| VSS user specific Parameter (prm) | 10 | prm18 | prm17 | prm16 | prm15 | prm14 | prm13 | prm12 | prm11 |
|  | 11 | prm28 | prm27 | prm26 | prm25 | prm24 | prm23 | prm22 | prm21 |
|  | 12 | prm38 | prm37 | prm36 | prm35 | prm34 | prm33 | prm32 | prm31 |

|  | . . . . . . . . |  | Denotes variable length field |
| --- | --- | --- | --- |

Table 1-53. General response field encoding

| Subfield | Range | Encoding | Notes |
| --- | --- | --- | --- |
| confirm/failure flag (ok) |  | 1 = General confirm 0 = General failure |  |
| Requested message ID (r-mi) | (See Section 1.3.2.3) | can extend into octet 7 for long extended ids |
| reserved bit (res) | 0 | 0 | send 0, ignore on receive |
| backoff delay (bd) | 0 to 255 | integer seconds, FF hex = forever | in seconds, ignore on confirm |
| error type (err) | See Table 1-54 |  |
| VSS user specific parameter (prm) | Defined by the VSS user |  |

The requested message ID (r-mi) shall define the VSS user, in accordance with Table 1-6a, which is responsible for handling the response.

If the ok bit is set to 1 (i.e., a general confirm), and the response does not utilise the parameter field, the information field shall contain the requested message ID (r-mi) subfield only and the remaining parameters shall be omitted. If the ok bit is set to 1 and the parameter field is used, then the bd and err fields shall be included and set to 00 hex. If the ok bit is set to 0 (i.e., a general failure), then the remaining parameters shall define the reason why the request failed.

Error type (err) shall be encoded in accordance with Table 1-54; error types 00 hex to 7F hex shall apply to the responding station; error types 80 hex to FF hex shall apply to the responding system. A VSS user receiving a general failure with an error type less than 80 hex shall not transmit another request to that peer station for the duration of time designated by the backoff delay (bd) subfield (in seconds). A VSS user receiving a general failure with an error type greater than 7F hex shall not transmit another request to that peer system for the duration of time designated by the backoff delay (bd) subfield (in seconds).

Note.— That is, a mobile VSS user receiving a ground station-based error type from one ground station may immediately transmit the same request to another ground station of the same ground system.

Table 1-54. Error type definition

| Cause | Function | Parameter Encoding (prm bits 1 to 8) |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 00 hex | Unsupported local function. The parameters (defining the protocol options supported) will be filled in when defined. | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 01 hex | Out of local resources | Reserved |
| 02 hex | VSS user-specific local error | Defined by the VSS user |
| 03 hex | Terrestrial network not available | Reserved. Set to zero on transmit, ignore on receipt. |
| 04 hex | Terrestrial network congestion |  |
| 05-7D hex | Reserved |  |
| 7E hex | No response from VSS user |  |
| 7F hex | Other unspecified local reason. |  |
| 80 hex | Unsupported global function. The parameters (defining the protocol options supported) will be filled in when defined. | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 81 hex | Out of global resources | Reserved |
| 82 hex | VSS user-specific global error | Defined by the VSS user |
| 83 to FD hex | Reserved | Reserved. Set to zero on transmit, ignore on receipt. |
| FE hex | No response from VSS user |  |
| FF hex | Other unspecified system reason. |  |

General response procedures

If a reservation has been placed for a response or acknowledgement but the VSS sublayer has not received the response or acknowledgement from the VSS user in time for the scheduled reservation, the station shall send a general failure (see Section 1.3.20) with cause code 7E hex or FE hex.

If a response is received, the VSS shall inform the VSS user.

Retransmission procedures

After transmitting a burst containing a reservation for a peer station (i.e., unicast request reservation, directed request reservation, information transfer request reservation) and not receiving a response by the expected slot, a station shall either retransmit the request or inform the VSS user and LME if Q5num attempts have already been made or if more than Q5wait seconds have elapsed since the VSS user initiated the request.

Note.— If Q5num = 1, no re-transmission is attempted and hence parameters Q5max, Q5min, Q5mult, Q5exp are not used.

The re-transmitting station shall wait for Q5min + min( U(x), Q5max) seconds before attempting to retransmit the burst, where:

| U(x) | is a uniform random number generated between 0 and x; |
| --- | --- |
| x | = Q5mult * Q5expretrans / (1-u); |
| u | is a measurement of channel utilization with a range of value from 0 to 1, with 1 corresponding to a channel that is 100 percent occupied. Channel utilization is the number of slots occupied in the last minute (see 1.2.4.3); |
| retrans | is the number of times that a burst has been retransmitted. |

DLS SUBLAYER

The DLS shall support communications on a shared communications channel as described in this section.

Services

The DLS shall support bit-oriented simplex communications using a negotiated setup connection-orientated protocol (NSCOP) and a zero-overhead connection-orientated protocol (ZOCOP).

##### Note 1.- It is the intention that NSCOP is used for air/ground (A/G) communications and ZOCOP for air/air (A/A) communications.

##### Note 2.- Apart from the procedures for link setup and teardown, the NSCOP and ZOCOP protocols operate identically.

###### The DLS shall support broadcast and multicast connectionless communications.

The DLS shall provide the following services

- transmission of user data

- indication that user data has been sent

- reception of user data

- indication that the DLS link has been established

- indication that the DLS link has been broken

Stations supporting the communications functionality provided by the DLS shall simultaneously support at least 8 peer-to-peer links with other stations.

Stations not supporting the communications functionality provided by the DLS shall implement Section 1.4.2.2 and Section 1.4.4.7only.

Data transfer

User data packets and LME data shall be transferred in the information fields of INFO, UDATA, and CTRL data link protocol data units (DLPDUs) which are collectively known as DATA DLPDUs.  LME data shall be contained in CTRL and UCTRL frames only.  The link layer shall process the largest packet size, specified in Section 1.4.3.5 of this document, without fragmenting. Larger packets shall be fragmented according to the procedures of Section 1.4.4.3.2. Only one data link user packet shall be contained in a DATA DLPDU.

Note 1. – The Frame Mode SNDCF may concatenate multiple packets, but this is presented as a single user data packet to the DLS.

Note 2. – UDATA DLPDUs consist of UINFO DLPDUs for broadcast of user data packets and UCTRL DLPDUs for broadcast of LME data.

DATA DLPDU duplicate suppression and sequencing

On a point-to-point connection, the receiving DLS sub-layer shall ensure that duplicated DATA DLPDUs are discarded and all DATA DLPDUs which are part of a fragmented packet are delivered in the same order in which they appear in the packet.

Note.— A toggle bit is included in the DLS DLPDU format to facilitate duplicate suppression.

Error detection

The DLS sub-layer shall ensure that DLPDUs corrupted during transmission are detected and discarded.

Note.- 16-bit CRC is provided in the burst format to support this service – the MAC layer will reject corrupted packets.

Station identification

A receiving station shall accept unicast DLPDUs addressed to its current station address.

Note.— Unique source and destination addresses are included in the VDL Mode 4 DLS burst format to facilitate this service. DLPDUs addressed to the current station address are routed to the DLS by the VSS. However, non-unique addressing is possible – with the resultant communications risk minimized through the assurance that any link address is locally unique. The ATN requires a  unique address and hence non-unique addressing is not for use with the ATN.

Broadcast addressing

A VDL Mode 4 station shall accept broadcast DLPDUs and multicast DLPDUs to multicast addresses to which it is listening.

DLS Priority

The DLS shall accept an indication of priority of the DATA DLPDU as defined in Table 1-10.

DLS link control DLPDUs

For the purposes of link control, the DLS shall provide the following DLS DLPDU types:

- ACK DLPDUs, consisting of INFO_ACK and CTRL_ACK, for the purposes of acknolwedgement of DATA DLPDUs and DLS link control DLPDUs respectively

- RTS DLPDUs, consisting of CTRL_RTS, INFO_RTS and UDATA_RTS, for the purposes of making reservations for the transfer of DATA DLPDUs

- CTS DLPDUs, consisting of CTRL_CTS, INFO_CTS and UDATA_CTS, for the purposes of acknowledging RTS DLPDUs and providing slots for subsequent transmission of DATA DLPDUs

- Other DLS link control DLPDUs, consisting of FRMR, FRMR_ACK, DM/DISC and SZOM, for purposes of link initialisation, reset and maintenance.

DLS protocol specification

State Variables

The DLS shall maintain the following state variables for each data link between two peer stations.

| State Variable | Usage |
| --- | --- |
| Tt | Current value of T bit (0 or 1) for transmitted DLPDUs |
| Tr | Value of T bit (0 or 1) for last received DLPDU. |
| send array | an array storing user data packets and M-bit linked fragments queued for transmission (one per priority level) |
| receive array | an array storing received M-bit linked fragments queued for concatenation (one per priority level) |

Note.- If the link is reset for any reason, the DLS will discard any fragments associated with a partially sent packet

Station address encoding

Address type

The address type field is defined in Table 1-55.

Table 1-55. Address type field encoding

| Bit encoding | Description type | Bits 1 to 24 |
| --- | --- | --- |
| 27 | 26 | 25 |  |  |
| 0 | 0 | 0 | Mobile | Non-unique identity |
| 0 | 0 | 1 | Aircraft | 24-bit ICAO address |
| 0 | 1 | 0 | Ground vehicles | Nationally administered address space |
| 0 | 1 | 1 | Reserved | Future use |
| 1 | 0 | 0 | Ground station | ICAO-administered address space |
| 1 | 0 | 1 | Ground station | ICAO-delegated address space |
| 1 | 1 | 0 | Reserved | Future use |
| 1 | 1 | 1 | All stations broadcast | All stations |

Non-unique identity address

A mobile station using the non-unique identity address shall randomly choose a 24-bit address. The non-unique identity address of all zeros shall not be used. The non-unique identity address of all ones shall be used for broadcast applications only. All radio units located at a station shall use the same non-unique identity address.

If the station detects that another station is using the same random address, it shall stop transmitting on the current address; it shall then randomly select a new address that is not already present in its PECT. It shall use this new address in subsequent transmissions.

Note 1.— Processing of ambiguous data resulting from use of the non-unique address is an end system issue.

When using VDL Mode 4 for ATS applications, aircraft shall use the unique 24-bit ICAO address.

Note 2.—  In this case bits 25, 26, and 27 of the full 27-bit address will be 1, 0, and 0 respectively, as is defined in Table 1-55.

Note 3.—Mobiles using non-unique addresses cannot be unambiguously identified and this mode of use is itself inherently insecure. Higher level functions are required when there is a need to provide data origin authentication when non-unique addresses are used.

Note 4—Non-unique addressing violates the subnetwork requirements of the ICAO ATN and mobiles using this addressing mode cannot implement ATN applications.

Aircraft specific addresses

The aircraft specific address field shall be the 24-bit ICAO aircraft address.

ICAO-administered ground station specific addresses

The ICAO-administered ground station specific address shall consist of a variable-length country code prefix (using the same country code assignment defined in Annex 10, Volume III, Chapter 9, Appendix 1, Table 1) and a suffix. The appropriate authority shall assign the bits in the suffix.

ICAO-delegated ground station specific addresses

The ICAO-delegated ground station specific address shall be determined by the organization to which the address space is delegated.

Broadcast and multicast addresses

The broadcast and multicast addresses shall be used only as a destination address for UDATA DLPDUs.

Broadcast and multicast address encoding

The broadcast and multicast addresses shall be encoded as in Table 1-55a:

Table 1-55a.  Broadcast and multicast address encoding

| Broadcast destination | Type field | Specific address field |
| --- | --- | --- |
| All mobiles that use non-unique addresses | 000 | All ones |
| All mobiles | 001 | All ones |
| All ground stations of a particular provider | 100 or 101, as necessary | Most significant bits: Variable length provider code Remaining bits: All ones |
| All ground stations with ICAO-administered addresses | 100 | All ones |
| All ground stations | 101 | All ones |
| All stations | 111 | All ones |

DLS burst formats

DLS burst

A DLS station shall transmit the  DLS burst defined in Table 1-57 with the VSS user supplied QoS and reservation parameters.

Table 1-57. DLS burst format

| Description | Octet | Bit Number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| burst id, | 5 | res | 0 | 1 | 1 | 0 | 0 | 0 | 1 |
| DLS DLPDU | 6 | As per Section 1.4.2.3.2 |
|  | 7 |  |
|  | 8 |  |
|  | 9 |  |
|  | 10 |  |

All bits labelled res are reserved and shall be set to zero.

Note 1.— TheDLS DLPDU field may continue past octet 10.

The DLS burst shall consist of one or two DLS DLPDUs combined according to the procedures of Section 1.4.4.12.  A DATA DLPDU shall be the final field in the burst (and thus the burst can contain only one of these fields).

Note 2. — DLS burst will be able to combine up to two DLPDUs.  DATA and UDATA must come last because they are  variable length DLPDUs.

DLS DLPDU encoding

The DLS DLPDU field shall indicate the DLPDU type and contain, as appropriate, the priority subfield, the more bit, the toggle bit, the initialise bit and length subfield.

DATA DLPDUs shall consist of a single octet containing link control information and a variable length information field and shall be encoded as defined in Table 1-57a

Table 1-57a. DATA DLPDU encoding

| Octet | n | n+1 | ................... | n+m |
| --- | --- | --- | --- | --- |
| Bit | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |
| CTRL | M | T | re | c/r | IB | 0 | 0 | 0 | information field of length m octets |
| INFO | M | T | pr4 | pr3 | pr2 | pr1 | 1 | 0 | information field of length m octets |
| UCTRL | ucid4 | ucid3 | ucid2 | ucid1 | 0 | 1 | 0 | 0 | information field of length m octets |
| UINFO | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | information field of length m octets |
| Reserved | X | X | X | 1 | 1 | 1 | 0 | 0 | information field of length m octets |
| Reserved | X | X | 1 | 0 | 1 | 1 | 0 | 0 | information field of length m octets |
| Reserved | X | 1 | 0 | 0 | 1 | 1 | 0 | 0 | information field of length m octets |
| Reserved | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | information field of length m octets |

Note.- “X” means 0 or 1

The command/response (c/r), response expected (re) and UCTRL ID (ucid) subfields, are defined in Sections 1.5.3.3.2 and 1.5.2.6.

RTS DLPDUs consist of two octets containing link control information and shall be encoded as defined in Table 1-57b

Table 1-57b. RTS DLPDU encoding

| Octet | n | n + 1 |
| --- | --- | --- |
| Bit | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| CTRL_RTS | lg5 | T | IB | 0 | 1 | 0 | 0 | 1 | pr4 | pr3 | pr2 | pr1 | lg4 | lg3 | lg2 | lg1 |
| INFO_RTS | lg5 | T | 0 | 1 | 1 | 0 | 0 | 1 | pr4 | pr3 | pr2 | pr1 | lg4 | lg3 | lg2 | lg1 |
| UDATA_RTS | lg5 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | pr4 | pr3 | pr2 | pr1 | lg4 | lg3 | lg2 | lg1 |
| Reserved | lg5 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | pr4 | pr3 | pr2 | pr1 | lg4 | lg3 | lg2 | lg1 |

Note.- “X” means 0 or 1

ACK, CTS and other DLS link control DLPDUs shall consist of one octet containing link control information and shall be encoded as defined in Table 1-57c.

Table 1-57c. ACK, CTS and other DLS link control DLPDUs encoding

| Octet | n |
| --- | --- |
| Bit | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| UDATA_CTS | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 |
| INFO_ACK | 0 | T | 0 | 1 | 0 | 0 | 0 | 1 |
| INFO_CTS | 0 | T | 0 | 1 | 1 | 0 | 1 | 1 |
| CTRL_ACK | 0 | T | IB | 0 | 0 | 0 | 0 | 1 |
| CTRL_CTS | 0 | T | IB | 0 | 1 | 0 | 1 | 1 |
| Reserved | 0 | X | X | 1 | 0 | 1 | 0 | 1 |
| FRMR_ACK | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 |
| FRMR | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 |
| DM/DISC | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 |
| Reserved | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 |
| Reserved | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 |
| Reserved | 1 | X | 0 | 1 | 1 | 0 | 1 | 1 |
| Reserved | 1 | X | X | 0 | 0 | 0 | 0 | 1 |
| Reserved | X | X | X | 0 | 0 | 1 | 0 | 1 |
| Reserved | 1 | X | X | 0 | 1 | 0 | 1 | 1 |
| Reserved | X | X | 1 | 1 | 0 | 0 | 0 | 1 |
| Reserved | X | X | X | X | 0 | 0 | 1 | 1 |
| Reserved | 1 | 1 | X | 1 | 0 | 1 | 0 | 1 |
| Reserved | X | X | X | X | 0 | 1 | 1 | 1 |
| Reserved | X | 1 | 1 | 1 | 1 | 0 | 1 | 1 |
| SZOM | neg4 | neg3 | neg2 | neg1 | 1 | 1 | 0 | 1 |
| Reserved | X | X | X | X | 1 | 1 | 1 | 1 |

Note.- “X” means 0 or 1

All header bits labelled res are reserved and shall be set to zero.

Toggle bit

The T (Toggle) bit shall be alternately set to zero and one on each successful transmission..

At the start of a communication between two stations, or when the link is reset, the toggle bit shall be initiated according to the procedures of Section 1.4.4.3.3.1 for NSCOP communication and Section 1.4.4.3.3.2 for ZOCOP communication.

Note.—The T (Toggle) bit is sufficient to provide duplicate detection and rejection.

More bit

The M (More) bit shall be set to zero to indicate the end of a user data packet and to one to indicate that this fragment is not the last fragment in a multi-fragment user data packet and that further fragments will be transmitted.

Note.—The M (More) bit is set to 0 if a user data packet is sent as a single fragment or on the last fragment of a fragmented user data packet and to 1 otherwise. The receiver reassembles a fragmented user data packet on reception before passing it to the user.

Priority subfield

The priority subfield (p) shall indicate the priority level of the transmission as defined in Section 1.4.1.6.

Length subfield

The length subfield (lg) shall indicate the length of the DLS burst containing a DATA DLPDU in slots.

Note —  The calculation of length needs to take account of the size of the reservation protocol (default is response) and the effects of bit stuffing

Initialise bit

When the IB (initialise) bit is set the receiver shall initialise the Tt and Tr state variables and clear the send and receive arrays whilst processing the DLPDU.

Negotiation subfield

The negotiation (neg) subfield shall indicate the link management parameters to be used for ZOCOP link control as defined in Table 1-57d:

Table 1-57d. Interpretation of negotiation subfield

| Negotiation subfield | Parameters to use for ZOCOP link |
| --- | --- |
| 0 | VDL Mode 4 default parameters for version 0 |
| 1 – 15 | reserved for future use |

DLS system parameters

The parameters needed by the DLS sublayer shall be as listed in Table 1-58.

DLS parameters for NSCOP communications shall be determined  during the exchange of CTRL DLPDUs, if the default values are not to be used.

DLS parameters for ZOCOP communications shall be determined by the exchange of the negotiation subfield within the SZOM DLPDU.

Table 1-58. Data link service system parameters

| Symbol | Parameter name | Minimum | Maximum | Default | Increment |
| --- | --- | --- | --- | --- | --- |
| TD1 | ZOCOP link transmit reset timer | 5 s | 600 s | 60 s | 1 s |
| TD2 | ZOCOP link receive reset timer | 10 s | 1200 s | 90 s | 1 s |
| ND1 | Maximum number of octets in any user data packet | 143 octets | 2063 octets | 1511 octets | 1 octet |
| ND2 | Maximum length of DLS transmission | 2 octets | 2063 octets | 86 octets | 1 octet |
| ND3 | Maximum length of fragment | 1 slot | 32 slots | 5 slots | 1 slot |

Note.- The value of ND3 should be chosen such that the length of each DLS transmission containing the fragment is less than the maximum length of the DLS transmission defined by ND1.

Parameter TD1 (ZOCOP transmit reset timer)

For a mobile station maintaining a ZOCOP link with another mobile station, Timer TD1 shall be reset when a DLPDU is sent to the peer.  Timer TD1 shall not be cancelled.  If Timer TD1 expires, then Tt shall be set to 0 and the send channel array shall be cleared.

Parameter TD2 (ZOCOP receive reset timer)

For a mobile station maintaining a ZOCOP link with another mobile station, Timer TD2 shall be reset when a DLPDU is received from the peer.  Timer TD2 shall not be cancelled.  If Timer TD2 expires, the link shall be considered to be terminated.

Parameter ND1 (maximum number of octets of any user data packet)

The parameter ND1 shall define the maximum number of octets in any user data packet that a DLS shall accept from the data link user or from a peer station.  A station receiving a user data packet from a peer station greater in length than ND1 shall discard the packet and shall reset the link in accordance with the procedures of  Section 1.4.4.11. A station receiving a user data packet from a data link user greater in length than ND1 shall discard the packet.

Note.- The maximum size of a user data packet for broadcast is set by parameter ND3.

Parameter ND2 (maximum length of DLS transmission)

The parameter ND2 shall define the maximum size in octets of a transmission  including flags and reservation data that shall be sent using the short transmission procedures defined in Section 1.4.4.5

A burst occupying x slots shall contain up to 23 + (x-1)*31 octets of data if x is odd or 24 + (x-1)*31 octets of data if x is even including flags and reservation data.

Note.— A slot can contain 32 octets of data. The last slot in a sequence should only contain 24 octets to allow for propagation guard time. Allowing an average  octet/2 slots for bit stuffing, one slot could contain 23 octets of data including flags and reservation blocks. Two slots could contain 54 octets. Three slots could contain 86 octets, etc.

Parameter ND3 (maximum length of fragment)

The parameter ND3 shall define the maximum size in slots of a DLS burst.

##### Note.- To be used to control fragmentation and also applies to the maximum size of a burst containing a UDATA DLPDU

DLS procedures

Note.- Either station may send user data packets at any time and are considered peers with respect to management of the link

Broadcast

Only UDATA DLPDUs shall be broadcast.

Setting of re-transmission parameter

For all DLS bursts containing CTRL, INFO, CTRL_RTS and INFO_RTS DLPDUs, quality of service parameters Q5min, Q5max, Q5mult, Q5exp and Q5num shall be set as defined in Table 1-58a.

Note.— Retransmission of DLS DLPDUs is handled in the VSS.

Table 1-58a. Re-transmission parameters

| Symbol | Parameter name | Default |
| --- | --- | --- |
| Q5min | VSS retransmission parameters | Minimum | 1.0s |
| Q5max |  | Maximum | 15s |
| Q5mult |  | Multiplier | 1.45 |
| Q5exp |  | Exponent | 1.7 |
| Q5num |  | number of attempts | 4 |
| Q5wait |  | maximum time to wait for a reply | 20s |

Selection of user data packet for transmission

User data packet priority

A sending station shall maintain a prioritised queue of user data packets for transmission.

When determining which user data packet to transmit, the highest priority user data packet shall be sent first.

The DLS DLPDUs CTRL,and CTRL_RTS shall be classified as network management messages and given the highest priority.

The DLS DLPDUs INFO_RTS, and UDATA_RTS shall be assigned the same priority as the DATA DLPDU with which they are associated.

Note.- All other DLS DLPDU types will be sent in pre-reserved slots(FRMR and DM/DISC) or take the priority of the DATA packet to which they are combined (SZOM)  and hence priority is not an issue.

User data packet fragmentation

Determination of number of segments

If the length of the DLS burst containing a CTRL or INFO DLPDU is greater than ND3 slots, the sending station shall fragment the user data packet and format it according to the procedures of Section 1.4.4.3.2.3.  Otherwise the user data packet shall be sent as a single fragment formatted according to the procedures of Section 1.4.4.3.2.2.

The fragmentation of a user data packet shall take account of whether the station is combining a CTRL or INFO DLPDU with another DLS DLPDU in accordance with the procedures of Section 1.4.4.12.3.

Single fragment user data packet transmission

A single fragment user data packet shall be transferred as a CTRL or INFO DLPDU.

a)	The M bit shall be set to zero.

b)	For an INFO DLPDU, the pr bits shall indicate the priority of the DLPDU.

Multiple fragment user data packet transmission

A multiple fragment user data packet shall be transferred as a series of CTRL or INFO DLPDUs.

a)	The M bit shall be set to 1 for all fragments except the last fragment.

b)	The M bit shall be set to 0 for the last fragment.

c)	For INFO DLPDUs, the pr bits shall indicate the priority of the DLPDU.

Setting of T bit

T bit initialisation for NSCOP communication

When there is no current connection between a mobile station and a ground station and the LME of either station requests the transmission of a CTRL user data packet, the sending station shall fragment the user data packet in accordance with the procedures of 1.4.4.3.2 and send the fragments using either the short transmission procedures see Section 1.4.4.5) or the long transmission procedures (see Section 1.4.4.6). In the first fragment, it shall send either a CTRL DLPDU (short transmission procedures) or a CTRL_RTS (long transmission procedures) and set the IB bit to 1, the T bit to 0 and the state variable Tt to 0.

On receipt of a CTRL_RTS DLPDU (long transmission procedures), the receiving station shall send a CTRL_CTS with IB = 1 in accordance with the procedures of Section 1.4.4.6.3.

On receipt of a CTRL_CTS DLPDU with IB = 1 (long transmission procedures), the sending station shall send an INFO DLPDU with IB = 1 in accordance with the procedures of Section 1.4.4.6.4.

On receipt of a CTRL DLPDU with IB = 1, the receiving station shall set its own state variable Tr to 0, clear its receive arrays, and consider the link established for receipt of further DATA DLPDUs.  The receiving station shall set IB = 1 in the CTRL_ACK response to the CTRL DLPDU.

On receipt of the CTRL_ACK with T = 0 and IB = 1, produced in response to a CTRL DLPDU with IB = 1, the sending station shall set its state variable Tt to 1 and consider the link established for transmission of further DATA DLPDUs.

Note.- At this stage the state variables Tt for the sending station and Tr for the receiving station are initialised.  The receiving station must separately initialise the state variables for data transfer in the opposite direction.

On receipt of a CTRL_RTS, CTRL_CTS, CTRL or CTRL_ACK DLPDU in a DLS burst addressed to it for which IB = 1 and for which the T bit is equal to 1 a station shall reset the link in accordance with the procedures of Section 1.4.4.11.

T bit initialisation for ZOCOP communication

A mobile sending station (the “sending station”) wishing to send data to a mobile station (the “receiving station”) for which it does not currently have a link, shall send a DLS burst containing a Start Zero Overhead Mode (SZOM) DLPDU and the first INFO (short transmission procedures) or INFO_RTS (long transmission procedures) DLPDU to the receiving station using respectively the short transmission procedures (see Section 1.4.4.5) or the long transmission procedures (see Section 1.4.4.6).  It shall set the negotiation field to the highest value that is supported by the DLS in the SZOM DLPDU, the T bit to 0 in the INFO DLPDU and the state variable Tt to 0.

On receipt of an SZOM DLPDU combined with an INFO DLPDU (short transmission procedures) or INFO_RTS DLPDU (long transmission procedures), the receiving station shall set its own state variable Tr to 0, clear its receive arrays and consider the link established for receipt of further DLPDUs from the sending station.  The receiving station shall send a SZOM DLPDU combined with an INFO_ACK (short transmission procedures) or an INFO_CTS (long transmission procedures)  in the slot reserved for the transmission setting T=0.  In the SZOM DLPDU, the receiving station shall set the negotiation field to the highest value that is supported by the DLS.

On receipt of the INFO_ACK (short transmission procedures) or INFO_CTS (long transmission procedures) combined with an SZOM DLPDU, the sending station shall set its state variable Tt to 1 and consider the link established for transmission of further DATA DLPDUs.

For both sending and receiving stations, link parameters shall be selected which correspond to the lower value of the negotiation subfields contained in the SZOM DLPDU sent by the sending station and in the SZOM DLPDU sent by the receiving station.

Note.- At this stage the state variables Tt for the sending station and Tr for the receiving station are initialised.  The receiving station must separately initialise the state variables for data transfer in the opposite direction.

Transfer after initialisation

When the T bit has been initialised, the sending station shall set the T bit for transmitted DLPDUs to the value of Tt.

Selection of transmission procedures

After a packet has been selected for transmission according to the procedures of Section 1.4.4.3 the sending station shall calculate the total length in octets of the  DLS burst required to contain the DLPDU queued for transmission using the short transmission procedures defined in Section 1.4.4.6. The total length shall include the length of any reservation fields contained within the  DLS burst, together with any flags. The calculation of the length of the DLS burst shall take account of whether the station will combine a DATA DLPDU with another DLS DLPDU in accordance with the procedures of Section 1.4.4.12.3. If the total length is less than or equal to ND2, then the station shall use short transmission procedures (Section 1.4.4.6) to transmit the queued data. Otherwise, the station shall use the long transmission procedures (Section 1.4.4.7). The M bit shall be set to 0 for a short transmission.

Short transmission procedures

Transmission of DATA DLPDU

After the selection of a short transmission procedure, the sending station shall transmit a DLS burst containing the DATA DLPDU queued for transmission with QoS parameters as defined in Table 1-60 using the random access procedures. For CTRL and INFO DLPDUs, the T bit shall be set to Tt.

A burst containing a CTRL or INFO DLPDU shall contain a unicast request reservation field for the acknowledgement with the parameters in Table 1-60.

Note.— If the responder VSS sublayer has not received a response from the VSS user in the scheduled reservation it can send a general failure (see Section 1.3.20) with error type 7E hex or FE hex and a unicast request reservation (with itself as the transmitter) according to the procedures of Section 1.3.19.2.

Acknowledgement of DATA DLPDU

Valid link with sender

If a station receiving a CTRL or INFO DLPDU has a valid link to the sender it shall transmit a DLS burst containing an ACK DLPDU in the slot reserved by the unicast request reservation field contained in the data DLPDU transmission:

a)	A CTRL_ACK DLPDU shall be sent in response to a CTRL DLPDU and an INFO_ACK DLPDU shall be sent in response to an INFO DLPDU

b)	The T bit shall be set to the value of the T bit in the received DATA DLPDU.

Non-receipt of acknowledgement

If an acknowledgement to a CTRL or INFO DLPDU is not received from the receiving station, the sending station shall retransmit the DLS burst containing the CTRL or INFO DLPDU and a unicast request reservation field according to the procedures of Section 1.3.21.

Action on receipt of a UDATA DLPDU

A station receiving a UDATA DLPDU shall forward the contents of the information field to the DLS user and take no further action.

Table 1-60. Short transmission INFO DLPDU parameters

| Symbol | Parameter name | Default |
| --- | --- | --- |
| V32 | Minimum response delay | (54 msec) * M1 / 60 slots |
| V33 | Maximum response delay | (5 sec) * M1 / 60 slots |
| V34 | Source/destination control | 0 |
| V35 | Broadcast control | 0 |
| V36 | Length of reserved block | 1 slot |
| Q1 | Priority | Priority of INFO DLPDU |
| Q2a | Slot selection range constraint for level 1 | 150 NMI |
| Q2b | Slot selection range constraint for level 2 | 150 NMI |
| Q2c | Slot selection range constraint for level 3 | 0 NMI |
| Q2d | Slot selection range constraint for level 4 | 300 NMI |
| Q3 | Replace queued data | FALSE |
| Q4 | Number of available slots | 3 |

Long transmission procedures

Transmission of request to send

After the selection of a long transmission procedure, the sending station shall transmit a DLS burst containg an RTS DLPDU to the receiving station in the transmit queue with QoS parameters as defined in Table 1-61. When using the long transmission procedure:

- A station shall send a  CTRL_RTS, INFO_RTS or UDATA_RTS DLPDU if a CTRL, INFO or UDATA DLPDU respectively is to be transmitted.

b) The pr subfield shall indicate the priority of the DATA DLPDU to be transmitted (see Section   1.4.1.6)

- The length subfield shall indicate the length of the DLS burst required to contain the DATA DLPDU (see Section 1.4.2.3.6).

d) For CTRL_RTS and INFO_RTS DLPDUs, the T bit shall be set to Tt.

Each burst shall contain a unicast request reservation field with the parameters set as defined in Table 1-61.

Note1.- The ground may use the priority subfield to manage the link resource during congestion.

Note 2.- Transfer of broadcast data using the long transmission procedures involves directing the UDATA_RTS at a specific station, receiving a set of slots from that station via the UDATA_CTS and then broadcasting the UDATA in the reserved slots

No response to RTS

Note.- If a response is not received to the RTS DLPDU, the station retransmits the DLS burst containing the RTS DLPDU and the unicast request according to the procedures of Section  1.3.14.4.4

Table 1-61. Long transmission RTS DLPDU parameters

| Symbol | Parameter name | Default |
| --- | --- | --- |
| V32 | Minimum response delay | (54 msec) * M1 / 60 slots |
| V33 | Maximum response delay | (5 sec)* M1 / 60 slots |
| V34 | Source/destination control | 0 |
| V35 | Broadcast control | 0 |
| V36 | Length of reserved block | 1 slot |
| Q1 | Priority | Priority of RTS |
| Q2a | Slot selection range constraint for level 1 | 150 nmi |
| Q2b | Slot selection range constraint for level 2 | 150 nmi |
| Q2c | Slot selection range constraint for level 3 | 0 nmi |
| Q2d | Slot selection range constraint for level 4 | 300 nmi |
| Q3 | Replace queued data | FALSE |
| Q4 | Number of available slots | 3 |

Response to RTS

Response if a DATA DLPDU has not previously been received

If the responder has a valid link to the sender and the received DLPDU is an RTS_UDATA or if the T bit within the CTRL_RTS or INFO_RTS DLPDU is not equal to Tr, then the receiving station shall transmit a CTS DLPDU in a DLS burst in the slot reserved by the RTS DLPDU.

a)	A CTRL_CTS, INFO_CTS or UDATA_CTS DLPDU shall be sent in response to a CTRL_RTS, INFO_RTS or UDATA_RTS DLPDU respectively

b)	The T bit shall be set to T bit of the RTS DLPDU to which the CTS is a response

For CTRL_CTS and INFO_CTS DLPDUs, the burst shall contain an information transfer request reservation field and be transmitted with the parameters in Table 1-63, indicating the number of slots reserved for transfer of the DATA DLPDU.

For a UDATA_CTS DLPDU, the burst shall contain a unicast request reservation field and be transmitted with the parameters in Table 1-61, indicating the number of slots reserved for transfer of the DATA DLPDU.

Response if a DATA DLPDU has previously been received

If the responder has a valid link to the sender and if the T bit within the CTRL_RTS or INFO_RTS DLPDU is equal to Tr, then the receiving station shall transmit an ACK DLPDU in the slot reserved by the RTS.

a)	A CTRL_ACK or INFO_ACK DLPDU shall be sent in response to a CTRL_RTS or INFO_RTS DLPDU respectively

b)	The T bit shall be set to the value of the T bit in the received DATA DLPDU.

The DLS burst containing the ACK DLPDU shall contain a response reservation type except as determined by the procedures of Section 1.4.4.12.

Channel too busy

If the channel is too busy (either the receiving station cannot find a sufficiently large series of contiguous slots or the priority is too low for the channel utilization), then the receiving station shall transmit either a general confirm including a unicast reservation with V34 = 1 indicating when the responder will transmit an information transfer request in response to the RTS or a general failure (see Section 1.3.20) with error type = 01 hex.

Note .— If the responder sends a general failure (see Section 1.3.20) the sender can retransmit the RTS after the timeout defined by the back-off delay or in the slot reserved by the destination.

Table 1-62. General response to RTS parameters

| Symbol | Parameter name | Default |
| --- | --- | --- |
| Q1 | Priority | Priority of RTS |
| Q2a | Slot selection range constraint for level 1 | 150 nmi |
| Q2b | Slot selection range constraint for level 2 | 150 nmi |
| Q2c | Slot selection range constraint for level 3 | 0 nmi |
| Q2d | Slot selection range constraint for level 4 | 300 nmi |
| Q3 | Replace queued data | FALSE |
| Q4 | Number of available slots | 3 |

Table 1-63. CTS DLPDU parameters

| Symbol | Parameter name | Default |
| --- | --- | --- |
| V42 | Length of information transfer | Sufficient to included requested INFO DLPDUs |
| V43 | Minimum information transfer delay | (54 msec) * M1 / 60 slots |
| V44 | Maximum information transfer delay | (5 sec) * M1 / 60 slots |
| V45 | Minimum response delay | (54 msec) * M1 / 60 slots |
| V46 | Maximum response delay | (5sec) * M1 / 60 slots |
| Q1 | Priority | Priority of RTS |
| Q2a | Slot selection range constraint for level 1 | 150 nmi |
| Q2b | Slot selection range constraint for level 2 | 150 nmi |
| Q2c | Slot selection range constraint for level 3 | 0 nmi |
| Q2d | Slot selection range constraint for level 4 | 300 nmi |
| Q3 | Replace queued data | FALSE |
| Q4 | Number of available slots | 3 |

Response to CTS

Transmission of DATA DLPDU

On receipt of a CTRL_CTS or INFO_CTS DLPDU in a DLS burst addressed to it for which the T bit is equal to Tt and with an information transfer request reservation field shall transmit the requested DATA DLPDU in the allocated reservation with the T bit set to Tt.

On receipt of a CTRL_CTS or INFO_CTS DLPDU in a DLS burst addressed to it for which the T bit is not equal to Tt shall reset the link in accordance with the procedures of Section 1.4.4.11.

On receipt of a UDATA_CTS DLPDU in a DLS burst addressed to it with a unicast request reservation field shall transmit the requested UDATA DLPDU in the allocated reservation.

Response if no information to transmit

If the station has nothing to transmit (e.g., after a reset), it shall not transmit.

Acknowledging the data

DATA DLPDU received

A receiving station which transmitted a CTRL_CTS or INFO_CTS DLPDU in a DLS burst containing an information transfer request reservation field (and consequently has a reservation for an acknowledgement) and which has received the DATA DLPDU with the same setting of T bit as is contained in the CTS, shall transmit in the slot reserved for an acknowledgement an ACK DLPDU in a DLS burst.

a)	A CTRL_ACK or INFO_ACK DLPDU shall be sent in response to a CTRL or INFO DLPDU respectively;

b)	The T bit shall be set to the value of the T bit in the received DATA DLPDU.

The DLS burst containing the ACK DLPDU shall contain a response reservation type except as determined by the procedures of Sections 1.4.4.12.

Response if DATA DLPDU not received

A receiving station which transmitted a CTRL_CTS, INFO_CTS or UDATA_CTS DLPDU in a DLS burst containing an information transfer request reservation field (and consequently has a reservation for an acknowledgement) and which has not received the CTRL, INFO or UDATA DLPDU with the same setting of T bit as is contained in the CTS, shall transmit in the slot reserved for an acknowledgement an ACK DLPDU in a DLS burst.

a)	A CTRL_ACK or INFO_ACK DLPDU shall be sent in response to a CTRL or INFO DLPDU respectively

b)	The T bit shall be set to the inverse of the value of the T bit in the last transmitted CTS DLPDU.

Note.- The use of the T bit not equal to the last transmitted CTS indicates a “negative acknowledgement (NACK)”

The DLS burst containing the ACK DLPDU shall contain a response reservation type.

DLS not supported

If the responder to a CTRL, CTRL_RTS, INFO, INFO_RTS or SZOM DLPDU does not support the DLS, then it shall transmit a general failure (see Section 1.3.20) with an error type of 80 hex in the slot reserved by the unicast request reservation field contained in the data DLPDU transmission.

No link with sender

If the responder to a CTRL or CTRL_RTS DLPDU with IB not equal to 1 or an INFO or INFO_RTS DLPDU which is not combined with a SZOM DLPDU does not have a link with the sender, the responder shall send a DLS burst containing a DM/DISC DLPDU in the slot reserved by the unicast request reservation field contained in the data DLPDU transmission.

User data packet reception

Receipt and forwarding of received DATA DLPDUs

When a CTRL or INFO DLPDU is received without errors from another station, the value of the T bit shall be inspected and recorded.

If this is:

a)	a CTRL DLPDU with IB = 1 or an INFO DLPDU combined with a SZOM DLPDU, or

b)	the value of the T bit is not equal to Tr,

then the user data packet or user data packet fragment shall be accepted and Tr shall be set to the value of the T bit in the received INFO or CTRL DLPDU. Otherwise, the received user data packet or user data packet fragment shall be discarded as a duplicate.

When a UDATA DLPDU is received without errors from another station, it shall be passed to the service user as a single incoming user data packet. Otherwise it shall be discarded.

Concatenation of multiple fragment user data packets

If any preceding user data packet fragments have been received with, in the case of an INFO DLPDU, the same value of pr subfield and with the M bit set to one, then the user data part of the received DATA DLPDU shall be concatenated to the end of the user data packet fragments.

If the M bit is set to zero on the received DATA DLPDU, then the user data part of the received DATA DLPDU, including any user data packet fragments received earlier and with which it has been concatenated, shall be passed to the service user as a single incoming user data packet. Otherwise, the received user data shall be retained awaiting the arrival of the remaining parts of the multiple fragment user data packet.

Unacknowledged DLPDUs

UDATA, DM/DISC and all ACK DLPDUs shall be unacknowledged.

Receipt of ACK DLPDU

When an ACK DLPDU is received without errors from another station, the value of the T bit shall be inspected.

If T = Tt, then the DATA DLPDU shall be assumed successfully received and the value of Tt shall be set to the inverse of the current value of Tt.

If T is not equal to Tt or if the ACK DLPDU is not received, then the sending station shall re-send the DATA DLPDU using the short or long transmission procedures as determined by the procedures of Section 1.4.4.4.

When a DATA DLPDU has been successfully received, the highest priority fragment (either the next fragment of the current user data packet or the first fragment/complete DLPDU of the next user data packet) in the send queue, if any, shall be selected for transmission using the procedures of Section 1.4.4.3.

Note.- The selection of highest priority allows the station to pre-empt eg a lower priority transfer of M-bit linked fragments with a higher priority user data packet or set of fragments.

Link reset

The sending station shall reset the link by sending a FRMR DLPDU in a DLS burst placing a unicast reservation for the response, and shall discard all outstanding user data packets in the send and receive array.  If a FRMR_ACK is not received in the reserved slot, the FRMR shall be sent again using the re-transmission procedures.  Only when a FRMR_ACK has been received shall the station attempt to re-send data to the receiving station using the procedures of Section 1.4.4.3.3. If the sending station receives an INFO or RTS DLPDU from the peer whilst waiting for a FRMR_ACK, it shall send an FRMR in response.

On receipt of a FRMR DLPDU, the receiving station shall discard any outstanding fragments in the receive array and shall transmit a FRMR_ACK DLPDU in a DLS burst in the reserved slot.

Linking DLS DLPDU transmissions

Recommendation

A station with a queue of transmissions to send to a receiving station should link transmissions using the procedures set out in this section.

An implementation of the DLS shall be capable of providing a combined frame response even if the station does not initiate the use of combined frames.

Allowed DLPDU combinations

It shall be possible to combine the following DLPDUs:

- RTS/DATA

- ACK/CTS

- ACK/DATA

- ACK/RTS

- SZOM/other DLPDUs as described in Section 1.4.4.3.3.2

Recommendation: Combined RTS/DATA DLPDUs

When a receiving station has selected a user data packet for transmission using the procedures of Section 1.4.4.3 it should also select the next user data packet with the highest priority and place an RTS DLPDU in the DLS burst containing the DATA DLPDU for the first user data packet.  For CTRL_RTS and INFO_RTS DLPDUs, the T bit shall be set to the inverse of Tt.

Note- This recommendation also applies to the case where the short transmission procedures would normally be selected for transmission but for which there is an opportunity to combine it with the end of the previous long transmission procedure.

Combined ACK/CTS DLPDUs

On receipt of a RTS/DATA DLS burst, a station shall process the DATA DLPDU first according to the procedures of Section 1.4.4.6.5.1. If the station can find sufficient resources for a subsequent DATA DLPDU transfer, then the DLS burst containing the ACK DLPDU shall also contain a CTS DLPDU for the next DATA DLPDU transfer:

a)	A CTRL_CTS, INFO_CTS or UDATA_CTS DLPDU shall be sent in response to a CTRL_RTS, INFO_RTS or UDATA_RTS DLPDU respectively

b)	The T bit shall be set to the T bit of the RTS DLPDU to which the CTS is a response

In the case of CTRL_CTS and INFO_CTS DLPDUs, instead of the response reservation type required by the procedures of Section 1.4.4.6.5.1, the burst shall contain an information transfer request reservation field transmitted using the parameters defined in Table 1-63, indicating the number of slots reserved for transfer of the DATA DLPDU.

A receiving station which has data that would fit into a single slot DLS burst containing an ACK DLPDU to send back to the sending, shall include its own DATA DLPDU in this DLS. The burst shall contain a unicast request reservation field with the parameters in Table 1-61 for the acknowledgement of the DATA DLPDU.

Note.-  Hence a station may combine a transport acknowledgement with the ACK if this can be produced in time.

Combined ACK/RTS DLPDUs

If a receiving station has data to send back to the sending station which cannot fit into a single slot DLS burst containing an ACK DLPDU, then the station shall combine an RTS DLPDU for its own DATA DLPDU in the DLS burst containing the ACK DLPDU and use the long transmission procedures for the data transfer.

Recommendation – Combined ACK/RTS DLPDUs to different peers

If a station is sending an ACK DLPDU to one destination and has data to send to a different destination, then the station should include a unicast reservation field with sdf = 1 with the DLS burst containing the ACK and then transmit an RTS DLPDU to the new destination in the reserved slot.

Note.- This makes it possible for eg a ground station to link a series of transmissions to different destinations.

CTRL DLPDU

The CTRL DLPDU shall be used for the LME to establish and maintain links as defined in Section 1.5.

Procedures for air-air communication

Air-air communication services shall be supported by a zero-overhead connection oriented protocol (ZOCOP).

Air-air data exchange after link initialisation

When a ZOCOP link has been established, data shall be exchanged as determined by either the short or long transmission procedures as described in Sections 1.4.4.5 and 1.4.4.6.

Link maintainance

A station that has established a ZOCOP link with a peer, and which has not sent a packet to that peer for TD1 seconds, and that wishes to send a DATA packet to the peer, shall re-establish the link according to the procedures of Section 1.4.4.3.3.2.

A station shall regard the link as terminated if it has not transmitted to the same peer for TD1 seconds and if it has not received a transmission from the same peer for TD2 seconds.

A station shall regard the link as terminated if it receives a DM/DISC DLPDU from the peer station or an attempt to send a packet to the peer station fails because of a failure notified by the retransmission procedures of Section 1.3.21.

LINK MANAGEMENT ENTITY SUBLAYER

Services

The services of the LME shall be as follows:

a) link provision, and

b) link change notification.

Link provision

Each Ground System and each Mobile System supporting air/ground point to point communication services shall include the functionality of a VDL Management Entity (VME). A VME shall be responsible for the data link management policy of the System. In a Mobile System the VME shall be responsible for determining with which Ground System(s) the Mobile System maintains datalink communications, at any given time. In a Ground System, the VME shall be responsible for determining to which Mobile System(s) datalink communications are provided, through which Ground Station and, when the Ground System supports multiple frequency operations, which mobiles are assigned to which frequency.

A VME shall have a link management entity (LME) for each peer LME. Hence, a ground VME shall have an LME per mobile and a mobile VME shall have an LME per ground system. An LME shall establish a link between a local DLE and a remote DLE associated with its peer LME. A ground LME shall determine if a mobile station is associated with its peer mobile LME by comparing the station address; two mobile stations with identical station addresses are associated with the same LME. A mobile LME shall determine if a ground station is associated with its peer ground LME by bit-wise logical ANDing the DLS address with the station ground system mask provided by the peer ground LME; two ground stations with identical masked DLS addresses are associated with the same LME.

Note.— If a mobile receives a frame from a ground station, only one LME will process and react to that frame. Thus the qualifying phrase “from a ground station associated with its peer LME” will not be included and should be understood to be implied.

Each ground and mobile LME shall monitor all transmissions (both DLS and VSS) from its peer’s stations to maintain a reliable link between some ground station and the mobile while the mobile is in coverage of an acceptable ground station in the ground system.

Link change notifications

The VME shall notify the intermediate-system system management entity (IS-SME) of changes in link connectivity supplying information contained in the CTRL frames received.

Synchronization burst format

All VDL Mode 4 stations shall transmit synchronization bursts to support link management.

Fixed and variable data fields

The synchronization burst shall consist of two portions: a fixed data field containing information that is sent with each synchronization burst and a variable data field containing additional system management information that does not need to be included in each synchronization burst.

Note 1.— The variable data field can also include VSS user specific information.

Note 2.— The fixed data field contains 55 bits of data consisting of bits 2 through 8 of octet 5 and all of octets 6 through 11 inclusive (the fixed data field begins after the source address and message identification fields which consist of the first four octets and bit 1 of octet 5). The variable portion contains 54 bits of data consisting of octets 12 through 17 and bits 3 through 8 of octet 18.

Note 3.— Certain variable information fields have been assigned and are described in  Section 3.

Fixed data field format

Stations shall have fixed data fields as defined in Table 1-65.

Table 1-65. Synchronization burst format

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| TCP change flag (tc) baro/geo altitude (b/g) CPR Format even/odd (cprf) position uncertainty (nucp) | 5 | nucp4 | nucp3 | nucp2 | nucp1 | cprf | b/g | tc | 0 |
| latitude (lat) | 6 | lat8 | lat7 | lat6 | lat5 | lat4 | lat3 | lat2 | lat1 |
| base altitude (balt) | 7 | balt12 | balt11 | balt10 | balt9 | lat12 | lat11 | lat10 | lat9 |
|  | 8 | balt8 | balt7 | balt6 | balt5 | balt4 | balt3 | balt2 | balt1 |
| longitude (lon) | 9 | lon8 | lon7 | lon6 | lon5 | lon4 | lon3 | lon2 | lon1 |
| time figure of merit (tfom) | 10 | tfom2 | tfom1 | lon14 | lon13 | lon12 | lon11 | lon10 | lon9 |
| data age (da) information field ID (id) | 11 | da4 | da3 | da2 | da1 | id4 | id3 | id2 | id1 |
| ID extension 1 (id1) ID extension 2 (id2) | 12 | id14 | id13 | id12 | id11 | id24 | id23 | id22 | id21 |
| ID extension 3 (id3) | 13 | id34 | id33 | id32 | id31 | ink |  |  |  |
| information field (in) | 14 |  |  |  |  |  |  |  |  |
|  | 15 |  |  | . . . . . . . . |  |  |
|  | 16 |  |  |  |  |  |  |  |  |
|  | 17 | in14 | in13 | in12 | in11 | in10 | in9 | in8 | in7 |
|  | 18 | in6 | in5 | in4 | in3 | in2 | in1 |  |  |

|  | . . . . . . . . |  | Denotes variable length field |
| --- | --- | --- | --- |

Note.— Mobile and ground stations are identified by the address type field in the 27-bit code (see Section 1.4.2.1).

The subfields shall be computed as defined in Table 1-66.

Table 1-66. Synchronization burst field encoding(fixed data field)

| Subfield | Range | Encoding | Notes |
| --- | --- | --- | --- |
| TCP change flag (tc) | Boolean | (see Section 3.6) |  |
| time figure of merit (tfom) | 0 to 3 | 0 = primary certified 1 = primary/non-certified 2 = secondary 3 = tertiary | (see Section 1.2.3) |
| position navigation uncertainty category (nucp) | 0 to 9 | See Table 1-67 |  |
| latitude (lat) | -90 to + 90° | 12-bit low-resolution encoding according to the CPR encoding algorithm adapted for VDL Mode 4, as described in Section 4 | The 12-bit CPR encoding provides position to a resolution of approximately (140 m, within a segment (patch) of approximately 600 nmi |
| longitude (lon) | -180° to + 180° | 14-bit low-resolution encoding according to the CPR encoding algorithm adapted for VDL Mode 4, as described in Section 4 | The 14-bit CPR encoding provides position to a resolution of approximately (120 m, within a segment (patch) of approximately 600 nmi |
| CPR format even/odd | 0 to 1 | 0 = even 1 = odd The CPR flag shall apply to all CPR encoded sub-fields included in the synchronisation burst |  |
| base altitude (balt) | 0 to 4095 | Base altitude is reported as specified in Table 1-68 |  |
| baro/geo altitude (b/g) | 0 to 1 | 0 = barometric 1 = geometric | Indicates whether barometric or geometric base altitude is reported |
| data age (da) | 0 to 15 | See Table 1-69 |  |
| information field ID (id) | 0 to 15 | As defined by application standards. Some values for the information field ID are pre-reserved and defined in Section 3 | Provides the information field identity contained in the variable data field (see Section 1.5.2.3) |
| ID extension | 0 to 15 | See below | Provides a means of increasing the number of variable fields that can be accommodated |
| information field (in) | - | As defined by application standards | The information field contained in the variable data field (see Section 1.5.2.3) |

The TCP change flag (tc) shall be encoded as defined in Section 3.6 if the message ID (see Table 1-6a) indicates that the burst is a directed synchronisation burst.  Otherwise it shall be reserved for future definition and set equal to 1.

The information field ID (id) and ID extension (idn) subfields shall provide addresses for information fields (in) as follows:

1.	An information field ID (id) equal to F hex shall indicate that no information field is present.

2.	An information field ID (id) subfield equal to 0 hex to 9 hex or B hex to E hex shall indicate one of 14 information fields of length 54 bits.

3.	ID extension 1 (id1) subfield shall only be present if the information field ID (id) is equal to A hex. An ID extension 1 (id1) subfield equal to 0 hex to 9 hex or B hex to F hex shall indicate one of 15 information fields of length 50 bits.

4.	ID extension n (idn) subfield shall only be present if the ID extension n-1 (idn-1) subfield is equal to A hex. An ID extension n (idn) subfield equal to 0 hex to 9 hex or B hex to F hex shall indicate one of 15 information fields of length 54 – 4n bits.

The station shall encode its navigation uncertainty category of position (nucp) in accordance with Table 1-67.

Table 1-67. Encoding of position navigation uncertainty category (nucp)

| nucp | Required Navigation Performance (RNP) class | Horizontal Protection Limit (HPL) (0.9999999 integrity bound) (nmi) | Horizontal error (nmi unless otherwise stated) | Vertical error (ft) |
| --- | --- | --- | --- | --- |
|  |  |  | Horizontal and vertical errors are 95% numbers. |
| 0 | N/A | N/A | N/A | N/A |
| 1 | RNP-10 | <20 | <10 | reserved |
| 2 | RNP-5 | <10 | <5 | reserved |
| 3 | RNP-1 | <2 | <1 | reserved |
| 4 | RNP-0.5 | <1 | <0.5 | reserved |
| 5 | e.g., NPA, DME-DME | <0.5 | <0.25 | reserved |
| 6 | e.g., GPS-SPS | <0.2 | <0.1 | reserved |
| 7 | e.g., GNSS (no SA) | <0.1 | <0.05 | reserved |
| 8 | e.g., SBAS | reserved | <10m | <15m |
| 9 | e.g., GBAS | reserved | <3m | <4m |

The station shall encode base altitude in accordance with Table 1-68.

Table 1-68. Base altitude encoding

| Actual base altitude of transmitting station (feet) | Transmitted value of altitude | Decoded base altitude (feet) (geo = WGS84 height except as noted) |
| --- | --- | --- |
| Unknown | 0 | altitude unknown |
| altitude < -1 305 | 1 | less than -1 300 |
| -1 305 ( altitude < -1 295 | 2 | -1 300 |
| -1 295 ( altitude < -1 285 | 3 | -1 290 |
| ( | ( | ( |
| -15 ( altitude < -5 | 131 | -10 |
| -5 ( altitude < 5 | 132 | 0 |
| 5 ( altitude < 15 | 133 | 10 |
| ( | ( | ( |
| 7 995 ( altitude < 8 005 | 932 | 8 000 |
| 8 005 ( altitude < 8 015 | 933 | 8 010 |
| 8 015 ( altitude < 8 037.5 | 934 | 8 025 |
| 8 037.5 ( altitude < 8 062.5 | 935 | 8 050 |
| 8 062.5 ( altitude < 8 087.5 | 936 | 8 075 |
| ( | ( | ( |
| 71 912.5 ( altitude < 71 950 | 3 490 | 71 925 |
| 71 950 ( altitude < 72 050 | 3 491 | 72 000 |
| 72 050 ( altitude < 72 150 | 3 492 | 72 100 |
| 72 050 ( altitude < 72 250 | 3 493 | 72 200 |
| 72 250 ( altitude < 72 350 | 3 494 | 72 300 |
| 72 350 ( altitude < 72 450 | 3 495 | 72 400 |
| ( | ( | ( |
| 129 950 ( altitude < 130 050 | 4 072 | 130 000 |
| 130 050 ( altitude | 4 073 | more than or equal to 130 100 |
|  | 4 074 to 4 094 | reserved |
| station on ground | 4 095 | station at 0 AGL |

The data age (da) subfield shall be encoded based on the report latency which shall be the difference between the time of validity of the horizontal position data (latitude and longitude) and the time of transmission, in accordance with Table 1-69.

Table 1-69. Report latency encoding and decoding

| Report latency (msec) | Transmitted value of data age (da) | Decoded latency (msec) |
| --- | --- | --- |
| difference < 100 | 0 | 50 |
| 100 ( difference < 200 | 1 | 150 |
| 200 ( difference < 300 | 2 | 250 |
| ( | ( | ( |
| 900 ( difference < 1 000 | 9 | 950 |
| 1 000 ( difference < 1 200 | 10 | 1 100 |
| 1 200 ( difference < 1 500 | 11 | 1 350 |
| 1 500 ( difference < 2 000 | 12 | 1 750 |
| 2 000 ( difference < 3 000 | 13 | 2 500 |
| 3 000 ( difference < 4000 | 14 | 3 500 |
| 4 000 ( difference or unknown | 15 | unknown |

If the report latency is greater than 4 seconds, then nucp shall be set to 0.

Variable data field format

The variable data field shall be available to carry additional information as may be required by another VSS user or application. The content and format of the variable data field shall be identified by the information field ID (id). The format of the variable data field corresponding to a given id shall be as specified in the appropriate application standard.

Note.— Up to 15 different information fields can be addressed. Information fields 1 to 9 are given priority over other information fields (see Section 1.5.6.1.1). Further short information fields may be addressed with the use of the extension field ID of 10 (see Section 1.5.2.2).

Synchronization burst request

To request that a station transmit a synchronization burst with a specific information field, a station shall transmit a general request burst to the appropriate application process as defined in Section C.4.

CTRL frame

Link management data shall be contained within a CTRL frame encoded within the information field of a CTRL DLPDU (see Table 1-57a) as defined in Table 1-69a.

Table 1-69a.  CTRL DLPDU format

| Description | Octet | Bit Number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| CTRL DLPDU header | n | M | T | re | c/r | IB | 0 | 0 | 0 |
| CTRL parameter 1: Parameter ID | n+1 | id8 | id7 | id6 | id5 | id4 | id3 | id2 | id1 |
| Parameter length | n+2 | m8 | m7 | m6 | m5 | m4 | m3 | m2 | m1 |
| Parameter value | n+3 | q18 | q17 | q16 | q15 | q14 | q13 | q12 | q11 |
|  | to | to |
|  | n+2 + m | qm8 | qm7 | qm6 | qm5 | qm4 | qm3 | qm2 | qm1 |
|  |  | more CTRL parameters |

The settings of the M, IB and T bits are defined in Section 1.4.

The settings of the c/r and re bits shall be as defined in Section 1.5.3.3.2.

Broadcast link management frame

Broadcast link management data shall be contained within the information field of a UCTRL DLPDU (see Table 1-57a) as defined in Table 1-69b.

Table 1-69b.  UCTRL DLPDU format for broadcast of link management infromation

| Description | Octet | Bit Number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| UCTRL DLPDU header | n | ucid4 | ucid3 | ucid2 | ucid1 | 0 | 1 | 0 | 0 |
| CTRL parameter 1: Parameter ID | n+1 | id8 | id7 | id6 | id5 | id4 | id3 | id2 | id1 |
| Parameter length | n+2 | m8 | m7 | m6 | m5 | m4 | m3 | m2 | m1 |
| Parameter value | n+3 | q18 | q17 | q16 | q15 | q14 | q13 | q12 | q11 |
|  | to | to |
|  | n+2 + m | qm8 | qm7 | qm6 | qm5 | qm4 | qm3 | qm2 | qm1 |
|  |  | more CTRL parameters |

The setting of the UCTRL identity (ucid) subfield shall be follows:

- ucid = 0 indicates that the UCTRL DLPDU is a GSIF containing data defined in Table 1-97 and used according to the procedures of Section 1.5.7.3.

- ucid = 1 indicates that the UCTRL DLPDU is a GSIF containing a DOS parameter only as defined in Section 1.5.3.6.6

- ucid = 2 indicates that the UCTRL DLPDU is a GSIF containing a channel management parameter only as defined in Section 3.7.2

- ucid = 3 indicates that the UCTRL DLPDU contains a broadcast CTRL_CMD.  The values of c/r and ho shall be assumed to be equal to 0.

- ucid = 4 to 15 are currently unassigned and available for future definition.

Control (CTRL) parameter formats

Encoding

The user data field of CTRL and UCTRL frames may include the CTRL parameters described in this section.

Note 1.— The tables in this section are divided into three major columns that define the field name, the bit encoding and brief explanatory notes.

Note 2. – CTRL parameters are extracted from the DLS sublayer CTRL frames and sent to the LME.

VDL Mode 4 parameter identification

The parameter identifier field shall allow simple identification of the purpose of the parameter as defined in Table 1-71c.

Table 1-71c  VDL Mode 4 parameter identifier purpose

| Bit 8 | Bit 7 | Purpose |
| --- | --- | --- |
| 0 | 0 | General purpose information parameter |
| 0 | 1 | Ground-initiated modification parameter |
| 1 | 0 | Mobile-initiated information parameter |
| 1 | 1 | Ground-initiated information parameter |

General purpose information parameters

VDL Mode 4 shall use the CTRL parameters defined below to allow mobile and ground-based LMEs to transfer basic information to each other.

Parameter set identifier

The parameter set identifier shall be sent first in a group of non-VDL Mode 4 parameters and indicates to which set the parameters belong. It shall be encoded as per Table 1-72.

There shall be no VDL Mode 4 parameter set identifier. VDL Mode 4 parameters shall always be sent before any other parameter groups.

Parameter ID 00hex means change to different set, in which case the parameter value contains the identity of the new parameter set.  A parameter set identity starting with “X” (equals 58 hex) is proprietary and not defined in ICAO Technical Manuals.

Note.- Parameters defined in other standards may be included in the CTRL frame starting with the parameter set identifier applicable to the particular standard.

Parameter ID FFhex is reserved for upper layer data, in which case the parameter value contains upper layer data.

Table 1-72. Parameter set identifier encoding

| Parameter ID | id8 | id7 | id6 | id5 | id4 | id3 | id2 | id1 | Parameter set identifier |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |  |
| Parameter value | q8 | q7 | q6 | q5 | q4 | q3 | q2 | q1 |  |

Connection management parameter

The connection management parameter shall define the type of CTRL sent and the connection options negotiated for that particular link. It shall be used in CTRL frames sent during link establishment and ground-based initiated ground station handoff, and shall be encoded as per Tables 1-71e, 1-71f and 1-71g. An LME shall set the reserved bits to 0 on transmission, and shall ignore the value of the reserved bits on receipt.

Table 1-71e.  Connection management parameter

| Parameter ID | 0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 1 | Connection management |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 |  | n4 | n3 | n2 | n1 |  |
| Parameter value | 0 | 0 | 0 | 0 |  | 0 | 0 | r | h |  |
| Note.( The value in the parameter length field is variable to allow for the possibility of additional options. |

Table 1-71f.  Connection management parameter values

| Bit | Name | Encoding |
| --- | --- | --- |
| 1 | H | h = 0 | No link currently established. |
|  |  | h = 1 | Link currently established. |
| 2 | R | r = 0 | Link connection accepted. |
|  |  | r = 1 | Link connection refused. |
| 3-8 | Reserved | Set to 0 |  |

Table 1-71g.  Abbreviated CTRL names

| Name | c/r | re | h | r | Notes |
| --- | --- | --- | --- | --- | --- |
| GSIF | - | - | - | - | Ground Station Identification Frame – sent using format defined in Section 1.5.2.6 |
| CTRL_CMD_LCR | 0 | 0 | 0 | 1 | Link Connection Refused |
| CTRL_CMD_HO | 0 | 1 | 1 | 0 | If re=1, then Initiating Handoff. |
| CTRL_CMD_HO | 0 | 0 | 1 | 0 | If broadcast and re=0, then comanding a Broadcast Handoff. If unicast and re=0, then Requesting Handoff. |
| CTRL_RSP_LE | 1 | 1 | 0 | 0 |  |
| CTRL_RSP_LCR | 1 | 1 | 0 | 1 |  |
| CTRL_RSP_HO | 1 | 1 | 1 | 0 |  |

CTRL sequencing parameter

The CTRL sequencing parameter shall define the CTRL sequence number (sss) and a CTRL retransmission number (rrr). It shall be encoded as per Table 1-71i. An LME shall increment the sequence number for every new CTRL (setting the retransmission field to 0 on the first transmission) and shall increment the retransmission field after every retransmission. In a CTRL_RSP, the sequence number shall be set to the value of the CTRL_CMD sequence number generating the response (the retransmission field shall be ignored).

Table 1-71i.  CTRL sequencing parameter

| Parameter ID | 0 | 0 | 0 | 0 |  | 0 | 0 | 1 | 0 | CTRL sequencing |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | 0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 1 |  |
| Parameter value | r4 | r3 | r2 | r1 |  | 0 | s3 | s2 | s1 |  |

Protocol options parameter

The protocol options parameter shall define which protocol options are supported by the transmitting station.  It shall be encoded as per Tables 1-71ia and 1-71ib.  When both this parameter and the Connection Management parameter are included in a CTRL, the bit values for those options which are included in both parameters shall be determined by the Connection Management parameter.

Table 1-71ia.  Protocol options parameter

| Parameter ID | 0 | 0 | 0 | 0 |  | 0 | 0 | 1 | 1 | CTRL sequencing |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | 0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 1 |  |
| Parameter value | 0 | 0 | 0 | 0 |  | 0 | b | i | 0 |  |

Table 1-71ib.  Protocol options parameter values

| Bit | Name | Encoding |
| --- | --- | --- |
| 2 | I | i = 0 | Does not support initiated Handoff |
|  |  | i = 1 | Supports initiated Handoff |
| 3 | B | b = 0 | Broadcast link handoff not supported |
|  |  | b = 1 | Broadcast link handoff supported |
| 1, 4-8 | Reserved | Set to 0 |  |

LCR cause parameter

The LCR cause parameter shall define the reason why the link connection request was refused. The parameter, which may be repeated, shall consist of a rejection cause code (c bits), backoff delay time in seconds (d bits), and any additional data required by the various parameters. It shall be encoded as per Table 1-71j. Cause codes 00 hex to 7F hex shall apply to the responding station; cause codes 80 hex to FF hex shall apply to the responding system and shall be encoded as per Table 1-71k. At least one copy of this parameter shall be included whenever the “r” bit in the Connection Management parameter is set to 1; this parameter shall not be included if the “r” bit is set to 0. An LME receiving an LCR Cause parameter less than 80 hex shall not transmit another CTRL_CMD to that peer station for the duration of time designated in the LCR Cause parameter. An LME receiving an LCR Cause parameter greater than 7F hex shall not transmit another CTRL_CMD to that peer system for the duration of time designated in the LCR Cause parameter.

Note.— An mobile LME receiving a station-based cause code from one ground station may immediately transmit the same CTRL_CMD to another ground station of the same ground system.

Table 1-71j.  LCR cause parameter

| Parameter ID | 0 | 0 | 0 | 0 |  | 0 | 1 | 0 | 0 | LCR cause |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 |  | n4 | n3 | n2 | n1 |  |
| Parameter value | c8 | c7 | c6 | c5 |  | c4 | c3 | c2 | c1 | cause |
|  | d16 | d15 | d14 | d13 |  | d12 | d11 | d10 | d9 | delay |
|  | d8 | d7 | d6 | d5 |  | d4 | d3 | d2 | d1 |  |
|  | a8 | a7 | a6 | a5 |  | a4 | a3 | a2 | a1 | additional data |

Table 1-71k.  Cause code table

| Cause | Function | Additional data encoding |
| --- | --- | --- |
| 00h | Bad local parameter. The additional data block, which may be repeated, Contains the PI of a parameter which cannot be Satisfied by this ground station. This cause will not be Sent for an illegal Connection Management parameter. | g8 p8 | g7 p7 | g6 p6 | g5 p5 | g4 p4 | g3 p3 | g2 p2 | g1 p1 |
| 01h | Out of link layer resources. | undefined |
| 02h | Out of packet layer resources. |  |
| 03h | Terrestrial network not available. |  |
| 04h | Terrestrial network congestion. |  |
| 05h | Cannot support autotune. |  |
| 06h | Station cannot support initiating handoff. |  |
| 07-7Eh | Reserved |  |
| 7Fh | Other unspecified local reason. |  |
| 80h | Bad global parameter. The additional data block, which may be repeated, Contains the PI of a parameter which cannot be Satisfied by any ground station in the system. This cause Will not be sent for an illegal Connection Management Parameter. | identical to cause code 00 |
| 81h | Protocol Violation. The first octet of the additional data block contains: 1 - c/r bit (c bit) of the received CTRL; 2 - rebit of the received CTRL; 3 - Disconnected bit (d bit) shall be set to 1 if the LME has no links with the remote LME (the unexpected bit shall also be set to 1); 4 - Illegal bit (i bit) shall be set to 1 if the LME receives an illegal CTRL (i.e., not listed in Table 1-97 and described in Section 5.3.4); 5 - Unexpected bit (u bit) shall be set to 1 if the LME receives a legal CTRL which is not legal in the context in which it was received. The remaining octets contains the parameter value of the Connection Management parameter (m bits) if included in the illegal CTRL. After transmitting or receiving an LCR with this cause Code, an LME shall delete all of its links. | 0 m8 | 0 m7 | 0 m6 | u m5 | i m4 | d m3 | p m2 | c m1 |
| 82h | Ground system out of resources. |  |
| 83-FEh | Reserved |  |
| FFh | Other unspecified system reason. |  |

Mobile-initiated information parameters

A mobile LME shall use mobile-initiated information parameters to inform the ground station about the capabilities or desires of that mobile. Ground LMEs shall not send these parameters.

Modulation support parameter

This parameter defines a list of modulation schemes that are supported. This parameter shall be sent on link establishment. It shall be encoded as shown in Table 1-73 and 1-74.

Table 1-73. Modulation support list encoding

| Field | Bit Position | Notes |
| --- | --- | --- |
| Parameter ID | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Modulation support |
| Parameter length | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |  |
| Parameter value | res | res | res | res | m4 | m3 | m2 | m1 | Mode |

Table 1-74. Modulation encoding

| Encoding | Meaning |
| --- | --- |
| 0 to 1 | Reserved |
| 2 | VDL Mode 2 |
| 3 | VDL Mode 3 |
| 4 | VDL Mode 4 (GFSK modulation) |
| 5 to F | Reserved |

Acceptable alternate ground station parameter

The acceptable alternate ground station parameter shall define a list of ground stations in order of preference. This parameter shall be defined by a list of DLS addresses encoded as per Table 1-71l. These shall be used by the ground LME during handoffs as possible alternate ground stations, if the proposed ground station is not acceptable to the ground LME.

Table 1-71l.  Acceptable alternative ground station parameter

| Parameter ID | 1 | 0 | 0 | 0 |  | 0 | 0 | 0 | 1 | Alternate ground station |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 |  | n4 | n3 | n2 | n1 |  |
| Parameter value | 0 | 0 | 0 | 0 |  | 0 | g27 | g26 | g25 | DLS Address |
|  | g24 | g23 | g22 | g21 |  | g20 | g19 | g18 | g17 |  |
|  | g16 | g15 | g14 | g13 |  | g12 | g11 | g10 | g9 |  |
|  | g8 | g7 | g6 | g5 |  | g4 | g3 | g2 | g1 |  |

Destination airport parameter

The destination airport parameter parameter shall define the  destination airport identifier of the mobile. It shall be encoded as four 8-bit ISO IA5 characters as defined in Table 1-71m.

Table 1-71m.  Destination airport parameter

| Parameter ID | 1 | 0 | 0 | 0 |  | 0 | 0 | 1 | 0 | Destination airport |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 |  | n4 | n3 | n2 | n1 |  |
| Parameter value | a8 | a7 | a6 | a5 |  | a4 | a3 | a2 | a1 | (first character) |
|  | b8 | b7 | b6 | b5 |  | b4 | b3 | b2 | b1 |  |
|  | c8 | c7 | c6 | c5 |  | c4 | c3 | c2 | c1 |  |
|  | d8 | d7 | d6 | d5 |  | d4 | d3 | d2 | d1 | (fourth character) |

Ground-initiated modification parameters

A ground LME shall use the ground-initiated information parameters to change the value of various parameters in one or more mobiles. Mobile LMEs shall not send a CTRL with these parameters.

Data link service parameter

The data link service parameter parameter shall define the value of ND1, ND2, ND3, TD1, TD2 that a mobile shall use for priority levels Q1min to Q1max, and shall be encoded as per Table 1-75.

Table 1-75. Data link service parameter encoding

| Field | Bit position | Notes |
| --- | --- | --- |
| Parameter ID | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | Data link service parameter |
| Parameter length | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |  |
| Parameter value | Q1max4 | Q1max 3 | Q1max 2 | Q1max 1 | Q1min4 | Q1min 3 | Q1min 2 | Q1min 1 | minimum priority (Q1min), maximum priority (Q1max) |
|  | ND18 | ND17 | ND16 | ND15 | ND14 | ND13 | ND12 | ND11 | ND1 |
|  | ND28 | ND27 | ND26 | ND25 | ND24 | ND23 | ND22 | ND21 | ND2 |
|  | TD113 | ND111 | ND110 | ND19 | ND212 | ND211 | ND210 | ND29 |  |
|  | TD213 | ND37 | ND36 | ND35 | ND34 | ND33 | ND32 | ND31 | ND3 |
|  | TD18 | TD17 | TD16 | TD15 | TD14 | TD13 | TD12 | TD11 | TD1 |
|  | TD212 | TD211 | TD210 | TD29 | TD112 | TD111 | TD110 | TD19 |  |
|  | TD28 | TD27 | TD26 | TD25 | TD24 | TD23 | TD22 | TD21 | TD2 |

VSS sublayer parameter

This parameter defines the value of VS1, VS2, VS4 and VS5 that a mobile shall use, encoded as per Table 1-76.

Table 1-76. VSS sublayer parameter encoding

| Field | Bit position | Notes |
| --- | --- | --- |
| Parameter ID | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | VSS sublayer parameter |
| Parameter length | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |
| Parameter value | VS54 | VS53 | VS52 | VS51 | VS14 | VS13 | VS12 | VS11 | VS1, VS5 (dB) |
|  | 0 | 0 | VS26 | VS25 | VS24 | VS23 | VS22 | VS21 | VS2 (nmi) |
|  | 0 | VS47 | VS46 | VS45 | VS44 | VS43 | VS42 | VS41 | VS4 |

Quality of service parameter

This parameter defines the quality of service parameters that a mobile shall use for priority levels Q1min to Q1max, encoded as per Table 1-78.

Table 1-78. Quality of service parameter encoding

| Field | Bit position | Notes |
| --- | --- | --- |
| Parameter ID | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | Quality of service parameter |
| Parameter length | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |  |
| Parameter value | Q1max4 | Q1max 3 | Q1max 2 | Q1max 1 | Q1min4 | Q1min 3 | Q1min 2 | Q1min 1 |  |
|  | Q2a8 | Q2a7 | Q2a6 | Q2a5 | Q2a4 | Q2a3 | Q2a2 | Q2a1 | Q2a (nmi) |
|  | Q2b8 | Q2b7 | Q2b6 | Q2b5 | Q2b4 | Q2b3 | Q2b2 | Q2b1 | Q2b (nmi) |
|  | Q2c8 | Q2c7 | Q2c6 | Q2c5 | Q2c4 | Q2c3 | Q2c2 | Q2c1 | Q2c (nmi) |
|  | Q2d8 | Q2d7 | Q2d6 | Q2d5 | Q2d4 | Q2d3 | Q2d2 | Q2d1 | Q2d (nmi) |
|  | Q2d10 | Q2d9 | Q2c10 | Q2c9 | Q2b10 | Q2b 9 | Q2a10 | Q2a9 |  |
|  | 0 | 0 | 0 | Q45 | Q44 | Q43 | Q42 | Q41 | Q4 |

m2 filter parameters

Table 1-80 defines the values of parameters used for the m2 filter that a mobile shall use. M2inc is encoded as an 8-bit unsigned integer. M2limit is encoded as a 16-bit unsigned integer.

Table 1-80. m2 filter parameter encoding

| Field | Bit position | Notes |
| --- | --- | --- |
| Parameter ID | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | m2 filter parameters |
| Parameter length | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |
| M2inc parameter value | i8 | i7 | i6 | i5 | i4 | i3 | i2 | i1 | M2inc |
| M2limit parameter value | l16 | l15 | l14 | l13 | l12 | l11 | l10 | l9 | M2limit |
|  | l8 | l7 | l6 | l5 | l4 | l3 | l2 | l1 |  |

CG1 filter parameters

Table 1-81 defines the values of parameters used for the CG1 filter that a mobile shall use. CG1_plea is encoded as an 8-bit unsigned integer. CG1_range is encoded as an 8-bit unsigned integer. TG6 is encoded as an 8-bit unsigned integer. CG1_inc is encoded as an 8-bit unsigned integer. 1/CG1_decay is encoded as an 8-bit unsigned integer. CG_limit is encoded as a 16-bit unsigned integer.

Table 1-81. CG1 filter parameter encoding

| Field | Bit position | Notes |
| --- | --- | --- |
| Parameter ID | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | CG1 filter parameters |
| Parameter length | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 |  |
| CG1_plea parameter value | p8 | p7 | p6 | p5 | p4 | p3 | p2 | p1 | CG1_plea |
| CG1_range parameter value | r8 | r7 | r6 | r5 | r4 | r3 | r2 | r1 | CG1_range |
| TG6 parameter value | t8 | t7 | t6 | t5 | t4 | t3 | t2 | t1 | TG6 |
| CG1_limit parameter value | l16 | l15 | l14 | l13 | l12 | l11 | l10 | l9 | CG1_limit |
|  | l8 | l7 | l6 | l5 | l4 | l3 | l2 | l1 |  |
| CG1_inc parameter value | i8 | i7 | i6 | i5 | i4 | i3 | i2 | i1 | CG1_inc |
| 1/CG1_decay parameter value | d8 | d7 | d6 | d5 | d4 | d3 | d2 | d1 | 1/CG1_decay |

Autotune frequency parameter

This parameter defines the frequency and modulation scheme that a mobile LME shall use to reply to a ground station listed in the replacement ground station list parameter. This parameter shall be sent by a ground LME when an autotune is required. The parameter shall be encoded as a 16-bit field as per Table 1-82. The modulation subfield (m bits) shall be defined as per Table 1-74. The frequency subfield (f bits) shall be defined as per Table 1-30.

Table 1-82. Autotune parameter encoding

| Field | Bit position | Notes |
| --- | --- | --- |
| Parameter ID | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | Autotune frequency |
| Parameter length | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |  |
| Parameter value | m4 | m3 | m2 | m1 | f12 | f11 | f10 | f9 |  |
|  | f8 | f7 | f6 | f5 | f4 | f3 | f2 | f1 |  |

1.5.4.3.9		Maximum number of missed reservations parameter

This parameter defines the number of consecutive missed reservations that will be used to determine a station is unreachable. This parameter shall be sent by a ground LME, as required, to adjust the timeliness of the LEAVE event. The parameter shall be encoded as per Table 1-82a. The parameters (L1 and TL3) shall be defined as per Table 1-89.

Table 1-82a. L1 parameter encoding

| Field | Bit position | Notes |
| --- | --- | --- |
| Parameter ID | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | Autotune frequency |
| Parameter length | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |  |
| Parameter value | L18 | L17 | L16 | L15 | L14 | L13 | L12 | L11 | L1 counter |
|  | 0 | 0 | 0 | TL35 | TL34 | TL33 | TL32 | TL31 | TL3 timer |

Note: The range of the L1 counter is 1 to 255. The value of 0 (L1=0) is invalid.

Replacement ground station list parameter

The replacement ground station list parameter defines a list of ground stations in order of ground LME preference. This parameter shall be encoded as a list of DLS addresses in 32-bit fields as per Table 1-71n. These addresses shall be used by the mobile LME during handoffs as possible alternate ground stations if the proposed ground station is not acceptable to the LME.

Table 1-71n.  Replacement ground station list parameter encoding

| Parameter ID | 0 | 1 | 0 | 0 |  | 0 | 1 | 1 | 1 | Replacement ground station list parameter |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 |  | n4 | n3 | n2 | n1 |  |
| Parameter value | 0 | 0 | 0 | 0 |  | 0 | g27 | g26 | g25 |  |
|  | g24 | g23 | g22 | g21 |  | g20 | g19 | g18 | g17 |  |
|  | g16 | g15 | g14 | g13 |  | g12 | g11 | g10 | g9 |  |
|  | g8 | g7 | g6 | g5 |  | g4 | g3 | g2 | g1 |  |

Random access parameter

The random access parameter shall define p, VS3 and TM2 used within the random access protocol, and shall be encoded as per Table 1-71p

Note. p is encoded as hexadecimal 00 (= decimal 1/256) to hexadecimal FF (= decimal 256/256).

Table 1-71p.  Random access parameter encoding

| Parameter ID | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | Random access parameter encoding |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |  |
| Parameter value | p8 | p7 | p6 | p5 | p4 | p3 | p2 | p1 | p |
|  | VS38 | VS37 | VS36 | VS35 | VS34 | VS33 | VS32 | VS31 |  |
|  | VS316 | VS315 | VS314 | VS313 | VS312 | VS311 | VS310 | VS39 |  |
|  | TM28 | TM27 | TM26 | TM25 | TM24 | TM23 | TM22 | TM21 |  |

Re-transmission parameter

The re-transmission parameter shall define the value of Q5 that a mobile MAC shall use for priority levels Q1min to Q1max. It shall be encoded as per Table 1-71r.

Table 1-71r.  Re-transmission parameter encoding

| Parameter ID | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | Re-transmission parameter |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |  |
| Parameter value | Q1max4 | Q1max 3 | Q1max 2 | Q1max 1 | Q1min4 | Q1min 3 | Q1min 2 | Q1min 1 | minimum priority (Q1min), maximum priority (Q1max) |
|  | min8 | min7 | min6 | min5 | min4 | min3 | min2 | min1 | Q5min |
|  | 0 | min15 | min14 | min13 | min12 | min11 | min10 | min9 |  |
|  | max8 | max7 | max6 | max5 | max4 | max3 | max2 | max1 | Q5max |
|  | 0 | max15 | max14 | max13 | max12 | max11 | max10 | max9 |  |
|  | mult8 | mult7 | mult6 | mult5 | mult4 | mult3 | mult2 | mult1 | Q5mult |
|  | exp8 | exp7 | exp6 | exp5 | exp4 | exp3 | exp2 | exp1 | Q5exp |
|  | 0 | 0 | 0 | 0 | num4 | num3 | num2 | num1 | Q5num |
|  | 0 | wait7 | wait6 | wait5 | wait4 | wait3 | wait2 | wait1 | Q5wait |

Timer TL1parameter

The timer TL1 parameter shall define the value of Timer TL1 (in seconds) that the initiating and responding LMEs shall use. It shall be encoded as two 8-bit integers per Table 1-71s.

Table 1-71s.  Timer TL1 parameter encoding

| Parameter ID | 0 | 1 | 0 | 0 |  | 1 | 0 | 1 | 0 | Timer TL1 parameter |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | 0 | 0 | 0 | 0 |  | 0 | 0 | 1 | 0 |  |
| Parameter value | i8 | i7 | i6 | i5 |  | i4 | i3 | i2 | i1 | (initiating) |
|  | r8 | r7 | r6 | r5 |  | r4 | r3 | r2 | r1 | (responding) |

Ground station address filter parameter

This parameter defines the DLS address of the ground station from which links are handed-off. This parameter shall be sent in a CTRL_CMD and a receiving mobile LME shall process the CTRL_CMD only if it has a link to the identified ground station. The ground station address filter shall be encoded as defined in Table 1-71u.

Table 1-71u.  Ground station address filter parameter

| Parameter ID | 0 | 1 | 0 | 0 |  | 1 | 0 | 1 | 1 | Ground station address filter |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | 0 | 0 | 0 | 0 |  | 0 | 1 | 0 | 0 |  |
| Parameter value | 0 | 0 | 0 | 0 |  | 0 | g27 | g26 | g25 | DLS address |
|  | g24 | g23 | g22 | g21 |  | g20 | g19 | g18 | g17 |  |
|  | g16 | g15 | g14 | g13 |  | g12 | g11 | g10 | g9 |  |
|  | g8 | g7 | g6 | g5 |  | g4 | g3 | g2 | g1 |  |

Broadcast connection parameter

The broadcast connection parameter shall define a single mobile’s link attributes for a new link, ie: the station address whose link was successfully established on the new link. As per Table 1-71ua, the mobile id subfield (a bits) shall be the station address

Table 1-71ua.  Broadcast connection parameter encoding

| Parameter ID | 0 | 1 | 0 | 0 |  | 1 | 1 | 0 | 0 | Ground station address filter parameter |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 |  | n4 | n3 | n2 | n1 |  |
| Parameter value | 0 | 0 | 0 | 0 |  | 0 | a27 | a26 | a25 | mobile ID |
|  | a24 | a23 | a22 | a21 |  | a20 | a19 | a18 | a17 |  |
|  | a16 | a15 | a14 | a13 |  | a12 | a11 | a10 | a9 |  |
|  | a8 | a7 | a6 | a5 |  | a4 | a3 | a2 | a1 |  |

Ground-initiated information parameters

A ground LME shall use ground initiated information parameters to inform one or more mobile LMEs about that ground-based system’s capabilities. Mobile LMEs shall not send these parameters.

Airport coverage indication parameter

The airport coverage indication parameter shall define a list of four-character airport identifiers of airports for which the ground station can support communication with a mobile on the ground. Each four-character identifier shall be encoded as four 8-bit ISO IA5 characters as per Table 1-71v.

Table 1-71v.  Airport coverage indication parameter encoding

| Parameter ID | 1 | 1 | 0 | 0 |  | 0 | 0 | 0 | 0 | Airport coverage indication parameter |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 |  | n4 | n3 | n2 | n1 |  |
| Parameter value | a8 | a7 | a6 | a5 |  | a4 | a3 | a2 | a1 | (first character) |
|  | b8 | b7 | b6 | b5 |  | b4 | b3 | b2 | b1 |  |
|  | c8 | c7 | c6 | c5 |  | c4 | c3 | c2 | c1 |  |
|  | d8 | d7 | d6 | d5 |  | d4 | d3 | d2 | d1 | (fourth character) |

Nearest airport parameter

The nearest airport parameter shall define the four-character airport ID of the airport nearest the ground station. It shall be encoded as four 8-bit ISO IA5 characters as per Table 1-71w. The nearest airport parameter shall not be included in a CTRL if the Airport Coverage Indication is included.

Table 1-71w.  Nearest airport parameter encoding

| Parameter ID | 1 | 1 | 0 | 0 |  | 0 | 0 | 0 | 1 | Nearest airport parameter |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | 0 | 0 | 0 | 0 |  | 0 | 1 | 0 | 0 |  |
| Parameter value | a8 | a7 | a6 | a5 |  | a4 | a3 | a2 | a1 | (first character) |
|  | b8 | b7 | b6 | b5 |  | b4 | b3 | b2 | b1 |  |
|  | c8 | c7 | c6 | c5 |  | c4 | c3 | c2 | c1 |  |
|  | d8 | d7 | d6 | d5 |  | d4 | d3 | d2 | d1 | (fourth character) |

ATN router NETs parameter

The ATN router NETs parameter shall define a list of ATN air-ground routers identified by the “administration identifier” (ADM) and “administration region selector” (ARS) subfields of their network entity titles (NETs). It shall be encoded as per Table 1-71x.

Table 1-71x.  ATN router NETs parameter encoding

| Parameter ID | 1 | 1 | 0 | 0 |  | 0 | 0 | 1 | 0 | ATN router NETs parameter |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 |  | n4 | n3 | n2 | n1 |  |
| Parameter value | a24 | a23 | a22 | a21 |  | a20 | a19 | a18 | a17 | ADM subfield |
|  | a16 | a15 | a14 | a13 |  | a12 | a11 | a10 | a9 |  |
|  | a8 | a7 | a6 | a5 |  | a4 | a3 | a2 | a1 |  |
|  | r24 | r23 | r22 | r21 |  | r20 | r19 | r18 | r17 | ARS subfield |
|  | r16 | r15 | r14 | r13 |  | r12 | r11 | r10 | r9 |  |
|  | r8 | r7 | r6 | r5 |  | r4 | r3 | r2 | r1 |  |

Ground-based system mask parameter

The ground-based system mask parameter shall define the ground-based system mask. It shall be encoded as a 27-bit mask in a 32-bit field as per Table 1-71y.

Table 1-71y.  Ground-based system mask parameter encoding

| Parameter ID | 1 | 1 | 0 | 0 |  | 0 | 0 | 1 | 1 | Ground-based system mask parameter |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | 0 | 0 | 0 | 0 |  | 0 | 1 | 0 | 0 |  |
| Parameter value | 0 | 0 | 0 | 0 |  | 0 | g27 | g26 | g25 |  |
|  | g24 | g23 | g22 | g21 |  | g20 | g19 | g18 | g17 |  |
|  | g16 | g15 | g14 | g13 |  | g12 | g11 | g10 | g9 |  |
|  | g8 | g7 | g6 | g5 |  | g4 | g3 | g2 | g1 |  |

Frequency support list

This parameter, encoded per Table 1-83, shall provide the mode, frequency, ground station address information and the relative location of the ground station listed. The location shall be encoded as an offset relative to the position of the source station: easterly offset (eo) (west is negative)and northerly offset (no) (south is negative) shall each be 8 bit parameters with a resolution of 4 nmi encoded using two’s complement math. The mode shall be encoded per Table 1-74 and the frequency shall be encoded per Table 1-30. The usage of this parameter is defined in Section 1.5.7.1.2.

Table 1-83. Frequency support list encoding

| Field | Bit position | Notes |
| --- | --- | --- |
| Parameter ID | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | frequency support list |
| Parameter length | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |  |
| Parameter value | m4 | m3 | m2 | m1 | f12 | f11 | f10 | f9 | mode/frequency |
|  | f8 | f7 | f6 | f5 | f4 | f3 | f2 | f1 |  |
|  | 0 | 0 | 0 | 0 | 0 | g27 | g26 | g25 | ground station identification |
|  | g24 | g23 | g22 | g21 | g20 | g19 | g18 | g17 |  |
|  | g16 | g15 | g14 | g13 | g12 | g11 | g10 | g9 |  |
|  | g8 | g7 | g6 | g5 | g4 | g3 | g2 | g1 |  |
|  | eo8 | eo7 | eo6 | eo5 | eo4 | eo3 | eo2 | eo1 | easterly offset |
|  | no8 | no7 | no6 | no5 | no4 | no3 | no2 | no1 | northerly offset |

Directory of service (DOS) parameter

The directory of service parameter shall be encoded as defined in Table 1-84.

Table 1-84. Directory of service message encoding

| Field | Bit position | Notes |
| --- | --- | --- |
|  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |
| parameter ID | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | DOS parameter |
| Parameter length | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |  |
| parameter value | gsc | ai3 | ai2 | ai1 | ent4 | ent3 | ent2 | ent1 | entry number (ent), current channel subfield additional service info (ai); GSC flag (gsc) |
|  | si8 | si7 | si6 | si5 | si4 | si3 | si2 | si1 | service information (si) |
|  | res | res | res | res | anum4 | anum3 | anum2 | anum1 | application number (anum) res field absent if anum field is absent. |
|  | a18 | a17 | a16 | a15 | a14 | a13 | a12 | a11 | application 1 (a1) |
|  |  |  |  |  | to |  |  |  |  |
|  | ak8 | ak7 | ak6 | ak5 | ak4 | ak3 | ak2 | ak1 | application k (ak) |
|  | gsc | ai3 | ai2 | ai1 | f12 | f11 | f10 | f9 | channel subfield: additional service info (ai); GSC flag (gsc) |
|  | f8 | f7 | f6 | f5 | f4 | f3 | f2 | f1 | frequency (f) |
|  | si8 | si7 | si6 | si5 | si4 | si3 | si2 | si1 | service information (si) |
|  | res | res | res | res | anum4 | anum3 | anum2 | anum1 | application number (anum) |
|  | a18 | a17 | a16 | a15 | a14 | a13 | a12 | a11 | application 1 (a1) |
|  |  |  |  |  | to |  |  |  |  |
|  | ak8 | ak7 | ak6 | ak5 | ak4 | ak3 | ak2 | ak1 | application k (ak) |
|  | sit6 | sit5 | sit4 | sit3 | sit2 | sit1 | x | x | service information type (sit) |

Note.— Bits denoted “x” may be used within the reservation field.

If the DOS parameter is included within a GSIF DLPDU with the ucid subfield set to 1, then the DOS parameter ID shall be omitted and no other parameter shall be included in the GSIF.

Note.- this makes it possible to provide a single slot transmission of basic DOS information

The current channel subfield shall always be present. One, two or more other channel subfields (channel 1, channel 2, etc) shall be added as required in a continuous bit sequence. The contents of the channel subfields shall be determined by the ai subfield as defined in Table 1-85. The service information type (sit) subfield shall follow the last channel subfield.

The subfields within each channel subfield shall be computed as defined in Table 1-85.

Table 1-85. Directory of service message subfield encoding

| Subfield | Range | Encoding | Notes |
| --- | --- | --- | --- |
| entry number (ent) | 0 – 15 | ent = entry number of Directory of Services message | up to 16 different DOS parameters can be accommodated associated with each ground station transmitting DOS parameters. |
| frequency (f) |  | See Table 1-30 Absent in current channel subfield | indicates the channel on which the DOS service is provided |
| GSC flag (gsc) | 0 – 1 | set to 1 if channel is a GSC |  |
| additional service information (ai) | 0 – 7 | bit 1: set to 1 if si field included bit 2: set to 1 if anum field present. bit 3: set to 1 if application (a) subfield(s) present |  |
| service information type (sit) | 0 – 63 | Defines services indicated by each bit in the service information field. As defined by application standards |  |
| service information (si) | Contains 8 single bit flags | Bits indicate the services provided on the indicated channel. bit set if service is available Meaning of bits defined by application standards. field absent if ai bit 0 = 0 |  |
| application number (anum) | 0 – 15 | Indicates the number of application fields present. field absent if ai bit 1 = 0 |  |
| application (a) | 0 – 255 | Identifies a single service defined by application standards field absent if ai bit 2 = 0 if ai bit 1 = 0 and ai bit 2 ( 0, only one application subfield shall be present |  |

Each DOS parameter shall override any previous DOS parameter from the same ground station with the same entry number (ent).

The upper bit of the application field shall be used as an extension field, so that a 0 indicates a one byte field and a 1 indicates that the ID continues in the next byte.

Application fields shall be allocated as defined in Table 1-86.

Table 1-86. Allocation of application fields

| Encoding (decimal equivalent) | Allocation |
| --- | --- |
| 0 - 31 | reserved for future allocation by ICAO |
| 32 - 63 | reserved for private allocation by service provider |
| 64 –127 | reserved for future allocation by ICAO delegated authority |
| 128 – 255 | reserved for future use (extension of application field) |

Service information type (sit) fields shall be allocated as defined in Table 1-87.

Table 1-87. Allocation of service information type fields

| Encoding (decimal equivalent) | Allocation |
| --- | --- |
| 0 – 31 | reserved for future allocation by ICAO |
| 32 – 47 | reserved for private allocation by service provider |
| 48 –63 | reserved for future allocation by ICAO delegated authority |

Channel management parameter

The channel management parameter shall have a parameter ID equal to C6h and be encoded as defined in Section 3.7.2.

LME timers and parameters

The LME service shall implement the system parameters defined in Table 1-88 and detailed in Sections 1.5.4.1 to 1.5.4.3.

Table 1-88. Management entity system parameters

| Symbol | Parameter name | Minimum | Maximum | Default | Increment |
| --- | --- | --- | --- | --- | --- |
| L1 | Maximum number of missed reservations | 1 | 255 | 3 | 1 |
| TL1 | Maximum link overlap time initiating responding | 0 s 0 s | 255 s 255 s | 20 s 60 s | 1 s 1 s |
| TL2 | Link initilization time | 5 s | 25 s | 6 s | 1 ms |
| TL3 | Inter-miss timer | 0 | 31 s | 5s | 1 s |

Counter L1 (maximum number of missed reservations) and Timer TL3 (inter-miss timer)

Parameter L1 shall be the maximum number of missed reservations before a station assumes that a peer station is unreachable. Counter L1 shall be set to zero when a transmission is received from a peer station. Counter L1 shall be incremented when no transmission is received from a peer station for which there was a prior reservation if L1 has not been incremented in the TL3seconds, except that a station shall not increment L1 when the prior reservation was made by a station other than the peer station. When counter L1 exceeds the maximum number of missed reservations (the value of parameter L1), the peer station shall be marked as unreachable in the peer entity contact table (PECT) (see Section 1.5.6.2), and links to the peer station shall be cancelled. There shall be one Counter L1 per peer station. Stations marked as unreachable shall be retained in the PECT for a period of time not less than 60 minutes.

Note 1.— The reason that L1 is not incremented when no response is heard in a slot that another station reserved for its peer is the possibility that the reservation itself was lost and thus no reliable inference can be made on the reachability of the peer station.

Note 2.— PECT entries are retained for a period of time in order to stabilize acquisition and track re-initialization performance for stations at the limits of coverage, and also to support potential search and rescue applications that may be developed in the future. Reservations for unreachable stations are retained in the reservation table and allowed to expire normally. These reservations represent real transmissions that may be expected to occur at the indicated times.

Note 3.— The timeliness of the generation of leave events depends on the value of the L1 counter and the number of reservations known to have been made by a station within a time interval. If the L1 counter is set to a low value then a leave event may be generated when a string of messages closely spaced in time is lost due to aircraft banking, antenna shadowing effects and interference. A ground station can readjust the L1 counter with the CTRL parameter defined in section 1.5.4.3.9 in order to minimise the likelihood of a leave event false alarm.

Timer TL1 (maximum link overlap time)

Timer TL1 shall be set to the maximum time that initiating and responding LMEs shall maintain the old link during handoffs. The LME initiating the handoff shall start its Timer TL1 when it receives an CTRL_RSP_HO. The LME responding to the handoff shall start its Timer TL1 when it transmits its CTRL_RSP_HO. The initiating LME shall never restart its Timer TL1; the responding LME shall restart its Timer TL1 if it retransmits a CTRL_RSP_HO. Timer TL1 shall be cancelled if either the old or new link is prematurely disconnected. After TL1 expires, each LME shall silently disconnect its half of the old link.

Note.— There is one Timer TL1 per LME.

Parameters TL2 (link initialization time)

The parameter TL2 shall control the retransmission of CTRL frames for which an expected response has not been received.

After transmitting a CTRL frame for which a response is expected and not receiving a response by TL2, the LME  it shall attempt to handoff to another ground station in accordance with the procedures of Section 1.5.7 .

LME procedures

Synchronization burst procedures

All stations shall transmit the appropriate synchronization burst defined in Section 1.5.2 depending on whether it is a mobile station or a ground station with the QoS and either the periodic broadcast or incremental broadcast parameters defined in Table 1-90. The values of the subfields shall be the latest available data that can be obtained by the station at the start of the slot immediately preceding the first slot of the intended transmission. Where time is used to calculate fields in the transmission, it shall be the time associated with the latitude and longitude data contained in the transmission.

A station transmitting a synchronization burst in a slot assigned by another station shall set the a/d bit to 1; otherwise, the station shall set the a/d bit to 0.

Table 1-90. Synchronization burst parameters

| Symbol | Parameter name | Default |
| --- | --- | --- |
| TV11min | Reservation | minimum | 4 |
| TV11max | Hold timer | maximum | 8 |
| V11 | Nominal periodic rate | 6 |
| V12 | Periodic dither range | 0.1 |
| V21 | Nominal rate | 100 |
| V22 | Max Dither range | 31 |
| Q1 | Priority | As per information field |
| Q2a | Slot selection range constraint for level 1 | 150nmi |
| Q2b | Slot selection range constraint for level 2 | 150nmi |
| Q2c | Slot selection range constraint for level 3 | 0nmi |
| Q2d | Slot selection range constraint for level 4 | 300nmi |
| Q3 | Replace queued data | TRUE |
| Q4 | Number of available slots | 3 |

Transmission of synchronization bursts supporting applications

A station shall transmit synchronization bursts in accordance with a request from a peer station as described in 1.5.2.4, at the specified rate, and containing the information field corresponding to the requested information field ID (r-id).

The station shall transmit additional synchronization bursts required to meet the demands of any application. In the event that an application request requiring the transmission of synchronization bursts is delivered by means of a directed request, the required bursts shall be transmitted in the slots reserved by the directed request protocol.

Note.— The interaction between the LME and the application of specific requirements for transmission of synchronization bursts is a local issue.

Mobile stations

Whenever mobile stations are not directed to transmit synchronization bursts on any frequency, they shall transmit mobile synchronization bursts on all GSCs which they can receive at least once per M1 slots. When transmitting autonomously on the GSCs, mobile stations shall use the standard parameters defined in Table 1-66.

Note.— Upon termination of all directed synchronization burst transmissions on a channel(s) other than the GSCs, mobile stations may employ the network entry procedures as described in Section 1.5.6.3 to quickly enter the GSC network(s).

Ground stations

Recommendation

A set of ground stations should ensure that sufficient synchronisation bursts are available to support the derivation of secondary timing.

Note.— To optimize the secondary navigation calculations, the transmissions from the various ground stations should all be in contiguous slots so that aircraft movement does not add additional error.

Procedures for conflict resolution

For the purposes of assessing whether another reservation conflicts with a reservation for a synchronization burst, the station shall apply the procedures defined in Section 1.3.6.5 except that the default quality of service parameters defined in Table 1-91 shall be applied to the synchronization burst reservation.

Table 1-91. Synchronization burst parameters for conflict resolution

| Symbol | Parameter name | Default |
| --- | --- | --- |
| Q1 | Priority | As per information field |
| Q2a | Slot selection range constraint for level 1 | 150nmi |
| Q2b | Slot selection range constraint for level 2 | 150nmi |
| Q2c | Slot selection range constraint for level 3 | 75nmi |
| Q2d | Slot selection range constraint for level 4 | 300nmi |

Note.— These default parameters place a tighter constraint at level 3 than the defaults for original slot selection, which would always result in a slot being selected. The tighter constraint forces the stream to dither to find slots that might be available at higher levels and hence reduces the probability of slot conflict.

Peer entity contact Table (PECT)

Every station shall maintain a table of all known stations. For each station, the table shall include the type of the station, a copy of the last of each type of broadcast burst, the time of the last transmission and a L1 counter. The ability to reach a peer station shall be assumed lost after L1 missed reservations.

Network entry protocol specifications

Network entry parameters

The network entry protocol shall implement the system parameters defined in Table 1-92.

Table 1-92. Plea parameters

| Symbol | Parameter name | Minimum | Maximum | Recommended default | Increment |
| --- | --- | --- | --- | --- | --- |
| CG1_plea | Minimum pool size of peer stations for plea | 1 | 256 | 2 | 1 |
| CG1_range | Maximum range for exposure filter | 0 nmi | 255 nmi | 100 nmi | 1 nmi |
| TG6 | Maximum delay for plea response | 0.1 sec | 16 sec | 2 sec | 0.1 sec |
| CG1_limit | Exposure filter threshold | 1 | 65 536 | 2 000 | 1 |
| CG1_inc | Exposure filter unknown station increment | 1 | 256 | MAX(MIN(5* (V11-1), 256), 1) | 1 |
| CG1_decay | Decay rate for CG1 filter | 1/256 | 1 | 247/256 | 0 |
| CG1_reach | Maximum unreachability time | 1 minute | 15 minutes | 3 minutes | 1 minute |
| TG7 | Minimum time delay for plea | 1 slot | 255 slot | 75 slot | 1 slot |

Note.— There is a separate CG1 filter for each channel which implements the exposure filter.

Parameter CG1_plea (minimum pool size of peer stations for plea)

CG1_plea shall define the minimum number of viable peer stations which must be identified before a plea can be issued. The plea target is selected uniformly from a set of CG1_plea viable peer stations.

Parameter CG1_range (maximum range for exposure filter)

CG1_range shall define the threshold beyond which newly-identified peer stations are disregarded for purposes of determining “exposure”.

Note 1.— This digital filter is intended to trigger network re-entry in cases where a station identifies a large number of new peer stations in a short period of time (e.g., during climb-out from an airport, or when crossing a mountain range). Conversely, since it is normal for new stations to be identified at great range, stations at great range should not be included in the determination of when a station has become “exposed”.

Note 2.— If range cannot be determined (i.e., because a station is not aware of its own location), it is set to a default value of 0. Therefore, unless a service provider has specifically reset CG1_range = 0 by a previous command detected by the station, all newly identified peer stations will increment the value of the filter.

Parameter TG6 (maximum delay for plea response)

TG6 shall specify the maximum allowed time interval between receiving a plea and transmitting a plea response. A station receiving a plea shall attempt to respond as quickly as possible. If a response cannot be generated in TG6 seconds, the station shall purge the plea and not respond.

Note.— This is intended to avoid creating reservations that will not be used.

Parameter CG1_limit (exposure filter threshold)

When CG1 is greater than or equal to CG1_limit, the station shall consider itself “exposed” (i.e., it has recently detected a large number of users which were not previously in its PECT, indicating that its reservation table may be incomplete). Consistent with the requirements of Section 1.5.6.3, the station shall then reset CG1 = 0, and perform network entry, on the affected channel.

Parameter CG1_inc (exposure filter unknown station increment)

CG1_inc shall be the value by which CG1 is incremented each time a  station which has been unreachable for at least CG1_reach minutes or a previously unknown peer station is detected with a station-to-station range less than or equal to CG1_range, or with station-to-station range which is indeterminate.

Parameter CG1_decay (decay rate for CG1 filter).

CG1_decay shall be the per second decay rate for CG1.

Recommendation

CG1_decay should be selected such that CG1 represents an approximate metric for the uncertainty in reservation information associated with newly detected stations.

Parameter CG1_reach

CG1_reach shall be the maximum allowed time between two successfully received transmissions from a peer station without increase the CG1_filter.

Parameter TG7 (minimum time delay for plea)

TG7 shall be the minimum time delay, measured in slot intervals, between the initiation of network entry procedures and the issuance of the first plea on the channel, and also the retry interval between successive examinations of the pool of viable peer stations for ple1. TG7 shall be set when a station tunes to a new frequency on which it has less than nr reservations for synchronization bursts over the next M1 slots; or, upon expiration, if there are no viable peer stations for the plea.

TG7 shall be cleared when the number of reservations for synchronization bursts, over the next M1 slots, equals or exceeds nr; or, when the station has monitored the frequency for M1 slots since the initiation of network entry procedures. Upon expiration of TG7, the station shall transmit a plea if a viable peer station exists.

Conditions for application of network entry procedures

When entering the network, a VSS user shall apply at least one of the network entry procedures defined in Sections 1.5.6.3.3, 1.5.6.3.4 or 1.5.6.3.5, under any of the conditions identified in Table 1-93, on the indicated channels.

Table 1-93. Conditions for network entry

| Condition | Channel(s) |
| --- | --- |
| Power ON | Global signalling channels |
| m2 is greater than or equal to M2_limit (see Section 1.2.2.2). Note.— The m2 test addresses retuning as well as short periods of receiver non-performance for reasons such as receiver deactivation or desensitization in a single-antenna configuration during transmission on another channel. | Any channel on which the station intends to transmit synchronization bursts in autonomous mode |
| CG1 is greater than or equal to CG1_limit. | Any channel on which the station intends to transmit synchronization bursts in autonomous mode |

The events affecting the value of the CG1 filter are defined in Table 1-94.

Table 1-94. Asynchronous events affecting value of management filter CG1

| Events | Values of CG1 |
| --- | --- |
| Station detects a synchronization burst from a station which has been unreachable on the channel for at least CG1_reach minutes or a previously unknown station at a station-to-station range which can either be calculated as less than CG1_range, or is indeterminate. | CG1new = CG1old + CG1_inc |
| Station detects a synchronization burst from a station which has been unreachable on the channel for less than CG1_reach minutes or a previously unknown station at a station-to-station range which can be calculated as greater or equal to CG1_range | CG1new = CG1old |
| Once per second | CG1new = truncate(CG1old * CG1_decay) |

If CG1 >= CG1_limit, CG1 shall be reset to 0.

Following successful application of the network entry procedures of this section on a given channel, yielding (60/nr) reservations, nr = nominal rate, a station shall not re-apply the procedures of this section, on that channel, for a period of M1 slots.

Network entry using plea/response procedures

Plea transmission procedures

A station desiring to transmit synchronization bursts on a VDL Mode 4 channel, which has been tuned to the channel for at least TG7 slots but which is prevented from transmission by lack of a valid reservation table, shall identify a set of peer stations S with the highest reported altitudes. The size of S, S_count, shall be defined by

S_count =  min((number of viable peer stations identified), CG1_plea)

and a peer station shall be considered viable if it is a mobile station which is known to have transmitted a synchronization burst on the channel on the normal slot boundary with the a/d bit set = 0, or if it is a ground station which is known to have transmitted a synchronization burst on the channel. If S_count is equal to zero, the TG7 timer shall be reset. If  S_count is greater than 0, the station shall transmit a plea to a peer station selected randomly from S. The plea shall be transmitted using the response reservation encoding in Section 1.3.18.1 (the destination address bits being set to the address of the selected peer station), with transmission starting on the delayed burst slot boundary of an unoccupied slot. The station shall continue to transmit plea requests, using the Q5 parameters specified in Table 1-95, until one of the following conditions is satisfied:

a)	it receives a plea response directed reservation request;

b)	it receives an autotune directed reservation request;

c)	it creates the necessary number of synchronization burst streams for the channel.

Table 1-95. Plea burst parameters

| Symbol | Parameter name | Default |
| --- | --- | --- |
| Q1 | Priority | 2 |
| Q2a | Slot selection range constraint for level 1 | 150 nmi |
| Q2b | Slot selection range constraint for level 2 | 150 nmi |
| Q2c | Slot selection range constraint for level 3 | 0 nmi |
| Q2d | Slot selection range constraint for level 4 | 300 nmi |
| Q3 | Replace queued data | TRUE |
| Q4 | Number of available slots | 2 |
| Q5num | VSS retransmission parameters | number of attempts | 1 |
| Q5wait |  | maximum time to wait for a reply | 3 seconds |

On each transmission of a plea request, the set S shall be rebuilt and the destination shall be selected randomly from the set.

A network entry burst (defined in Table 1-6a) shall have length n ( 11 octets excluding frame flags and bit stuffing and shall have a priority of 14. The information field, if present, shall be set to 0 on transmit and shall be ignored on receive.

Note 1.— A station may consider its reservation table for a channel invalid, for the purpose of selecting slots for synchronization bursts, if it has been tuned to a channel for less than M1 slots or if the conditions for rapid network entry, defined in Table 1-93, are satisfied.

Note 2.— If the station has less than nr reservations for synchronization bursts over the next M1 slots at the time the last directed reservation is executed, it may repeat the plea transmission procedure in order to generate additional reservations. The TG7 timer will not be running, and is not required, in this scenario.

Note 3.— In the event that a station issues multiple pleas and receives multiple responses, the final plea/response interaction could result in a total number of synchronization burst streams per M1 slots which exceeds nr. In this case the station would be required to cancel some of the reservations and shift individual nominal slots (or sets of nominal slots) in order to form a periodic sequence of synchronization bursts in time, in accordance with paragraph 1.3.10.5.1.

Plea response transmission procedures

Upon receiving a network entry burst with a response reservation addressed to itself (i.e., a plea) , a station shall take the following actions. If the station has observed the given frequency for at least the previous 60 seconds, and has not initiated a network entry or re-entry procedure within the previous 60 seconds, it shall transmit a synchronization burst request with a plea response reservation containing: min(12, number of reservations required to allow one minute of transmissions at the default synchronization burst rate for this channel) reservations or else if the transmission rate is not known  once per 10 second reservations. These reservations shall be identified as follows:

a)	unexpired reservations from any prior plea response addressed to the requesting station;

b)	any periodic reservations for the requesting station, not otherwise contained in a prior plea response and which a) do not conflict with other known reservations, and b) can be appended to a possible list of reservations in accordance with item (1) above (considering the encoding constraints of the plea response);

c)	additional reservations as required, using the selection parameters of Table 1-96.

Otherwise the station shall ignore the burst.

If the station cannot transmit the plea response within TG6 seconds of receiving the plea, the plea response shall be purged and not transmitted.

Table 1-96. Plea response parameters

| Symbol | Parameter name | Default |
| --- | --- | --- |
| Q1 | Priority | 14 |
| Q2a | Slot selection range constraint for level 1 | 150 nmi |
| Q2b | Slot selection range constraint for level 2 | 150 nmi |
| Q2c | Slot selection range constraint for level 3 | 0 nmi |
| Q2d | Slot selection range constraint for level 4 | 300 nmi |
| Q3 | Replace queued data | TRUE |
| Q4 | Number of available slots | 3 |

Recommendation

The station should attempt to transmit the plea response as soon as possible following the plea (while still selecting the transmit slot randomly). The first reservation contained in the plea response should occur as soon as possible in time following the plea response, but not sooner than V52 slots. This supports rapid network entry while still providing sufficient time for the station entering the network to plan for, and form, its first synchronization burst. The station should attempt to reserve slots which are currently unreserved, and which are related to available slots for which the plea recipient can transmit BND reservations.

Note.— The constraints on transmission time avoid possible race conditions and conflicting reservation sets associated with multiple exchanges of pleas and plea responses. The requirement to include unexpired reservations, if known, minimizes the likelihood of wasted channel resources in the case where a station fails to hear its requested plea response, but other station(s) in the airspace heard it and allocated the appropriate slots.

Plea response reception procedures

A station receiving a plea response shall transmit in the reserved slots.

Note.— If the station has not yet declared/transmitted an existing set of periodic reservations for all required synchronization bursts on the given frequency, it may use the reservation fields in the slots reserved by the plea response to set up these periodic streams using periodic reservations (if it has been listening to the channel for at least 60 seconds) or BND reservations (if it has been listening to the channel long enough to use the BND reservation, but not long enough for a periodic reservation). A station may also transmit a null reservation (See Section 1.3.9) or a periodic cancellation (see Section 1.3.10.5.9) in the slots reserved by the plea response. See Section 1.3.10.5.1 for requirements regarding transmissions after the first M1 slots.

Network entry via BND

A station intending to initiate synchronization burst transmissions on a channel, which has insufficient reservations for its intended number of synchronization burst streams, and which cannot make periodic reservations, shall transmit a series of delayed network entry bursts with BND reservations. The number per minute of delayed network entry bursts with BND reservations  shall be equal to or less than the intended number of synchronization burst streams per minute. The station shall stop transmitting delayed network entry bursts with a BND reservation if it has set up the required number of streams or it receives a plea response or a directed reservation request. If it receives a plea response or directed reservation request, and thus does not require the reservations created by previous BND transmissions, it shall include a no reservation field in the synchronization bursts transmitted in the unnecessary slots. At most one delayed network entry burst using a BND broadcast reservation shall be made per intended stream.

A station which has reservations for synchronization burst transmissions and which intends to continue operations on the channel, but which is unable to make periodic reservations, shall use BND reservations in lieu of periodic reservations.

A network entry burst (defined in Table 1-6a) shall have length n ( 11 octets excluding frame flags and bit stuffing and shall have a priority of 14. The information field, if present, shall be set to 0 on transmit and shall be ignored on receive.

Note.— A station may be temporarily unable to make periodic reservations if its existing reservations are due to a recently received plea response, or if it determines that it has become “exposed” (i.e., CG1 exceeded CG1_limit within the previous 60 seconds).

Network entry by full-slot random transmission or plea-to-self

In the event that a station has listened to a channel for a full minute prior to net entry, a station shall use one of two procedures to begin transmitting synchronization bursts:

a)	use default random transmission protocols with combined periodic/incremental reservation types to place each new periodic reservation and to simultaneously reserve the next selected slot in the same superframe for the transmission containing the next periodic reservation, or

b)	use default random transmission protocols to transmit a plea response addressed to itself, followed by synchronization bursts with periodic reservations in the reserved slots (note: these may be affected by other reservations detected after transmission of the plea response).

Note.— These default procedures may also be used when a station reverts to autonomous operations after a period of directed operations on the GSC(s), such that the station has a valid reservation table at the time of reversion to autonomous mode.

CTRL frame types and procedures

The mobile and ground LMEs shall use the CTRL frame types listed in Table 1-97, and the procedures described below to provide a reliable connection between the mobile and ground-based system. If an LME receives any valid CTRL_HO frame from a system with which it does not have a link, it shall respond with a CTRL_LCR with the “d” bit set to 1 in the Protocol Violation Cause Code..

Table 1-97. CTRL parameters

|  |  | GSIF | Air initiated link establishment |
| --- | --- | --- | --- |
|  | Source address | Ground station | Mobile | New ground station |
|  | Destination address | All aircraft | Proposed ground station | Mobile |
| CTRL parameters | PI hex | GSIF | CTRL_CMD_LE | CTRL_RSP_LE |
| Connection management | 01h | N/A | M | M |
| CTRL sequencing | 02h | N/A | M | M |
| Protocol options | 03h | N/A | O | O |
| LCR cause | 04h | N/A | N/A | N/A |
| Datalink service | 40h | O | N/A | O |
| VSS sublayer | 41h | O | N/A | O |
| Quality of Service | 42h | O | N/A | O |
| m2 filter | 43h | O | N/A | O |
| CG1 filter | 44h | O | N/A | O |
| Autotune | 45h | O | N/A | O |
| Maximum number of missed reservations | 46h | N/A | N/A | O |
| Repl. ground station | 47h | O | N/A | O |
| Random access | 48h | O | N/A | O |
| Re-transmission | 49h | O | N/A | O |
| Timer TL1 | 4Ah | O | N/A | O |
| Ground Station Address filter | 4Bh | N/A | N/A | N/A |
| Broadcast connection | 4Ch | N/A | N/A | N/A |
| Modulation support | 80h | N/A | O | N/A |
| Alternate grd stations | 81h | N/A | O | N/A |
| Destination airport | 82h | N/A | O | N/A |
| Airport coverage | C0h | O | N/A | O |
| Nearest airport | C1h | M1 | N/A | O2 |
| ATN router NETs | C2h | M1 | N/A | O2 |
| Ground-based system mask | C3h | M | N/A | M |
| Frequency support | C4h | O | N/A | O |
| Directory of service | C5h | O | N/A | O |
| Channel management | C6h | O | N/A | O |
| PI = Parameter identifier |
| M = Mandatory |
| O = Optional |
| N/A = Not applicable |
| h = hexadecimal |
| NOTES |
| 1. In a GSIF frame it is mandatory to include either the Airport Coverage Indication parameter or the Nearest Airport Identifier parameter but not both (see 5.4.2.7.3). |
| 2. Where the Airport Coverage Indication parameter and the Nearest Airport Identifier parameter are marked as optional, either parameter may be included in the frame or neither but not both. |

|  |  | Ground initiated handoff | Air initiated handoff |
| --- | --- | --- | --- |
|  | Source address | Proposed ground station | Mobile | Mobile | New ground station |
|  | Destination address | Mobile | New ground station | Proposed ground station | Mobile |
| CTRL parameters | PI hex | CTRL_CMD_HO (re=1) | CTRL_RSP_HO (re=1) | CTRL_CMD_HO (re=1) | CTRL_RSP_HO (re=1) |
| Connection Management | 01h | M | M | M | M |
| CTRL sequencing | 02h | M | M | M | M |
| Protocol options | 03h | O | O | O | O |
| LCR cause | 04h | N/A | N/A | N/A | N/A |
| Datalink service | 40h | O | N/A | N/A | O |
| VSS sublayer | 41h | O | N/A | N/A | O |
| Quality of service | 42h | O | N/A | N/A | O |
| m2 filter | 43h | O | N/A | N/A | O |
| CG1 filter | 44h | O | N/A | N/A | O |
| Autotune | 45h | O | N/A | N/A | O |
| Maximum number of missed reservations | 46h | O | N/A | N/A | O |
| Repl. ground station | 47h | O | N/A | N/A | O |
| Random access | 48h | O | N/A | N/A | O |
| Re-transmission | 49h | O | N/A | N/A | O |
| Timer TL1 | 4Ah | O | N/A | N/A | O |
| Ground Station Address filter | 4Bh | N/A | N/A | N/A | N/A |
| Modulation support | 80h | N/A | N/A | N/A | N/A |
| Alternate ground stations | 81h | N/A | N/A | O | N/A |
| Destination airport | 82h | N/A | O | O | N/A |
| Airport coverage | C0h | O1 | N/A | N/A | O1 |
| Nearest airport ID | C1h | O1 | N/A | N/A | O1 |
| ATN router NETs | C2h | M | N/A | N/A | O |
| Ground-based system mask | C3h | M | N/A | N/A | O |
| Frequency support | C4h | O | N/A | N/A | O |
| Directory of service | C5h | O | N/A | N/A | O |
| Channel management | C6h | O | N/A | N/A | O |
| PI = Parameter identifier M = Mandatory O = Optional N/A = Not applicable h = hexadecimal NOTES 1 Where the Airport Coverage Indication parameter and the Nearest Airport Identifier parameter are marked as optional, either parameter may be included in the frame or neither but not both. |

|  |  | Air requested handoff | Ground requested handoff | Ground requested broadcast | Link connection rejection |
| --- | --- | --- | --- | --- | --- |
|  | Source address | Mobile | Current ground station | New ground station | Any station |
|  | Destination address | Current or proposed ground station | Mobile | All mobiles | Any station |
| CTRL parameters | PI hex | CTRL_CMD_HO (re=0) | CTRL_CMD_HO (re=0) | CTRL_CMD_HO (re=0) | CTRL_RSP_LCR CTRL_CMD_LCR |
| Connection management | 01h | M | M | M | M |
| CTRL sequencing | 02h | M | M | M | M |
| Protocol options | 03h | O | O | O | O |
| LCR cause | 04h | N/A | N/A | N/A | M |
| Data link service | 40h | N/A | O | O | N/A |
| VSS sublayer | 41h | N/A | O | O | N/A |
| Quality of service | 42h | N/A | O | O | N/A |
| m2 filter | 43h | N/A | O | O | N/A |
| CG1 filter | 44h | N/A | O | O | N/A |
| Autotune | 45h | N/A | O | O | N/A |
| Maximum number of missed reservations | 46h | N/A | O | O | N/A |
| Repl. ground station | 47h | N/A | O | O | N/A |
| Random access | 48h | N/A | O | O | N/A |
| Re-transmission | 49h | N/A | O | O | N/A |
| Timer TL1 | 4Ah | N/A | O | O | N/A |
| Ground Station Address filter | 4Bh | N/A | N/A | M | N/A |
| Modulation support | 80h | N/A | N/A | O | N/A |
| Alternate ground | 81h | O | N/A | N/A | N/A |
| Destination airport | 82h | O | N/A | N/A | N/A |
| Airport coverage | C0h | N/A | N/A | O1 | N/A |
| Nearest airport | C1h | N/A | N/A | O1 | N/A |
| ATN router NETs | C2h | N/A | O | M | N/A |
| Ground-based system mask | C3h | N/A | O | O | N/A |
| Frequency support | C4h | N/A | O | O | N/A |
| Directory of service | C5h | N/A | O | O | N/A |
| Channel management | C6h | N/A | O | O | N/A |
| PI = Parameter identifier M = Mandatory O = Optional N/A = Not applicable h = hexadecimal NOTES 1. Where the Airport Coverage Indication parameter and the Nearest Airport Identifier parameter are marked as optional, either parameter may be included in the frame or neither but not both. |

CTRL transmission procedures

Frequency management procedures

The mobile LME shall use the following procedures to acquire a frequency on which reliable VDL services are available.

Frequency search

The mobile LME shall initiate the frequency search procedure on system initialization or after link disconnection, if there are no ground stations providing the requested service which are reachable according to the definition of Section. It shall attempt to identify a frequency on which the required VDL service is available by tuning the radio to the GSCs and/or to other frequencies on which it knows a-priori that VDL service is available.  On the basis of information contained in the GSIF, it shall select an appropriate channel to received the required service.

Frequency recovery

The mobile LME shall initiate the frequency recovery procedure if it can no longer establish a link on the current frequency or if the VSS indicates that the current frequency is congested. It shall tune the radio to an alternate frequency using the data in the Frequency Support List or Directory of Service message previously received on the current link.

Link connectivity procedures

The mobile and ground LMEs shall use the following procedures to maintain connectivity across the VHF link:

a) ground station identification;

b) initial link establishment;

c) mobile-initiated handoff;

d) mobile-requested ground-based initiated handoff;

e) ground-based initiated handoff;

f) ground-based requested mobile-initiated handoff;

g) ground-based requested broadcast handoff; and

h) autotune.

Ground station identification

A ground station providing a VDL Mode 4 service shall send a GSIF at least once per minute on each of the channels on which it offers the service, as well as on the GSCs by broadcasting a CTRL_CMD (re = 0) with parameters as per Tables 1-97. The operator of that ground station shall ensure that, in addition to transmitting GSIFs on the service frequency, GSIFs are transmitted on the CSCs. Mobile LMEs receiving a GSIF shall process its content to identify the functionality of the ground station as well as the correct operational parameters to be used when communicating with it. Mobile LMEs which have a connection with the transmitting ground station shall process only information parameters as per Table 1-97.

Link establishment

The mobile LME shall initiate the link establishment procedure with a ground station to establish an initial link with the ground-based system. A mobile transmitting or receiving a DM/DISC frame shall initiate link establishment according to the local link management policy if no links remain.

Mobile initiation

The mobile LME shall choose a ground station with which it wishes to establish a link based on its capability to support a link and so as to maximise the likely duration of the connection to the ground station.

Note,- To maximise the likely connection time, the mobile can take account of mobile position, intent, ground station position, the signal quality of all received uplink frames and on information in any received GSIFs.

It shall then attempt to establish a link with the chosen ground station by sending a CTRL_CMD_LE (re=1) frame. This frame shall include the mandatory parameters as per Table 1-97 and also any optional parameters for which the mobile LME does not wish to use the default value. If the mobile LME has received a GSIF from the ground station to which it is transmitting the CTRL_CMD_LE (re=1), then it shall use the parameters as declared; otherwise, it shall use the default parameters.

General ground response

If the ground LME receives the CTRL_CMD_LE, it shall confirm link establishment by sending a CTRL_RSP_LE frame containing the parameters as per Table 1-97. The ground LME shall include in the CTRL_RSP_LE any optional parameters for which it is not using the default values. If the CTRL_RSP_LE includes the Autotune parameter then the Replacement Ground Station List parameter shall be included indicating the ground stations on the new frequency with which the mobile LME can establish a new link using the operating parameters specified in the CTRL_RSP_LE. If the CTRL_RSP_LE does not include the Autotune parameter, the ground LME shall include the Replacement Ground Station List parameter if it wishes to indicate the ground stations which can be reached on the current frequency using the same operating parameters as the transmitting station.

Exceptional cases

If an LME receiving the CTRL_CMD_LE cannot establish the link with the sending LME, then it shall transmit a CTRL_RSP_LCR instead of a CTRL_RSP_LE. If the parameters in the CTRL_RSP_LE from the ground LME are not acceptable to the mobile LME, then the mobile LME shall transmit a DM/DISC to the ground. If the Autotune parameter is included in the CTRL_RSP_LE and the mobile LME is unable to perform the autotune, then the mobile LME shall respond with an CTRL_CMD_LCR (re=0); the link established on the current frequency shall not be affected. While waiting for a response to a CTRL_CMD_LE, a mobile LME receiving any unicasted frame other than an CTRL shall retransmit the CTRL_CMD_LE instead of transmitting a DM/DISC.

Mobile-initiated handoff

If a mobile LME implements this section, then it shall set the “i” bit in the Protocol Options parameter to 1; otherwise, it shall set the “i” bit to 0.

Mobile handoff

Once the mobile LME has established a link to a ground station, it shall monitor the VHF signal quality on the link and the transmissions of the other ground stations. The mobile LME shall establish a link to a new ground station if any of the following events occur:

a) the VHF signal quality on the current link is determined, in accordance with local link management policy, to be insufficient to maintain reliable communications and the signal quality of another ground station

is significantly better;

b) TL2 seconds have elapsed since the LME initiated the request  to send any frame to the current ground station;

c)The peer station has become unreachable as defined in Section 1.5.4.1; or

d) Timer TM2 expires. In this case, the mobile LME shall autonomously tune to an alternate

frequency (provided in a frequency support list) before initiating the handoff.

e) The mobile is at a position which, in accordance with local link management policy, requires the station to establish a link with a new ground station.

Site selection preference

From among those ground stations with acceptable link quality, the mobile LME shall prefer to handoff to a ground station which indicates (in the GSIF) accessibility to the air-ground router(s) to which the mobile DTE has subnetwork connections.

Recommendation

If a mobile has commenced approach to its destination airport and its current link is with a ground station that does not offer service at that airport, it should handoff to a ground station which indicates in its Airport Coverage Indication parameter that it offers service at that airport.

Interaction of LMEs

When a mobile VME hands off from a ground station in one ground-based system (and thus associated with one LME) to a ground station in another ground-based system (and thus associated with a different LME in the mobile), the new LME shall use the link establishment procedures and the old LME shall send a DM/DISC when directed by the VME.

Note.— Optimally the old link should not be disconnected until after the new link is capable of carrying application data. However this is outside the scope of this technical manual.

General ground response

If the ground LME receives the CTRL_CMD_HO, it shall confirm link handoff by sending a CTRL_RSP_HO frame containing the parameters as per Table 1-97. The ground LME shall include in the CTRL_RSP_HO the optional parameters for which it is not using the default values. If the CTRL_RSP_HO includes the Autotune parameter, then the Replacement Ground Station List parameter shall be included to indicate the ground stations with which the mobile LME can establish a new link on the new frequency, using the operating parameters specified in the CTRL_RSP_HO. If the CTRL_RSP_HO does not include the Autotune parameter, the ground LME shall include the Replacement Ground Station List parameter if it wishes to indicate the ground stations which can be reached on the current frequency using the same operating parameters as the transmitting station.

Disconnecting old link

If the new and old ground stations are associated with different systems, then the procedures of Section 1.5.7.5.4 shall be followed. Otherwise, the mobile LME shall set Timer TL1 when it receives the CTRL_RSP_HO. The ground LME shall set Timer TL1 after it transmits the CTRL_RSP_HO. Both stations shall continue to operate on the old link until their respective Timer TL1 expires, after which each will consider the link disconnected without sending or receiving a DM/DISC.

Exceptional cases

If the ground LME cannot satisfy the CTRL_CMD_HO, then it shall transmit a CTRL_RSP_LCR instead of a CTRL_RSP_HO; the current link shall not be affected. While waiting for a response to a CTRL_CMD_HO, a mobile LME receiving any unicasted frame other than a CTRL from any ground station other than the current station shall retransmit the CTRL_CMD_HO. more than TL2 seconds have elapsed since the LME initiated the request to send the CTRL_CMD_HO, the aircraft LME shall attempt to handoff to another ground station; the current link shall not be affected. If the mobile LME cannot perform the autotune, it shall transmit a CTRL_CMD_LCR (re=0); the current link shall not be affected. If the parameters in the CTRL_RSP_HO are not acceptable to the mobile LME, then the mobile LME shall transmit a DM/DISC to the ground on the new link.

Mobile-requested ground-initiated handoff

An mobile LME shall not perform this section when its peer LME does not support handoff initiation. A mobile LME shall only perform this section if the current and proposed ground stations are both managed by its peer LME.

Mobile action

For a mobile LME to request the ground LME to initiate a handoff, it shall send an CTRL_CMD_HO (re=0) addressed to its current or proposed ground station with the parameters as per Table 1-97. During this procedure the current link shall not be affected until the mobile LME receives a CTRL_CMD_HO (re=1).

General ground response

If the ground LME receives the CTRL_CMD_HO, it shall commence a ground-initiated handoff from a proposed ground station. The ground LME shall only transmit the CTRL_CMD_HO (re=1) once per CTRL_CMD_HO (re=0) request that it receives.

Exceptional cases

If the ground system cannot initiate the handoff, it shall send a CTRL_CMD_LCR (P=0); the current link shall not be affected.

Recommendation

If more than TL2 seconds have elapsed since the LME initiated the request to send the CTRL_CMD_HO, the mobile LME should attempt to request to handoff to another station before disconnecting all links to the ground and restarting link establishment.

Ground-based initiated handoff

If a ground LME implements this section, then it shall set the “i” bit in the Protocol Options parameter to 1; otherwise, it shall set the “i” bit to 0.

Ground action

To command a mobile, to which a link exists, to establish a new link to a proposed ground station on the same frequency, the ground LME shall send via that ground station a CTRL_CMD_HO (re=1) to the mobile with parameters as per Table 1-97. If the ground LME will accept a handoff to other ground stations, the CTRL_CMD_HO shall include the Replacement Ground Station List parameter specifying the link layer address of those other stations. Any operating parameters in the CTRL_CMD_HO (either modification or informational) shall be valid for the transmitting station and for all ground stations listed in the Replacement Ground Station List parameter, except the Airport Coverage Indication parameter and Nearest Airport parameter which are only valid for the transmitting ground station.

General mobile response

The mobile LME shall respond by sending a CTRL_RSP_HO with parameters as per Table 1-97 to either the proposed ground station or to its preferred ground station if the CTRL_CMD_HO included the Replacement Ground Station List parameter.

Disconnecting old link

The mobile LME shall set Timer TL1 after it transmits the CTRL_RSP_HO. The ground LME shall set Timer TL1 when it receives the CTRL_RSP_HO. Although new traffic will be sent over the new link, the old link shall not be disconnected immediately to allow any old traffic to be delivered.

Exceptional cases

If the mobile LME cannot accept the handoff request, it shall respond with a CTRL_RSP_LCR; the current link shall not be affected. While waiting for a response to a CTRL_CMD_HO, a ground LME receiving any unicasted frame other than a CTRL from the mobile shall retransmit the CTRL_CMD_HO. If the parameters in the CTRL_RSP_HO are not acceptable to the ground LME, then the ground LME shall transmit a DM/DISC to the mobile on the new link.

Recommendation

If TL2 seconds have elapsed since the LME initiated the request to send the CTRL_CMD_HO, the ground LME should attempt to handoff via another station before disconnecting all links to the mobile.

Ground-based requested mobile-initiated handoff

A ground LME shall not perform this section with mobiles that do not support handoff initiation.

Ground action

For the ground LME to request a mobile to initiate a handoff, it shall send a CTRL_CMD_HO (re=0) on the current link with parameters as per Table 1-97. The parameters in the CTRL (both modification and information) are valid for all ground stations listed in the Replacement Ground Station List. It shall only include operational parameters if it also includes the Replacement Ground Station List parameter. If the Autotune parameter is included, then the Replacement Ground Station List parameter shall apply to the new frequency.

General mobile response

If the mobile LME receives the CTRL_CMD_HO, it shall commence an aircraft-initiated handoff to a ground station, preferably one listed in the Replacement Ground Station List parameter.

Exceptional cases

If the mobile LME cannot initiate the handoff, it shall send a CTRL_CMD_LCR (re=0); the current link shall not be affected. If the Autotune parameter is included in the CTRL_CMD_HO (re=0), the mobile LME shall retransmit on the new frequency the CTRL_CMD_HO (re=1) using the normal retransmission procedures; otherwise, it shall only transmit the CTRL_CMD_HO (re=1) once per received CTRL_CMD_HO (re=0).

Recommendation

If TL2 seconds have elapsed since the LME initiated the request to send the CTRL_CMD_HO, the ground LME should attempt to request a handoff via another station before disconnecting all links to the mobile.

Ground-based requested broadcast handoff

If the ground LME supports broadcast link handoffs then it shall set the “bl ” bit in the AVLC options parameter to 1; otherwise, it shall set the “bl ” bit to 0.

Ground action

If the ground LME supports broadcast link handoffs, for each mobile that indicates it supports broadcast link handoff, the ground LME shall confirm the link handoff by including the Broadcast Connection parameter per Table 1-97.

Mobile response

The LME in each mobile shall process received broadcast CTRL_CMD_HO (re=0) and determine if the ground LME had performed a broadcast link recovery  for it. It shall do this by verifying that the Ground Station Address Filter parameter contains the DLS address of the ground station that it is connected to and that a Broadcast Connection parameter exists containing its station address. Mobile LMEs supporting broadcast recovery shall consider that a link handoff has occurred with the new link having the same parameters as the old link (as modified by the parameters in the broadcast CTRL). The old link shall be disconnected immediately.

Exceptional cases

If the mobile LME does not support broadcast recovery, but the ground LME performed a broadcast link recovery for it, then the mobile LME shall perform either an air-initiated link handoff, (if the aircraft LME supports same), or request a link handoff. If the mobile LME finds the new ground station unacceptable, it shall perform an air-initiated handoff (if the aircraft LME supports same), or request a link handoff. If the Ground Station Address Filter parameter does not equal the DLS address of a link that the mobile LME has or if no mobile identifier subfield in a Broadcast Connection parameter equals its mobile address, the mobile LME shall not process the ground requested broadcast handoff.

Ground-based commanded autotune

This section summarizes the autotune details found in Section 1.5.7.7.

Ground action

To command a mobile LME to handoff to a ground station on a different frequency, the ground LME shall include the Autotune and Replacement Ground Station List parameters in a CTRL it sends during a link establishment or handoff procedure.

General mobile response

On receipt of a CTRL commanding an autotune, the mobile LME shall retune the mobile radio to the new frequency and commence a mobile-initiated handoff to the chosen ground station.

Exceptional cases

If the mobile LME cannot perform the autotune, it shall transmit a CTRL_CMD_LCR (re=0); the current link shall not be affected.

SECTION  VDL MODE 4 MOBILE SUBNETWORK DEPENDENT CONVERGENCE FUNCTION (SNDCF)

The VDL Mode 4 shall support the Frame Mode SNDCF as defined in ICAO Doc 9705 Edition 3, section 5.7.8.  To support the interface, VDL Mode 4 shall:

- generate a Join event upon reception of a CTRL_RSP_LE or a CTRL_RSP_HO.

- generate a Leave event whenever either the link is terminated, or the link is abandoned.

Note 1.— A link can be terminated for a variety of reasons including a station becoming unreachable as defined in Section 1.5.5.1, protocol exchanges and link timeouts (e.g. expiration of the TL1 or the TL2 timer). A link is abandoned when the TM2 timer indicates that the frequency is congested and the LME enters frequency recovery mode trying to find a less congested frequency and the VDL 4 station does not have a spare receiver to monitor both the old and the new channel.

(3)	provide a data transfer service as defined in Section 1.4.

Note 2.— The timeliness of the generation of leave events depends on the value of the L1 counter and the number of reservations known to have been made by a station within a time interval.

SECTION  ADDITIONAL MATERIAL FOR ADS-B APPLICATIONS

INTRODUCTION

Note.— This section defines the additional requirements for VDL Mode 4 supporting ADS-B services.

ACRONYMS, ABBREVIATIONS AND PARAMETER SYMBOLS

Note.— Other acronyms, abbreviations and parameter symbols have been listed in previous sections of these SARPs.

The following acronyms and abbreviations are introduced in this section as they are defined below.

| Acronym | Description |
| --- | --- |
| MASPS | Minimum aviation system performance standards |

Note.— The following parameter symbols are introduced in this section as they are defined below. Other parameters have been listed in previous sections of these SARPs.

Table 3-1. Summary of parameter symbols for ADS-B applications

| Parameter | Name | Section or table defined in |
| --- | --- | --- |
| ac | Aircraft category | Table 3-11 |
| altr | Altitude rate | Table 3-11 |
| app | Application specific data | Table 3-35 |
| auto | Autonomous information | Table 3-21 |
| aux | Auxiliary parameters | Table 3-21 |
| bgo | Baro/geo offset | Table 3-11 |
| br/gr | Baro rate/geo rate offset | Table 3-11 |
| csid | Command set ID | Table 3-27 |
| csl | Call sign left | Table 3-11 |
| csr | Call sign right | Table 3-11 |
| day | Universal coordinated time (UTC) day subfield | Table 3-11 |
| dc | Directory count | Table 3-27 |
| fc | Frequency count | Table 3-27 |
| frq | Frequency index | Table 3-39 |
| gs | Ground speed | Table 3-11 |
| gt | Ground track | Table 3-11 |
| h | UTC hour | Table 3-11 |
| ido | Individual offset | Table 3-29 |
| lat4 | 4-bit latitude offset | Table 3-11 |
| lat6 | 6-bit latitude offset | Table 3-11 |
| lat8 | 8-bit latitude offset | Table 3-11 |
| len | Length | Table 3-35 |
| lg | Parameter group length | Table 3-21 |
| lon4 | 4-bit longitude offset | Table 3-11 |
| lon6 | 6-bit longitude offset | Table 3-11 |
| lon8 | 8-bit longitude offset | Table 3-11 |
| mb | More bit | Table 3-35 |
| mid | Message ID | Table 3-35 |
| min | UTC minute | Table 3-11 |
| mon | UTC month | Table 3-11 |
| NES | Number of elements in script | 3.7.2.1 |
| no | TCP number | Table 3-11 |
| nsd | Non-standard definition | Table 3-39 |
| NTM | Number of transmissions per minute | 3.7.2.1 |
| nucr | Rate uncertainty | Table 3-11 |
| pid | Patch ID | Table 3-11 |
| pos | Maximum sleep position | Table 3-21 |
| r-b/a | Requested baro/geo altitude | Table 3-21 |
| rcv | Must receive | Table 3-37 |
| r-id | Requested information ID subfield | Table 3-21 |
| rpt | Repeat count | Table 3-39 |
| sc | Script count | Table 3-27 |
| sec | UTC second | Table 3-11 |
| sleep | Autonomous monitoring | Table 3-21 |
| slt | Slot | Table 3-11 |
| snr | Secondary reporting rate | Table 3-21 |
| sr | Script rate | Table 3-27 |
| st | Status | Table 3-11 |
| styp | Script duration type | Table 3-27 |
| tc | Transmission definition count | Table 3-27 |
| tind | Turn indication | Table 3-11 |
| ttg | Time to go | Table 3-11 |
| txd | Transmission definition index | Table 3-39 |
| typ | TCP type | Table 3-11 |
| vc | Vertex count | Table 3-31 |
| vel | Maximum sleep velocity | Table 3-21 |
| yr | UTC year | Table 3-11 |

INFORMATION FIELD FORMATS

Table 3-2 defines the information field formats that have been assigned for use by the ADS-B application.

Table 3-2. ADS-B information fields

| Information field ID (id) | ID extension 1 (id1) | ID extension 2 (id2) | Information field name |
| --- | --- | --- | --- |
| 0 hex | not present | not present | Basic |
| 1 hex | not present | not present | High dynamic |
| 2 hex | not present | not present | Full position |
| 3 hex | not present | not present | Basic ground |
| 4 hex | not present | not present | UTC time |
| 5-7 hex | not present | not present | Available for future use |
| 8 hex | not present | not present | Two slot TCP |
| 9 hex | not present | not present | Single slot TCP |
| A hex | 0 hex | not present | Available for future use |
| A hex | 1 hex | not present | Aircraft data (call sign, category, status) |
| A hex | 2 – 9 hex | not present | Available for future use |
| A hex | A hex | 0 hex | High resolution |
| A hex | A hex | 1 - 9 hex | Available for future use |
| A hex | A hex | A hex | Extension (available for future use via further ID extension fields) |
| A hex | A hex | B – F hex | Available for future use |
| A hex | B – F hex | not present | Available for future use |
| B – E hex | not present | not present | Available for future use |
| F hex | not present | not present | No information field provided |

For each information field, data shall be encoded as defined in Tables 3-3 to 3-10.

Table 3-3. Information field 0 hex — Basic

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| information field ID | 11 | x | x | x | x | 0 | 0 | 0 | 0 |
| rate uncertainty (nucr) 6-bit latitude offset (lat6) | 12 | nucr2 | nucr1 | lat66 | lat65 | lat64 | lat63 | lat62 | lat61 |
| 6-bit longitude offset (lon6) baro rate/geo rate (br/gr) | 13 | nucr3 | br/gr | lon66 | lon65 | lon64 | lon63 | lon62 | lon61 |
| baro/geo offset (bgo) | 14 | altr9 | bgo7 | bgo6 | bgo5 | bgo4 | bgo3 | bgo2 | bgo1 |
| altitude rate (altr) | 15 | altr8 | altr7 | altr6 | altr5 | altr4 | altr3 | altr2 | altr1 |
| ground speed (gs) | 16 | gs8 | gs7 | gs6 | gs5 | gs4 | gs3 | gs2 | gs1 |
| ground track (gt) | 17 | gs11 | gs10 | gs9 | gt5 | gt4 | gt3 | gt2 | gt1 |
|  | 18 | gt11 | gt10 | gt9 | gt8 | gt7 | gt6 |  |  |

Note.— “x” denotes part of fixed data field.

Table 3-4. Information field 1 hex — High dynamic

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| information field ID | 11 | X | x | x | x | 0 | 0 | 0 | 1 |
| baro rate/geo rate (br/gr), baro/geo offset (bgo) | 12 | br/gr | bgo7 | bgo6 | bgo5 | bgo4 | bgo3 | bgo2 | bgo1 |
| altitude rate (altr) | 13 | altr8 | altr7 | altr6 | altr5 | altr4 | altr3 | altr2 | altr1 |
| rate uncertainty (nucr) | 14 | altr9 | nucr3 | nucr2 | nucr1 | gs12 | gs11 | gs10 | gs9 |
| ground speed (gs) | 15 | gs8 | gs7 | gs6 | gs5 | gs4 | gs3 | gs2 | gs1 |
| 4-bit longitude offset (lon4), 4-bit latitude offset (lat4) | 16 | lon44 | lon43 | lon42 | lon41 | lat44 | lat43 | lat42 | lat41 |
| ground track (gt) | 17 | gt8 | gt7 | gt6 | gt5 | gt4 | gt3 | gt2 | gt1 |
|  | 18 | gt12 | gt11 | gt10 | gt9 | res | res |  |  |

Note.—  “x” denotes part of fixed data field.

Table 3-5. Information field 2 hex — Full position

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| information field ID | 11 | X | x | x | x | 0 | 0 | 1 | 0 |
| 6-bit latitude offset (lat6) | 12 | pid10 | pid9 | lat66 | lat65 | lat64 | lat63 | lat62 | lat61 |
| patch ID (pid) | 13 | pid8 | pid7 | pid6 | pid5 | pid4 | pid3 | pid2 | pid1 |
| baro/geo offset (bgo) | 14 | gt11 | bgo7 | bgo6 | bgo5 | bgo4 | bgo3 | bgo2 | bgo2 |
| 6-bit longitude offset (lon6) | 15 | gt10 | gt9 | lon66 | lon65 | lon64 | lon63 | lon62 | lon61 |
| ground track (gt) | 16 | gt8 | gt7 | gt6 | gt5 | gt4 | gt3 | gt2 | gt1 |
| ground speed (gs) | 17 | gs8 | gs7 | gs6 | gs5 | gs4 | gs3 | gs2 | gs1 |
| rate uncertainty (nucr) | 18 | gs11 | gs10 | gs9 | nucr3 | nucr2 | nucr1 |  |  |

Note.— “x” denotes part of fixed data field.

Table 3-6. Information field 3 hex — Basic ground

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| information field ID | 11 | x | x | x | x | 0 | 0 | 1 | 1 |
| UTC hours (h) | 12 | res | res | res | h5 | h4 | h3 | h2 | h1 |
| UTC minute (min) | 13 | pid10 | pid9 | min6 | min5 | min4 | min3 | min2 | min1 |
| patch ID (pid) | 14 | pid8 | pid7 | pid6 | pid5 | pid4 | pid3 | pid2 | pid1 |
| baro/geo offset (bgo) | 15 | res | bgo7 | bgo6 | bgo5 | bgo4 | bgo3 | bgo2 | bgo1 |
| slot (slt) | 16 | slt8 | slt7 | slt6 | slt5 | slt4 | slt3 | slt2 | slt1 |
| 4-bit longitude offset (lon4), 4-bit latitude offset (lat4) | 17 | lon44 | lon43 | lon42 | lon41 | lat44 | lat43 | lat42 | lat41 |
| UTC second (sec) | 18 | sec6 | sec5 | sec4 | sec3 | sec2 | sec1 |  |  |

Note.— “res” denotes currently unused. “x” denotes part of fixed data field.

Table 3-7. Information field 4 hex — UTC time

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| information field ID | 11 | X | x | x | x | 0 | 1 | 0 | 0 |
| UTC day (day) | 12 | res | res | res | day5 | day4 | day3 | day2 | day1 |
| UTC year (yr) | 13 | yr8 | yr7 | yr6 | yr5 | yr4 | yr3 | yr2 | yr1 |
| UTC hours (h), UTC month (mon) | 14 | h4 | h3 | h2 | h1 | mon4 | mon3 | mon2 | mon1 |
| UTC minute (min) | 15 | res | h5 | min6 | min5 | min4 | min3 | min2 | min1 |
| slot (slt) | 16 | slt8 | slt7 | slt6 | slt5 | slt4 | slt3 | slt2 | slt1 |
| 4-bit longitude offset (lon4), 4-bit latitude offset (lat4) | 17 | lon44 | lon43 | lon42 | lon41 | lat44 | lat43 | lat42 | lat41 |
| UTC second (sec) | 18 | sec6 | sec5 | sec4 | sec3 | sec2 | sec1 |  |  |

Note.— “res” denotes currently unused. “x” denotes part of fixed data field.

Table 3-8a. Information field 8 hex — Two slot TCP

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| information field ID | 11 | x | x | x | x | 1 | 0 | 0 | 0 |
| TCP latitude (lat) | 12 | lat8 | lat7 | lat6 | lat5 | lat4 | lat3 | lat2 | lat1 |
|  | 13 | balt12 | balt11 | balt10 | balt9 | lat12 | lat11 | lat10 | lat9 |
| base altitude (balt) | 14 | balt8 | balt7 | balt6 | balt5 | balt4 | balt3 | balt2 | balt1 |
| longitude (lon) | 15 | lon8 | lon7 | lon6 | lon5 | lon4 | lon3 | lon2 | lon1 |
|  | 16 | ttg6 | ttg5 | lon14 | lon13 | lon12 | lon11 | lon10 | lon9 |
| time to go (ttg)/TCP type (typ) | 17 | ttg4 | ttg3 | ttg2 | ttg1 | typ4 | typ3 | typ2 | typ1 |
| TCP+1 latitude (lat) | 18 | lat8 | lat7 | lat6 | lat5 | lat4 | lat3 | lat2 | lat1 |
|  | 19 | balt12 | balt11 | balt10 | balt9 | lat12 | lat11 | lat10 | lat9 |
| base altitude (balt) | 20 | balt8 | balt7 | balt6 | balt5 | balt4 | balt3 | balt2 | balt1 |
| longitude (lon) | 21 | lon8 | lon7 | lon6 | lon5 | lon4 | lon3 | lon2 | lon1 |
|  | 22 | ttg6 | ttg5 | lon14 | lon13 | lon12 | lon11 | lon10 | lon9 |
| time to go (ttg)/TCP type (typ) | 23 | ttg4 | ttg3 | ttg2 | ttg1 | typ4 | typ3 | typ2 | typ1 |
| TCP+2 latitude (lat) | 24 | lat8 | lat7 | lat6 | lat5 | lat4 | lat3 | lat2 | lat1 |
|  | 25 | balt12 | balt11 | balt10 | balt9 | lat12 | lat11 | lat10 | lat9 |
| base altitude (balt) | 26 | balt8 | balt7 | balt6 | balt5 | balt4 | balt3 | balt2 | balt1 |
| longitude (lon) | 27 | lon8 | lon7 | lon6 | lon5 | lon4 | lon3 | lon2 | lon1 |
|  | 28 | ttg6 | ttg5 | lon14 | lon13 | lon12 | lon11 | lon10 | lon9 |
| time to go (ttg)/TCP type (typ) | 29 | ttg4 | ttg3 | ttg2 | ttg1 | typ4 | typ3 | typ2 | typ1 |
| TCP+3 latitude (lat) | 30 | lat8 | lat7 | lat6 | lat5 | lat4 | lat3 | lat2 | lat1 |
|  | 31 | balt12 | balt11 | balt10 | balt9 | lat12 | lat11 | lat10 | lat9 |
| base altitude (balt) | 32 | balt8 | balt7 | balt6 | balt5 | balt4 | balt3 | balt2 | balt1 |
| longitude (lon) | 33 | lon8 | lon7 | lon6 | lon5 | lon4 | lon3 | lon2 | lon1 |
|  | 34 | ttg6 | ttg5 | lon14 | lon13 | lon12 | lon11 | lon10 | lon9 |
| time to go (ttg)/TCP type (typ) | 35 | ttg4 | ttg3 | ttg2 | ttg1 | typ4 | typ3 | typ2 | typ1 |
| call sign left (csl) | 36 | csl 8 | csl 7 | csl 6 | csl 5 | csl 4 | csl 3 | csl 2 | csl1 |
|  | 37 | csl 16 | csl 15 | csl 14 | csl 13 | csl 12 | csl 11 | csl 10 | csl9 |
|  | 38 | res | res | res | csl 21 | csl 20 | csl 19 | csl 18 | csl17 |
| call sign right (csr) | 39 | csr8 | csr 7 | csr 6 | csr 5 | csr 4 | csr 3 | csr 2 | csr1 |
|  | 40 | csr16 | csr 15 | csr 14 | csr 13 | csr 12 | csr 11 | csr 10 | csr 9 |
| status (st) | 41 | st3 | st2 | st1 | csr 21 | csr 20 | csr 19 | csr 18 | csr 17 |
| current patch ID (pid) | 42 | pid8 | pid7 | pid6 | pid5 | pid4 | pid3 | pid2 | pid1 |
| 6-bit latitude offset (lat6) | 43 | pid10 | pid9 | lat66 | lat65 | lat64 | lat63 | lat62 | lat61 |
| rate uncertainty (nucr), 6-bit longitude offset (lon6), baro rate/geo rate (br/gr) | 44 | altr9 | br/gr | lon66 | lon65 | lon64 | lon63 | lon62 | lon61 |
| altitude rate (altr) | 46 | altr8 | altr7 | altr6 | altr5 | altr4 | altr3 | altr2 | altr1 |
| aircraft category (ac) | 46 | nucr3 | nucr2 | nucr1 | ac5 | ac4 | ac3 | ac2 | ac1 |
| ground speed (gs) | 47 | gs8 | gs7 | gs6 | gs5 | gs4 | gs3 | gs2 | gs1 |
| ground track (gt) | 48 | gs11 | gs10 | gs9 | gt5 | gt4 | gt3 | gt2 | gt1 |
|  | 49 | gt11 | gt10 | gt9 | gt8 | gt7 | gt6 | res | res |

Note.— “res” denotes currently unused. “x” denotes part of fixed data field.

Table 3-8b. Information field 9 hex — Single slot TCP

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| information field ID | 11 | x | x | x | x | 1 | 0 | 0 | 1 |
| base altitude (balt) | 12 | balt8 | balt7 | balt6 | balt5 | balt4 | balt3 | balt2 | balt1 |
| TCP number (no) | 13 | balt12 | balt11 | balt10 | balt9 | no2 | no1 | pid10 | pid9 |
| patch ID (pid) | 14 | pid8 | pid7 | pid6 | pid5 | pid4 | pid3 | pid2 | pid1 |
| latitude (lat) | 15 | lat8 | lat7 | lat6 | lat5 | lat4 | lat3 | lat2 | lat1 |
| longitude (lon) | 16 | lat12 | lat11 | lat10 | lat9 | lon14 | lon13 | lon12 | lon11 |
|  | 17 | lon10 | lon9 | lon8 | lon7 | lon6 | lon5 | lon4 | lon3 |
| time to go (ttg) | 18 | ttg6 | ttg5 | ttg4 | ttg3 | ttg2 | ttg1 |  |  |

Note.— “res” denotes currently unused. “x” denotes part of fixed data field.

Table 3-9. Information field A1 hex — Aircraft data

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| information field ID | 11 | x | x | x | x | 1 | 0 | 1 | 0 |
| aircraft category (ac) | 12 | 0 | 0 | 0 | 1 | ac4 | ac3 | ac2 | ac1 |
| status (st) | 13 | ac5 | st3 | st2 | st1 | csl 12 | csl 11 | csl 10 | csl9 |
| call sign left (csl) | 14 | csl 8 | csl 7 | csl 6 | csl 5 | csl 4 | csl 3 | csl 2 | csl1 |
|  | 15 | csl 20 | csl 19 | csl 18 | csl17 | csl 16 | csl 15 | csl 14 | csl 13 |
| call sign right (csr) | 16 | csl 21 | csr 7 | csr 6 | csr 5 | csr 4 | csr 3 | csr 2 | csr1 |
|  | 17 | csr 15 | csr 14 | csr 13 | csr 12 | csr 11 | csr 10 | csr 9 | csr8 |
|  | 18 | csr 21 | csr 20 | csr 19 | csr 18 | csr 17 | csr16 |  |  |

Table 3-10. Information field AA0 hex — High resolution

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| information field ID | 11 | x | x | x | x | 1 | 0 | 1 | 0 |
|  | 12 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |
| rate uncertainty (nucr) | 13 | res | nucr3 | nucr2 | nucr1 | Gs12 | gs11 | gs10 | gs9 |
| ground speed (gs) | 14 | gs8 | gs7 | gs6 | gs5 | Gs4 | gs3 | gs2 | gs1 |
| 8-bit longitude offset (lon8) | 16 | lon88 | lon87 | lon86 | lon85 | Lon84 | lon83 | lon82 | lon81 |
| 8-bit latitude offset (lat8) | 17 | lat88 | lat87 | lat86 | lat85 | Lat84 | lat83 | lat82 | lat81 |
| ground track (gt) | 18 | gt8 | gt7 | gt6 | gt5 | Gt4 | gt3 | gt2 | gt1 |
| turn indication (tind) | 18 | gt12 | gt11 | gt10 | gt9 | tind2 | tind1 |  |  |

Note.— “res” denotes currently unused. “x” denotes part of fixed data field.

The values of the information field subfields shall be as defined in Table 3-11.

Table 3-11. Information field encoding (variable data field)

| Subfield | Range | Encoding | Notes |
| --- | --- | --- | --- |
| rate navigation uncertainty category (nucr) | 0-4 | Values 0, 1, 2, 3, 4 in accordance with the five nucr categories specified for ADS-B MASPS by RTCA/DO-242 |  |
| 4-bit latitude (lat4) | - | A high-resolution component to enhance the 12-bit low-resolution encoding transmitted in the fixed part (see Table 1-66). Encoding of this high-resolution component is described in Section 4.6 |  |
| 6-bit latitude (lat6) | - | See note above |  |
| 8-bit latitude (lat8) | - | See note above |  |
| 4-bit longitude (lon4) | - | A high-resolution component to enhance the 14-bit low-resolution encoding transmitted in the fixed part (see Table 1-66). is described in Section 4.6 |  |
| 6-bit longitude (lon6) | - | See note above |  |
| 8-bit longitude (lon8) | - | See note above |  |
| baro/geo offset (bgo) | 0-127 | bgo = barometric - geometric altitude Encoding as in Table 3-12 below |  |
| baro rate/geo rate (br/gr) | Binary | 0 = altitude rate is barometric altitude rate 1 = altitude rate is geometric altitude rate |  |
| altitude rate (altr) | -32 100 fpm to +32 100 fpm | Bit altr9 encodes the sign of altitude rate of change with 0 = climb and 1 = descend. altr9 shall be set to 0 if the magnitude of altitude rate is unknown Bits altr8 ... altr1 encode the magnitude of altitude rate of change as specified in Table 3-14. |  |
| ground speed (gs) | 0 to (11 256 knots | Encoding as in Table 3-13 | Range is 0 to 3069 knots for 11 bits and 0 to 11 256 for 12 bits. Resolution steps from 1 knot to 4 knots. Note that bit 12 is only available in the high dynamic variable part. |
| ground track (gt) | 0° to 359.912° | due North ± ½N+1 degrees coded as 0 and decoded as due North Resolution is 360/2N degrees | Ground track is the same as true track. N is the number of bits (either 11 or 12) assigned in the variable field for ground track. |
| turn indication (tind) | 0 – 3 | 0 = Unknown, 1 = Left, 2 = Right and 3 = Straight | The threshold between straight and turning is an operational issue that will be specified elsewhere. |
| patch ID (pid) | - | Encoding is described in Section 4.8 |  |
| TCP type (typ) | 0 – 15 | Reserved for future definition |  |
| UTC year (yr) | 1-255 | current year - 1970, 0= N/A |  |
| UTC month (mon) | 1-12 | integer months |  |
| UTC day (day) | 1-31 | integer days, 00= N/A |  |
| UTC hours (h) | 0-23 | integer hours |  |
| UTC minute (min) | 0 to 59 | integer minutes |  |
| UTC second (sec) | 0 to 60 | integer seconds | Seconds run up to 60 to allow for leap seconds |
| slot (slt) | 0 to 255 | integer slots, 0 indicates the first slot in the second frame |  |
| TCP number (no) | 0 – 3 | 0 = current 1 = next 2 = next + 1 3 = next + 2 |  |
| TCP time to go (ttg) | 0 – 63 | Indicates the time to reach the indicated TCP from either the current position (no – 0) or from the previous TCP (no = 1, 2 or 3). Encoding as in Table 3-17 |  |
| call sign left (csl), call sign right (csr) |  | Encoding for call sign: 1) Call sign shall be left justified 2) Only valid characters are A-Z, 0 – 9 and null: Assign A- Z = 0 – 25, 0 – 9 = 26 – 35, null = 36 3) Call sign shall be an eight character string “c1, c2, c3, c4, c5, c6, c7, c8” 4) csl = c1 373 + c2 372 + c3 37 + c4 5) csr = c5 373 + c6 372 + c7 37 + c8 |  |
| aircraft category (ac) | 0 – 31 | Encoding as in Table 3-15 |  |
| status (st) | 0 – 7 | Encoding as in Table 3-16 |  |

For information field 9 hex, TCP, the encoding of the base altitude (balt) shall be as defined in Table 1-68 and the patch ID, latitude and longitude subfields shall be encoded as described in Section  4, except that the lowest two bits of the longitude subfield shall be omitted from the transmission and assumed equal to 01 binary.

Note.— For TCP transmission, position encoding shall use the Patch ID encoding described in Section  4.8. The longitude subfield is truncated by two bits. This means that the available resolution will be +/- 150m except at high latitudes where the resolution will increase to +/- 450m.

The encoding of the baro/geo offset subfield shall be as defined in Table 3-12.

Table 3-12. Baro/geo offset encoding (variable data field)

| Barometric/geometric altitude offset of transmitting station (ft) | Transmitted value of bgo | Decoded offset (ft) |
| --- | --- | --- |
| base alt ( 24 012.5 | 24 012.5 < base alt |  | base alt ( 24 012.5 | 24 012.5 < base alt |
| bgo < -2 075 | bgo < -5 050 | 1 | < -2 075 | < -5 050 |
| -2 075 ( bgo < -2 025 | -5 050 ( bgo < -4 950 | 2 | -2 050 | -5 000 |
| -2 025 ( bgo < -1 975 | -4 950 ( bgo < -4 850 | 3 | -2 000 | -4 900 |
| -1 975 ( bgo < -1 925 | -4 850 ( bgo < -4 750 | 4 | -1 950 | -4 800 |
| -1 925 ( bgo < -1 875 | -4 750 ( bgo < -4 650 | 5 | -1 900 | -4 700 |
| -1 875 ( bgo < -1 825 | -4 650 ( bgo < -4 550 | 6 | -1 850 | -4 600 |
| ( | ( | ( | ( | ( |
| 3 975 ( bgo < 4 025 | 7 050 ( bgo < 7 150 | 123 | 4 000 | 7 100 |
| 4 025 ( bgo < 4 075 | 7 150 ( bgo < 7 250 | 124 | 4 050 | 7 200 |
| 4 075 ( bgo < 4 125 | 7 250 ( bgo < 7 350 | 125 | 4 100 | 7 300 |
| bgo ( 4 125 | bgo ( 7 350 | 126 | > 4 125 | > 7 350 |
| reserved | 127 | error |
| offset unknown | 0 | offset unknown |

Note.— The encoding of the ground speed subfield shall be as defined in Table 3-13.

Table 3-13. Ground speed encoding (variable data field)

| Actual speed over ground of transmitting station (knots) | Transmitted value of gs (decimal equivalent of field) | Decoded speed over ground (knots) |
| --- | --- | --- |
| unknown | 0 | unknown |
| 0 ( speed < 0.5 | 1 | 0 |
| 0.5 ( speed < 1.5 | 2 | 1 |
| 1.5 ( speed < 2.5 | 3 | 2 |
| 2.5 ( speed < 3.5 | 4 | 3 |
| 3.5 ( speed < 4.5 | 5 | 4 |
| ( | ( | ( |
| 1 021.5 ( speed < 1 022.5 | 1 023 | 1 022 |
| 1 022.5 ( speed < 1 024 | 1 024 | 1 023 |
| 1 024 ( speed < 1 026 | 1 025 | 1 025 |
| 1 026 ( speed < 1 028 | 1 026 | 1 027 |
| ( | ( | ( |
| 3 068 ( speed < 3 070 | 2 047 | 3 069 |
| 3 070 ( speed < 3 074 | 2 048 | 3 072 |
| 3 074 ( speed < 3 078 | 2 049 | 3 076 |
| 3 078 ( speed < 3 082 | 2 050 | 3 080 |
| ( | ( | ( |
| 11 250 ( speed < 11 254 | 4 093 | 11 252 |
| 11 254 ( speed < 11 258 | 4 094 | 11 256 |
| 11 258 ( speed | 4 095 | more than or equal to 11 258 |

Note.— The time over which the ground speed is computed is station dependent.

The encoding of the magnitude part of the altitude rate subfield (bits 1 to 8) shall be as defined in Table 3-14.

Table 3-14. Altitude rate magnitude encoding and decoding

| Actual altitude rate of transmitting station (fpm) | Transmitted decimal value of altr8 ... altr1 | Decoded magnitude of altitude rate (fpm) |
| --- | --- | --- |
| unknown | 0 | unknown |
| ¦arate¦ < 50 | 1 | 0 |
| 50 ( ¦arate¦ < 150 | 2 | 100 |
| 150 ( ¦arate¦ < 250 | 3 | 200 |
| 250 ( ¦arate¦ < 350 | 4 | 300 |
| ( | ( | ( |
| 19 950 ( ¦arate¦ < 20 050 | 201 | 20 000 |
| 20 050 ( ¦arate¦ < 20 300 | 202 | 20 200 |
| 20 300 ( ¦arate¦ < 20 500 | 203 | 20 400 |
| ( | ( | ( |
| 29 900 ( ¦arate¦ < 30 100 | 251 | 30 000 |
| 30 100 ( ¦arate¦ < 30 500 | 252 | 30 250 |
| 30 500 ( ¦arate¦ < 31 000 | 253 | 30 750 |
| 31 000 ( ¦arate¦ < 32 000 | 254 | 31 500 |
| 32 000 ( ¦arate¦ | 255 | more than or equal to 32 000 |

Note.— The quantization step size of altr (100 fpm) is equivalent to a one sigma error of 0.5 fps.

The encoding of the aircraft category subfield shall be as defined in Table 3-15.

Table 3-15. Aircraft category encoding

| Encoded value | Aircraft/vehicle category | Comments |
| --- | --- | --- |
| 0 | light a/c | 7000 kgs (15500 lbs) or less |
| 1 | reserved |  |
| 2 | medium a/c | more than 7000 kgs (15500 lbs) and less than 136000 kgs (300000 lbs) |
| 3 | reserved |  |
| 4 | heavy a/c | 136000 kgs (300000 lbs) or more |
| 5 | highly manoeuvrable and high speed | >5g acceleration capability and >400 knots |
| 6, 7, 8 | reserved |  |
| 9 | rotorcraft |  |
| 10 | glider/sailplane |  |
| 11 | lighter than air |  |
| 12 | unmanned aerial vehicle |  |
| 13 | space/transatmospheric vehicle |  |
| 14 | ultra -light/hang-glider/ para -glider |  |
| 15 | parachutist/skydiver |  |
| 16, 17, 18 | reserved |  |
| 19 | surface vehicle — emergency vehicle |  |
| 20 | surface vehicle — service vehicle |  |
| 21 | fixed ground or tethered obstruction |  |
| 22, 23 | reserved |  |
| 24, 25, 26, 27, 28, 29, 30 | reserved |  |
| 31 | unknown |  |

The encoding of the aircraft status subfield shall be as defined in Table 3-16.

Table 3-16. Aircraft status (emergency/priority status) encoding

| Encoded value | Status |
| --- | --- |
| 0 | no emergency/not reported |
| 1 | general emergency |
| 2 | lifeguard/medical |
| 3 | minimal fuel |
| 4 | no communications |
| 5 | unlawful interference |
| 6, 7 | reserved |

The encoding of the time to go (ttg) subfield shall be as defined in Table 3-17.

Table 3-17. Time to go subfield encoding

| Actual time to go (minutes) | Transmitted decimal value of ttg | Decoded magnitude of time to go (minutes) |
| --- | --- | --- |
| unknown | 0 | No time to go information available |
| time to go < 0.125 | 1 | 0 |
| 0.125 ( time to go < 0.375 | 2 | 0.25 |
| 0.375 ( time to go < 0.625 | 3 | 0.5 |
| ( | ( | ( |
| 15.125 ( time to go < 15.375 | 62 | 15.25 |
| 15.375 ( time to go | 63 | more than or equal to 15.375 |

ADS-B REQUEST

ADS-B request format

To request that a station transmit an ADS-B report consisting of a synchronization burst , a station shall transmit a general request burst with r-mi1 = 0, and shall include the auxiliary information as shown in Tables 3-18, 3-19 and 3-20, as appropriate given the values of the sleep and auto bits in octet 6. The  information subfields shall be encoded according to Table 3-21. Parameter blocks shall be included only if the respective parameter flag bit is 1 and shall be included in the order (most significant to least significant) of the parameter flag bits. The parameter flag sub-field shall consist of bits 8 through 3 of octet 6.

Sleep mode

If the requesting station desires the responding station to respond at one specified rate as a default, but a different specified rate in the event certain position or velocity deviation thresholds are exceeded, the requesting station shall set the sleep bit = 1 and octets 7-8 in Table 3-19 shall be sent. Otherwise, the sleep bit shall be set = 0 and octets 7-8 in Table 3-19 shall not be sent.

Note.— The default reporting rate is defined by the reservation data. The contingency reporting rate, in the event that certain position or velocity deviation thresholds are exceeded, is defined by the snr field described here.

Automatic selection of variable information fields

If the requesting station desires the responding station to respond with synchronization burst variable parts selected autonomously by the responding station, the requesting station shall set the auto bit = 0 and octet k in Table 3-20 shall not be sent. Otherwise, the station shall set the auto bit = 1 and the desired variable part ID shall be encoded as indicated in Table 3-20.

Note 1.— The value of k = 7 if the sleep bit = 0 (implying that the auxiliary information for sleep mode is not transmitted), and is 9 if the sleep bit = 1.

Note 2.— The r-id field, which is variable-length, should be encoded in the minimum length allowed. Then, for r-id selections supported within 4 bits, the parameter set enabled by the auto bit fits in a single octet and the overall ADS-B request, with sleep parameters and requested variable part identification, fits in a single message of length = 20 octets.

Table 3-18. ADS-B request bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| r-mi1 (bit 8 = 0), burst ID | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| autonomous monitoring (sleep), autonomous information (auto), requested base altitude (r-b/a), auxiliary information (aux) auxiliary information as required | 6 7 to m | sleep | auto | res | res | res | res | r-b/a2 | r-b/a1 |
|  |  |  | see Tables 3-19 and 3-20 |  |  |

Table 3-19. ADS-B request bit encoding for sleep mode parameters when sleep bit = 1

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| secondary reporting rate (snr), maximum sleep velocity (vel) | 7 | snr4 | snr3 | snr2 | snr1 | vel4 | vel3 | vel2 | vel1 |
| maximum sleep position (pos) | 8 | pos8 | pos7 | pos6 | pos5 | pos4 | pos3 | pos2 | pos1 |

Table 3-20. ADS-B request bit encoding for auto parameters when auto bit = 1

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| length (lg), auxiliary data (aux), requested information field ID (r-id) (included if auto = 0)* | k | lg2 | lg1 | aux2 | aux1 | r-id4 | r-id3 | r-id2 | r-id1 |

* The r-id field may continue into additional octets depending on the variable part requested.

Table 3-21. ADS-B request field encoding

| Subfield | Range | Encoding | Out of Scale | Notes |
| --- | --- | --- | --- | --- |
| sleep | Boolean | 0 = no sleep mode; 1 = sleep mode | n/a | if 1, additional information describing sleep mode parameters is provided as a first additional information subfield starting in octet 7. |
| autonomous information (auto) | Boolean | 0 = autonomously select transmitted information field 1 = provide requested information field only | n/a | if 1, additional information describing requested information is provided as an additional information subfield starting in octet 7 (if sleep = 0 implying lack of sleep mode parameters), or octet 9 (if sleep = 1). |
| requested information ID (r-id) | Binary; variable length | See Table 3-2 | A value not contained in Table 3-2. | Requests the information field identity contained in the variable data field |
| maximum sleep velocity (vel) | 1 to 15 knots | integer knots | 0= ignore |  |
| maximum sleep position (pos) | 1 to 255 metres | integer metres | 0= ignore |  |
| secondary reporting rate (snr) | same as nr | n/a | n/a |  |
| parameter group length (lg) | 0 – 3 | Binary | n/a | Indicates number of additional octets in parameter group (e.g., a parameter group comprising a single octet is encoded as 0) |
| auxiliary parameters (aux) | 0 – 3 | If r-id = 0 or 1, then: 00 = baro rate; 01 = geo rate 10 = reserved 11 = don’t care. If r-id = 9hex, then: 00 = current TCP; 01 = next TCP, 10 = next + 1 TCP, 11 = next + 2 TCP. | Error if r-id and aux pairing is not listed as a valid encoding in this table. | Interpretation depends on value of r-id field. Unassigned values are reserved. If r-id  {0, 1, 9}hex, aux = 00. |
| requested base altitude (r-b/a) | 0 – 3 | 0 = report either barometric or geometric 1 = report barometric or, if not available, report geometric 2 = report geometric or, if not available, report barometric 3 = reserved for future use |  |  |

Note 3.— As an example, an ADS-B request for an aircraft off the airport movement area, which is stopped, could potentially be sent with the encoding of Table 3-22. This encoding imposes sleep mode with wakeup parameters vel = 4 kts and pos = 10 m, and requests the high-resolution variable part. The snr field indicates that the station should transmit once per second in the event that the velocity or position deviation thresholds are exceeded.

Table 3-22. Example ADS-B request bit encoding for sleep mode with request for high-precision variable part

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| r-mi1 (bit 8 = 0), burst ID | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| autonomous monitoring (sleep), autonomous information (auto), requested base altitude (r-b/a) | 6 | sleep (1) | auto (1) | res (0) | res (0) | res (0) | res (0) | r-b/a2 | r-b/a1 |
| secondary reporting rate (snr), maximum sleep velocity (vel) | 7 | snr4 (1) | snr3 (1) | snr2 (0) | snr1 (1) | vel4 (0) | vel3 (1) | vel2 (0) | vel1 (0) |
| maximum sleep position (pos) | 8 | pos8 (0) | pos7 (0) | pos6 (0) | pos5 (0) | pos4 (1) | pos3 (0) | pos2 (1) | pos1 (0) |
| requested information field ID (r-id) (included if auto = 0) | 9 | lg2 (0) | lg1 (0) | aux2 (0) | aux1 (0) | r-id4 (1) | r-id3 (0) | r-id2 (1) | r-id1 (0) |

DEFAULT ADS-B REPORTING

In the absence of an ADS-B request from a peer station or a request from the ADS-B application in the station, the station shall transmit at least 12 synchronization bursts per minute averaged over the two GSCs.

ADS-B PROCEDURES

A station issuing an ADS-B request (see Section C.4) shall set the auto bit to 0 and include the r-id field when requesting a specific information field. A requesting station shall set the auto bit to 1 and not include the r-id field when it desires that the responding unit determine which information field is the most important at any point in time. The sleep bit shall be set to 0 when requesting a single response (e.g. via a unicast request reservation); the vel, pos and rate fields shall be included in the transmitted request and ignored by the receiving station when the sleep bit is set to 0. A station requesting the time synchronization information field (information field ID 2) shall only transmit a request to a station that has announced that it is operating with a primary time source (tfom = 0 or 1).

A requesting station shall set the sleep bit to 1 when it wants the responding station to transmit a synchronization burst in directed slots at one rate, but transmit at a higher rate under certain circumstances. If the sleep bit is set to 1, a station shall monitor its position and velocity to determine if the station has exceeded either of two thresholds: (a) moving more than pos metres from the position reported in the last directed report or (b) moving more than vel knots. If pos is zero, then the position test shall be ignored. If vel is zero, then the velocity test shall be ignored. A station which exceeded either the position or velocity threshold, shall begin to transmit autonomously using the incremental broadcast procedures until one of the following occurs:

a)	it receives a directed request reservation for the frequency on which it is transmitting autonomously with the or bit set to 1 (both the autonomous incremental transmissions and the directed periodic transmissions shall be affected);

b)	it is transmitting autonomous synchronization bursts because it exceeded the position threshold, but not the velocity threshold, and it subsequently transmitted a directed synchronization burst (in this case, the station shall not make an incremental reservation past the slot in which it will transmit the directed synchronization burst);

c)	it is transmitting autonomous synchronization bursts because it exceeded the velocity threshold, and it subsequently transmitted a directed synchronization burst after its velocity had subsided below the threshold.

Note.— Note that the procedures for sleep mode apply to vertical as well as horizontal movement.

Information fields 0, 1, 2, 3, 4 and AA1 hex shall have priority over other information fields.

A station which is transmitting directed synchronisation bursts which, as part of a regular periodic series of synchronisation bursts, include the two slot TCP variable part defined in Table 3-8a, shall indicate when there is a change to any of its TCPs by setting the TCP change flag (see Section 1.5.2.2) to zero in all directed synchronisation bursts transmitted by the station.

When a mobile has set its TCP change flag to 0, only ground stations shall be allowed to respond by issuing an ADS-B request burst requesting that the mobile transmit a synchronisation burst containing the two slot TCP variable part.

The station shall set the TCP change flag to 1 when it has transmitted updated TCP information using the two slot TCP variable part.

A station which is transmitting directed synchronisation bursts which do not include the two slot TCP variable part in the regular periodic series of synchronisation bursts, shall set the TCP change flag to 1.

CTRL PARAMETERS

Directory of service (DOS) message

Directory of service information shall be transmitted using the CTRL DOS parameter defined in Section 1.5.4.4.2.

The application fields shall be encoded as defined in Table 3-23.

Table 3-23. Encoding of application fields

| Encoding (decimal equivalent) | Implied meaning |
| --- | --- |
| 0 | ADS-B |
| 1 | TIS-B |
| 2 | Secondary navigation capability |
| 3 | FIS-B |

The service information (si) field for service information type (sit) field equal to hex 00 shall be as defined in Table 3-24.

Table 3-24. Encoding of service information field for sit = hex 00

| Service information (si) field bit number | Service | Equivalent application field (see Table 3-23) |
| --- | --- | --- |
| 1 | ADS-B | 0 |
| 2 | TIS-B | 1 |
| 3 | Secondary navigation capability | 2 |
| 4 | FIS-B | 3 |
| 5 - 8 | reserved |  |

Channel management CTRL Parameter

The channel management CTRL parameter shall be divided into component blocks as described in Table 3-25. A station that matches a destination ID in a channel management CTRL parameter, or is contained in a defined region in a channel management CTRL parameter, shall not process subsequent channel management CTRL parameters with the same command set ID in the same CTRL.  A station receiving a channel management CTRL parameter with a script that matches an active command set shall update the script duration but otherwise not modify its transmissions.

Note.- If the destination block is an implied broadcast (dc = 0 per Table 3-27), it is considered to match the receiving station’s ID.

Table 3-25. Component blocks of channel management CTRLparameter

| Blocks | Description |
| --- | --- |
| Header block | Contains the CTRL header and the non-repetitive information for each of the sub-elements. |
| Destination block | Contains a list of zero or more destinations or a geographic region, along with the timeout and slot offset from the current slot to the start of the script (zero destinations included implies broadcast.) |
| Transmission definition block | Contains from 0 to 15 transmission definitions in an unordered list. Each definition describes a particular desired transmission (one not already specified in SARPs) and all relevant options. The location of a particular transmission block in this list defines an implicit pointer used in the script block (i.e., thereby specifying a particular message). |
| Frequency block | Contains from 1 to 7 frequencies in an ordered list and optional sleep parameters to use on each frequency. The location of a particular frequency block in this list defines an implicit pointer used in the script block (i.e., thereby specifying a particular frequency). |
| Parameter block | Contains QoS and other transmission parameters to use with the elements of this script. |
| Script block | Contains a repeat rate and from 1 to N script elements in an ordered list. Each script element consists of an optional repeat count, a frequency block pointer, and a transmission block pointer. |

Header block encoding

The channel management CTRL parameter header block shall be encoded as defined in Table 3-26 with subfield encodings as defined in Table 3-27.

Table 3-26. Header block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| CTRL parameter ID | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 |
| CTRL length | 2 | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |
| directed timeout (dt) | 3 | dt4 | dt3 | dt2 | dt1 | do12 | do11 | do10 | do9 |
| directed offset (do) | 4 | do8 | do7 | do6 | do5 | do4 | do3 | do2 | do1 |
| destination count (dc) | 5 | dc8 | dc7 | dc6 | dc5 | dc4 | dc3 | dc2 | dc1 |
| command set ID (csid), transmission definition count (tc) | 6 | csid4 | csid3 | csid2 | csid1 | tc4 | tc3 | tc2 | tc1 |
| frequency count (fc), script duration type (styp), script rate (sr) | 7 | fc3 | fc2 | fc1 | styp | sr4 | sr3 | sr2 | sr1 |
| transmit parameter count (pc) | 8 | res | res | pc6 | pc5 | pc4 | pc3 | pc2 | pc1 |
| script count (sc) | 9 | sc8 | sc7 | sc6 | sc5 | sc4 | sc3 | sc2 | sc1 |

If the channel management parameter is included within a GSIF DLPDU with the ucid subfield set to 2, the channel management parameter ID shall be omitted and no other parameter included in the GSIF.

Table 3-27. Header block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| directed timeout (dt) | See Table 1-35 |  |
| directed offset (do) | 0 or 2 to 212 – 1 do = 1: invalid | do = 0 implies directed rate reservation. do >1 implies directed slot reservation. For do >1, do = the first slot in which to transmit. |
| destination count (dc) | 0-255 | Number of bytes in the destination block. 0 implies broadcast. |
| command set ID (csid) | 0-14 : valid csid identifiers 15 : cancel all prior commands | ID specifying this command (See Note 1) |
| transmission definition count (tc) | 0-15 | The number of elements in the transmission definition block. |
| frequency count (fc) | 0 : no freq listed (csid = 15) 1-7 : number of frequencies | The number of elements in the frequency block. |
| script duration type (styp) | styp = 0: interpret sr as the number of times the entire script repeats per minute; styp = 1: interpret sr as the number of minutes until script repeats. |  |
| script rate (sr) | 0-15. Interpreted based on styp. For styp = 0, sr is encoded per Table 1-33. For styp = 1, sr is encoded as minutes between 2 (encoded as 0) and 17 minutes. |  |
| script count (sc) | 1 (encoded as 0) – 256 | Number of bytes in script block. |
| transmit parameter count (pc) | 0 - 63 | Number of bytes in the transmit parameter block. |

Note 1.- The command set ID allows a ground station to uplink several (up to 15) separate commands to each aircraft or set of aircraft (including all aircraft in view) which are each processed separately.  A transmission with csid = x overrides operations specified in a previous transmission with csid = x, but does not affect operations dictated by previous transmissions with csid ( x.  Hence a ground station can command multiple sets of messages (each set containing various types of transmissions), and the transmissions can have different report periods from one set to another.  An example is a sequence of sync bursts on two or more frequencies defined by command set csid = 0, and a separate sequence of TCPs on the same or different frequency(ies) defined by command set csid = 1.   The use of different command sets allows directed-slot operation for both command sets even though the two sets of commanded transmissions may have different burst lengths (e.g., one slot for sync bursts and two slots for TCPs).

The number of elements in the script (total number of transmissions over one repeat cycle) shall be designated NES.  The number of transmissions per minute shall be designated NTM.  A repeat cycle can be less than a sub-multiple of one minute, exactly one minute, or multiple minutes.

Note 2.- The NES  can be greater than sc because of the repeat capability.

Note 3.- The length of a single channel management CTRL parameter is limited to 255 bytes because a single byte length field is used in the CTRL parameter format.

Destination block encoding

The destination block shall consist of zero destinations (a broadcast), one or more addressed destinations, or a regional definition, as defined in the following sections.

Broadcast destination

If the destination count (dc) in the header block is zero, then the channel management CTRL parameter shall apply to all stations.

Addressed destination

If bit 8 of octet 1 of the destination block is a zero, then the destination block shall consist of one or more addresses per Table 3-28 with encodings defined in Table 3-29.  If none of the addresses matches the receiver, then further processing of this parameter shall terminate.

# Note.- The individual offset for the first destination is limited to 0-15 and not 0-31.

Table 3-28. Addressed destination block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| individual offset (ido) | 1 | ido5 | ido4 | ido3 | ido2 | ido1 | d27 | d26 | d25 |
| destination address (d) | 2 | d24 | d23 | d22 | d21 | d20 | d19 | d18 | d17 |
|  | 3 | d16 | d15 | d14 | d13 | d12 | d11 | d10 | d9 |
|  | 4 | d8 | d7 | d6 | d5 | d4 | d3 | d2 | d1 |

Table 3-29. Addressed destination block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| individual offset (ido) | Per Section 1.4.2.1 |  |
| destination address (d) | 0-31 | See description of usage below. |

Directed rate operations

If the directed offset is set equal to 0, then the addressed stations shall operate in directed rate mode. The individual offset parameter ido shall be set to 0 on transmit for each addressed station.

All stations that are not individually addressed shall operate in directed rate mode.

Directed slot operations

If the directed offset is not set equal to 0, then the addressed stations shall operate in directed slot mode. The individual offset parameter ido for each addressed station shall be set to the number of slots by which the transmissions of that station are to be offset from do after the first slot of the CTRL command.

A station transmitting a channel management CTRL parameter for which the directed offset is not set equal to 0 shall first ensure that the slots which will be used by addressed stations have first been reserved using block reservation protocols (see section 1.3.17) or ground quarantine (see section 1.3.6.4).

Note.- Directed slot operation is announced by setting bit 1 of octet 1 of the transmitted burst = 1.

Regional multicast

If bit 8 of octet 1 of the destination block is a one, then the destination block shall consist of a regional multicast per Table 3-30 with encodings defined in Table 3-31.  Stations operating in directed-slot mode shall not process regional multicast commands. A station shall determine that it is in the defined region if Condition 1 is true and either Condition 2a or Condition 2b is true:

Condition 1: altitude compliance

- the station altitude (using baro altitude if available, otherwise geo altitude) is greater than or equal to the lower altitude and less than or equal to the upper altitude

Condition 2a: radial range compliance when there is at least one vertex k with radial k less than or equal to the station’s radial from the center of the defined region

- the station distance from the center of the region, assuming a spherical Earth, is less than or equal to the distance k associated with the vertex k having greatest radial k less than or equal to the station’s radial from the center of the defined region, or

Condition 2b: radial range compliance when there is no vertex with radial k less than or equal to the station’s radial from the center of the defined region

- the station distance from the center of the region, assuming a spherical Earth, is less than or equal to the distance kvc associated with the last vertex in the list.

If the station is not in the defined region, then further processing of this parameter shall terminate.

Note.- The (radial, range) pairs may be parsed in a clockwise direction around the defined center of the region.  Each range applies at its associated radial, and in a clockwise direction until another radial is encountered.

# Table 3-30. Regional multicast block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| vertex count (vc) | 1 | 0 | res | lon14 | lon13 | vc4 | vc3 | vc2 | vc1 |
| center latitude (lat, lat4) | 2 | lon8 | lon7 | lon6 | lon5 | lon4 | lon3 | lon2 | lon1 |
|  | 3 | lon12 | lon11 | lon10 | lon9 | lat12 | lat11 | lat10 | lat9 |
| center longitude (lon, lon4) | 4 | lat8 | lat7 | lat6 | lat5 | lat4 | lat3 | lat2 | lat1 |
|  | 5 | lon44 | lon43 | lon42 | lon41 | lat44 | lat43 | lat42 | lat41 |
| lower altitude (lalt) | 6 | lalt8 | lalt7 | lalt6 | lalt5 | lalt4 | lalt3 | lalt2 | lalt1 |
| upper altitude (ualt) | 7 | ualt8 | ualt7 | ualt6 | ualt5 | ualt4 | ualt3 | ualt2 | ualt1 |
| vertex 1 | radial 1 (r1) | 8 | r1, 8 | r1, 7 | r1, 6 | r1, 5 | r1, 4 | r1, 3 | r1, 2 | r1, 1 |
|  | distance 1 (d1) | 9 | d1, 8 | d1, 7 | d1, 6 | d1, 5 | d1, 4 | d1, 3 | d1, 2 | d1, 1 |
| vertex 2 (as needed) | radial 2 (r2) | 10 | r2, 8 | r2, 7 | r2, 6 | r2, 5 | r2, 4 | r2, 3 | r2, 2 | r2, 1 |
|  | distance 2 (d2) | 11 | d2, 8 | d2, 7 | d2, 6 | d2, 5 | d2, 4 | d2, 3 | d2, 2 | d2, 1 |

# Table 3-31. Regional multicast block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| Vertex count (vc) | 0: vertex 1 1- 15: vertex 2 to vertex 16 | vertex k corresponds to radial k and distance k |
| center latitude (lat, lat4) | lat, lon, lat4, lon4 are CPR encoded per Section 4. | Sent using type=0, reference position is location of station transmitting this CTRL. |
| center longitude (lon, lon4) |  |  |
| lower altitude (lalt) | 0: alt = -1 500 feet 1: alt = -1 250 feet 2-254: 250ft linear increments up to 63 500 feet 255: no upper limit | Station only matches the broadcast if its altitude (baro if available, otherwise geo) is between lower and upper altitudes. Altitude code 255 is not valid for lower altitude. |
| upper altitude (ualt) |  |  |
| distance (d) | See table 3-32. | Vertex blocks are listed in monotonically increasing radial order (clockwise around center). |
| radial (r) | due North coded as 0. Resolution is 360/256 degrees, linear |  |

# Table 3-32. Vertex distance encoding

| Transmitted value of distance (decimal equivalent of field) | Within region if: |
| --- | --- |
| 0 | distance < 0.5 nmi |
| 1 | distance < 1.0 nmi |
| ( | ( |
| 59 | distance < 29.5 nmi |
| 60 | distance < 30 nmi |
| 61 | distance < 31 nmi |
| ( | ( |
| 89 | distance < 59 nmi |
| 90 | distance < 60 nmi |
| 91 | distance < 62 nmi |
| ( | ( |
| 119 | distance < 118 nmi |
| 120 | distance < 120 nmi |
| 121 | distance < 124 nmi |
| ( | ( |
| 254 | distance < 656 nmi |
| 255 | distance < 660 nmi |

Note. – As indicated in Section 3.7.2.2.2.1, a station that matches the regional broadcast filter operates per the directed rate mechanism.

Channel management parameter reception procedures

Upon receipt of a channel management CTRL command that is determined to apply to the station due to an ID or regional match, the station shall establish NTM streams. If styp = 0, then NTM shall equal NES * nr (where nr is the result of looking up the encoded sr in Table 1-33). If styp = 1, then NTM shall equal NES / (2 + sr). If styp=1 and NES is not a multiple of (2 + sr), then periodic streams cannot be defined according to the indicated script, the message shall be judged invalid, and the entire CTRL parameter shall be discarded without further processing.

The receiving station shall update its reservation table and carry out the actions as specified in Table 3-33. The mth individual offset idom shall correspond to the mth destination address matching that of the receiving station.

Note.- The station is only required to update its reservation table with the reservations that require transmission by the station.  Slot selections by other stations commanded in directed-rate mode are unknown at the time the command is processed.  Reservations for other stations commanded in directed-slot mode are known in principle, but are required to be located in blocked or quarantined slots according to 3.7.2.2.2.2.  Hence there is no operational need to record these reservations at the time the command is processed.

Table 3-33. Action on receipt of a channel management CTRL

| Directed offset (do) | Directed timeout (dt) | Action |
| --- | --- | --- |
| 0 | any | See 1.3.16.5.2. |
| 1 | any | Invalid |
| do > 1 | dt < 15 | Reserve the following slots for the destination to broadcast: for j equal to 0 to 3 and k equal to 0 to NTM - 1, the slots equal to truncate (do + idom + (k * M1/NTM) + j * M1) through (lg + truncate (do + idom + (k * M1/NTM) + j * M1)) after the first slot of the received burst |
| do > 1 | dt = 15 | Reserve the following slots for the destination to broadcast: for k equal to 0 to NTM - 1, the slots equal to truncate (do + idom + (k * M1/NTM)) through (lg + truncate (do + (k * M1/NTM))) after the first slot of the received burst |

Upon receipt of a burst containing an autotune reservation (pr_flag = 0), the station shall update its reservation table  and carry out the actions as specified in Table 1-39.

Response to a channel management CTRL with do = 0

If the directed offset subfield is equal to 0, the responder station shall operate autonomously using the periodic broadcast procedures with the nominal periodic rate (V11) set to NTM in the autotune reservation transmission for the next dt * M1 slots, with the a/d bit set equal to 0. The nominal slots shall be spaced such that the nominal slot for the kth element identified in the script occurs

truncate ((k-1)*M1/NTM) slots

after the nominal slot for the first element identified in the script. The first transmission made in accordance with the received channel management CTRL command shall occur within 4500 slots of the start of the received command.

Response to a channel management CTRL with do > 1

On receipt of an CTRL command with the mth destination address matching that of the receiving station and with the directed offset subfield (do) greater than 1, the responder station shall begin the transmission of the first script element at T0m slots after the first slot of the CTRL command where T0m = do + idom. Subsequent transmission slots shall be spaced such that the slot for the kth element identified in the script occurs

truncate ((k-1)*M1/NTM) slots

after the specified slot for the first element identified in the script. The a/d bit shall be set equal to 1.

Setting of TV11 timer

Upon receipt of a channel management CTRL command the station shall set the TV11 timer (see Section 1.3.10.2.1) equal to the value of the directed timeout (dt) subfield for each of the slots indicated in the CTRL transmission. The responder station shall transmit in each of the reserved slots. Each response burst shall contain the periodic broadcast reservation field with the periodic offset (po) subfield set to 0 and the periodic timeout (pt) subfield set to min(3, TV11-1). After transmission, the timer TV11 shall be decremented. When TV11 reaches zero, the responder shall not transmit a response to the directed request. Upon cessation of directed transmissions, the responder shall resume default autonomous behaviour on the GSCs, reserving new slots as required.

Sharing streams

If styp = 1, then the transmissions in successive minutes shall share streams with those script elements that are NTM (modulo NES) apart.  If all of the elements that share a stream are not transmitted on the same frequency, then the message shall be judged invalid and the entire CTRL parameter shall be discarded. If all of the elements that share a stream are not of the same length, then a basic sync burst shall be transmitted for all elements in that stream.

If a station receives a plea request, it shall use NTM as the default reporting rate for the frequency to construct the plea response.

Cancellation of channel management CTRL command

A station shall cancel a channel management CTRL command with known csid by transmitting a channel management CTRL with the directed timeout subfield set to 15, the directed offset (do) set to the offset from the first slot of the cancellation CTRL to the first slot for which the reservation shall be cancelled, and all other subfields set to the same values as in the original channel management CTRL command to be cancelled.

A station shall cancel the set of all channel management CTRL commands for a station or set of stations by transmitting a channel management CTRL with csid = 15.

A receiving station that is commanded to cancel all reservations for sync burst transmission shall revert to default sync burst operations.

Cancellation of autonomous streams

If the responder was transmitting autonomously the VSS user data for which a channel management CTRL command was received, then it shall cancel its existing reservations in accordance with paragraph 1.3.10.5.9, and operate in accordance with the parameters of the CTRL command.

Command set ID parameter

A station that receives a channel management CTRL parameter with csid = 0 shall terminate any previous default sync burst operations and initiate operations in accordance with the current CTRL parameter.

A station that receives a channel management CTRL parameter with csid matching a previously-received channel management CTRL parameter shall terminate any previous operations commanded by the previous CTRL parameter and initiate operations in accordance with the current CTRL parameter.

A station that does not receive a new CTRL parameter block with csid = 0 within (dt * M1) slots, with dt as specified in the CTRL parameter block with csid = 0, shall revert to default sync burst operations.

A station that receives a new CTRL parameter block with csid = 15 shall cancel all reservations for transmission associated with the previously-received channel management CTRL commands and revert to default sync burst operations.

A station that does not receive a new CTRL parameter block with csid > 0 within (dt * M1) slots, with dt as specified in the CTRL parameter block with csid > 0, shall terminate the operations indicated in the associated CTRL parameter block.

Transmission block encoding

Transmission block definitions in SARPs

The SARPs contain the following ordered list of standard transmission blocks (id = 0 through 15) which can be referenced by id without explicitly describing the referenced formats in the uplink CTRL. If a station receives an XID parameter containing a standard transmission definition (id = 0 through 15) that it does not recognize, it shall transmit a basic sync burst.

Table 3-34. Transmission block definitions in SARPs

| Encoding | Transmission definition |
| --- | --- |
| 0 | Sync burst with baro altitude, no sleep parameters, basic variable field, baro alt rate |
| 1 | Sync burst with geo altitude, no sleep parameters, basic variable field, geo alt rate |
| 2 | Sync burst with baro altitude, no sleep parameters, full position variable field, baro alt rate |
| 3 | Sync burst with baro altitude, no sleep parameters, aircraft data variable field |
| 4 – 15 | reserved |

Transmission block definitions not predefined in SARPs

The CTRL can contain explicit definitions of transmission blocks (i.e., if a desired transmission block is not predefined in Table 3-34).  Zero to fifteen such transmission blocks can be defined in the transmission block definition section (as indicated by the tc field) and shall be encoded as defined in Tables 3-35 and 3-37.

Table 3-35. Sync burst block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Boolean ID (id) | 1 | id4 | id3 | id2 | id1 | aux | b/g | res | 0 |
| ID-extension (if required) | 2 | id14 | id13 | id12 | id11 | id24 | id23 | id22 | id21 |

Table 3-36. Sync burst block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| baro/geo selection (b/g) | b/g = 0: send baro b/g = 1: send geo | If the preferred altitude encoding is not available, then send the other if it is available. |
| variable field ID (and extensions) | Per Table 3-2 | Octet 2 is only included when necessary |
| auxiliary selection (aux) | For those variable fields with a selection (e.g, basic, high dynamic, TCP), send selection = aux. | If the requested data is not available, but the alternate is, then send the alternate. As an example, for the basic variable field, aux=0 means send baro rate. |

If the mobile is travelling greater than 3069 knots (i.e., bit gs12=1), then the mobile shall transmit a high dynamic variable field whenever it otherwise would have transmitted a basic, full position, or high resolution variable field.

Table 3-37. Non-sync burst block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| message ID (mid), more bit (mb) | 1 | mb | mid7 | mid6 | mid5 | mid4 | mid3 | mid2 | mid1 |
| length (len), application specific (app) | 2 | app | app | app | app | len4 | len3 | len2 | len1 |

# Note.– Octets 3 through len+2 are all application specific.

Table 3-38. Non-sync burst block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| application specific data (app) |  | Defined by the application specified by the message ID |
| length (len) | 0-15 | Number of bytes following the length (i.e., an application requiring only 4 bits of parameters would encode a 0 for length) |
| message ID (mid) | Per Table 1-6a |  |
| more bit (mb) | mb = 0: octet 2 not included mb = 1: octet 2 (and possibly more follow) |  |

Whenever the mobile cannot transmit the requested information (either a new message ID, variable field, or other option was defined that the mobile does not understand or the mobile does not have the requested information), then the mobile shall transmit a sync burst with a basic variable field.

Frequency block encoding

Zero to seven frequencies are included in the frequency block section (as indicated by the fc field).  A single frequency shall be encoded as defined in Table 3-39 with subfield encodings as defined in Table 3-40:

# Table 3-39. Frequency block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| flags | 1 | sleep | auto | rcv | res | f12 | f 11 | f 10 | f 9 |
| freq | 2 | f 8 | f7 | f6 | f5 | f4 | f3 | f2 | f1 |

# Table 3-40. Frequency block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| frequency (f) | Per Section 1.3.15.1 |  |
| must receive (rcv) | rcv = 0: reception on this frequency is optional rcv = 1: reception on this frequency is mandatory | As the list is ordered in priority, a station receiving a list with a frequency with rcv=0 before a frequency with rcv=1 shall discard the entire CTRL parameter. |
| sleep and auto | Per section 3.4.3 | If the respective bit is set, then the respective block is appended per Section 3.4.3 |

The list of frequencies is ordered. A station with k available receivers shall monitor the first min(k, number of mandatory frequencies) frequencies in the frequency list.

3.7.2.7.1		Recommendation

A station with spare receivers should monitor the remaining frequencies in the list.

Transmission parameter block definition

The station shall transmit all of the streams defined in the script using the parameters defined in Table 3-41 with subfield encodings as defined in Section 1 for the appropriate variable.  The station shall use the first transmit parameter count (pc) octets from Table 3-41 instead of the default values for those parameters.  If pc is greater than the length of Table 3-41, then the station shall ignore all octets beyond the length.  These parameters shall be ignored for directed slot operations.

Note.– pc would be greater than the length of Table 3-41 if more parameters were added after the software was released.

# Table 3-41. Transmission parameter block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Q1, Q4 | 1 | Q12 | Q11 | res | Q45 | Q44 | Q43 | Q42 | Q41 |
| Q2a | 2 | Q2a8 | Q2a 7 | Q2a 6 | Q2a 5 | Q2a 4 | Q2a 3 | Q2a 2 | Q2a 1 |
|  | 3 | Q2a 12 | Q2a 11 | Q2a 10 | Q2a 9 | Q2b 12 | Q2b 11 | Q2b 10 | Q2b 9 |
| Q2b | 4 | Q2b 8 | Q2b 7 | Q2b 6 | Q2b 5 | Q2b 4 | Q2b 3 | Q2b 2 | Q2b 1 |
| Q2c | 5 | Q2c8 | Q2c 7 | Q2c 6 | Q2c 5 | Q2c 4 | Q2c 3 | Q2c 2 | Q2c 1 |
|  | 6 | Q2c 12 | Q2c 11 | Q2c 10 | Q2c 9 | Q2d 12 | Q2d 11 | Q2d 10 | Q2d 9 |
| Q2d | 7 | Q2d 8 | Q2d 7 | Q2d 6 | Q2d 5 | Q2d 4 | Q2d 3 | Q2d 2 | Q2d 1 |
| TV11min, TV11max | 8 | TV11min4 | TV11min3 | TV11min2 | TV11min1 | TV11max4 | TV11max3 | TV11max2 | TV11max1 |
| V11 | 9 | res | res | V116 | V115 | V114 | V113 | V112 | V111 |
| V12 | 10 | res | V127 | V126 | V125 | V124 | V123 | V122 | V121 |
| VS2 | 11 | res | res | VS26 | VS25 | VS24 | VS23 | VS22 | VS21 |
| VS4 | 12 | res | VS47 | VS46 | VS45 | VS44 | VS43 | VS42 | VS41 |

Script block definition

The channel management CTRL parameter script shall be encoded as defined in Table 3-42 with subfield encodings as defined in Table 3-43.

# The script block shall contain one or more script elements. There are two types of script elements as defined in Table 3-42. A transmitting station shall not transmit a script block with two consecutive octets having bits 6-8 equal to “111”. A receiving station shall discard a channel management CTRL command containing a script block with two consecutive octets having bits 6-8 equal to “111”.

# Table 3-42. Script block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| freq index (frq), transmission definition index (txd) | 1 | frq3 | frq2 | frq1 | nsd | txd4 | txd3 | txd2 | txd1 |
|  |  |  |  |  | or |  |  |  |  |
| repeat count (rpt) | 1 | 1 | 1 | 1 | rpt5 | rpt4 | rpt3 | rpt2 | rpt1 |
| freq index (frq), non-standard definition (nsd), transmission definition index (txd) | 2 | frq3 | frq2 | frq1 | nsd | txd4 | txd3 | txd2 | txd1 |

# Table 3-43. Script block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| frequency index (frq) | 0-6 : integer index into freq block 7 : repeat flag (second octet with freq index follows) | The offset from the beginning of the frequency list. (An encoding of 0 refers to the first element in the frequency block.) |
| Non-standard definition (nsd) | nsd = 0: defined in SARPs per Table 3-34. nsd = 1: defined in CTRL transmission definition list (see Section 3.7.2.6.2) |  |
| Transmission definition index (txd) | 0-15 | The offset from the beginning of the transmission definition list (An encoding of 0 refers to the first element in the list.) |
| Repeat count (rpt) | 3 (encoded as 0) to 34 | The number of times to repeat the frequency and (nsd, txd) listed in octet 2. |

SECTION  DEFINITIONS FOR COMPACT POSITION REPORTING

INTRODUCTION

Note.— This section provides the definition of the compact position reporting (CPR) encoding scheme to be used by VDL Mode 4 stations.

PARAMETER SYMBOLS, DATA TYPES, CONSTANTS AND VARIABLES

Parameter symbols

Note.— The following parameter symbols are introduced in this section as they are defined below. Other parameters have been listed in previous sections of these SARPs.

Table 4-1. Summary of parameter symbols for CPR

| Parameter | Name | Section or table defined in |
| --- | --- | --- |
| TR1 | Maximum age for use in global decode | 4.10.2.1 |
| TR2 | Maximum time between global updates | 4.10.2.2 |

Data Types

All calculations in this section shall use signed integers.

Note.— Division is therefore considered to be integer division (the result of a division is truncated to an integer).

Results of calculations to perform encoding and decoding shall match the results when performed with 64-bit signed integer operations.

Constants

Constants used in the description of CPR shall have the values defined in Table 4-2.

Table 4-2. Constants used in CPR calculations

| Type | Name | Value | Description |
| --- | --- | --- | --- |
| Integer |  | 9 | Number of zones from 0° to 90° latitude. |
| Integer |  | 251 | Maximum value for longitude and latitude. |
| Integer |  | 212 -1 | Maximum transmitted latitude value. |
| Integer |  | 214 -1 | Maximum transmitted longitude value. |

Variables

Note 1.— CPR calculations convert between three representations of a station’s position: 1) The external representation of latitude and longitude which is meaningful to applications. 2) The internal representation which provides an integer representation of the position. 3) The link representation which is the encoded position. Tables 4-3 and 4-4 divide the variables and functions used in the CPR calculations into these three categories.

Variables used in CPR calculations shall have the type and range restrictions defined in Table 4-3. [A,B] shall mean greater than or equal to A and less than or equal to B. [A,B) shall mean greater than or equal to A and less than B.

Table 4-3. Variables used in CPR calculations

| Type | Name | Range | Description |
| --- | --- | --- | --- |
| External representation |  |
| Real | latitude | [0,90], [270, 360) | The input latitude Note that a latitude of [-90,0) maps to [270,360). |
| Real | longitude | [0,360) | The input longitude. |
| Internal representation |  |
| Integer | type, typelast | 0 or 1 | The type of CPR (0 = even, 1 = odd). |
| Integer | clatin, clonin |  | Latitude and longitude to be encoded. |
| Integer |  |  | Temporary variable number n. Only used to make expressions and functions more readable. |
| Integer | clatref, clonref |  | Reference latitude and longitude for local decoding. |
| Integer | x |  | Any integer. |
| Integer | pos1, pos2 |  | A latitude or longitude. |
| Integer | clatdec, clondec |  | Decoded latitude and longitude. |
| Integer | bits | 3, 5 or 7 | Number of bits for the magnitude offset. |
| Integer | latoffs, lonoffs | [0, 2bits -1] | Latitude and longitude offset. |
| Integer | slat, slon | 0 or 1 | Sign of the latitude and longitude offset. |
| Integer | latp | [0, 18] | The latitude patch. |
| Integer | lonp | [0, 35] | The longitude patch. |
| Link representation |  |
| Integer | cprf | 0 or 1 | CPR format even/odd. |
| Integer | lat |  | Encoded latitude. |
| Integer | lon |  | Encoded longitude. |
| Integer | latref, lat0, lat1 |  | Encoded latitude. |
| Integer | lonref, lon0, lon1 |  | Encoded longitude. |
| Integer | lat4, lat6, lat8 |  | Encoded latitude offset. |
| Integer | lon4, lon6, lon8 |  | Encoded longitude offset. |
| Integer | pid | [0, 179] | Encoded patch ID. |

Note 2.— All CPR computations use integer-valued longitude and latitude (in the range , where each step is  degrees). The conversion from arbitrary-precision real numbers is detailed in the following sections.

Functions

Functions used in CPR shall have the input parameters and return values defined in Table 4-4.

Note.— The detailed definitions for the functions are given in the following sections.

Table 4-4. Input parameters and return values for functions used in CPR calculations

| Type | Name | Description |
| --- | --- | --- |
| Function returns value in internal representation |  |
| Integer | nz (type) | Number of zones depending on the type (odd/even) of CPR format. |
| Integer | dlat (type) | Latitude patch size for type type. |
| Integer | nl (clatdec, type) | Looks up the value in the transition level table 4-5. |
| Integer | dlon (clatdec, type) | Longitude patch size at latitude clatdec for type typ5. |
| Integer | latoffs (lat, latref) | Latitude zone offset. |
| Integer | lonoffs (lon, lonref) | Longitude zone offset. |
| Integer | declat (clatref, lat, latref, type) | Local latitude decoding. |
| Integer | declon (clatdec, clonref, lon, lonref, type) | Local longitude decoding. |
| Integer | latseg (lat0, lat1, typelast) | Latitude segment for global decoding. |
| Integer | lonseg (lon0, lon1, clatdec, typelast) | Longitude segment for global decoding. |
| Integer | globalDeclat (lat0, lat1, typelast) | Global latitude global. |
| Integer | globalDeclon (lon0, lon1, clatdec, typelast) | Global longitude global. |
| Integer | fix (x) | Converts negative co-ordinates to positive. |
| Integer | lookup (clatin, type) | The value that corresponds to clatin and type in the transition level table. |
| Integer | diff (pos1, pos2) | The (shortest) distance between pos1 and pos2. |
| Integer | sign (pos1, pos2) | The sign of diff (pos1, pos2). |
| Integer |  | Calculates the true offset for the latitude offset given in bits bits. |
| Integer |  | Calculates the true offset for the longitude offset given in bits bits. |
| Integer | fullDeclat (lat, latp, type) | Decodes full position latitude. |
| Integer | fullDeclon (clatdec, lon, lonp, type) | Decodes full position longitude. |
| Function returns value in link representation |  |
| Integer | enclat (clatin, type) | Returns the CPR encoded value for clatin using type type. |
| Integer | enclon (clatdec, clonin, type) | Returns the CPR encoded value for clonin using type type. |
| Integer |  | The difference between clatin and clatdec expressed using bits bits. |
| Integer |  | The difference between lonin and clondec expressed using bits bits. |
| Integer | encpatch (latp, lonp) | Encode the patch id. |

Patch constants

Transition table

The function lookup(clatin, type) shall return the value in the number of zones (even or odd, depending on type) column in Table 4-5 for which the clatin value satisfies the restriction in the Range(integer) column.

Note.- The table is symmetrical for latitudes in the range   (i.e. [–90, 0) degrees).  This means that for latitude the range 0 – 90 degrees is mapped to  and -90 – 0 = 270 – 360 is mapped to .

Table 4-5. Transition table for lookup function

| Range (degrees) | Range (integer) | Number of zones Even | Number of zones Odd |
| --- | --- | --- | --- |
| <13.518674176405572 | <84559299976949 | 35 | 34 |
| [13.518674176405572,19.162797152134097) | [84559299976949,119863286269066) | 34 | 33 |
| [19.162797152134097,23.5247169626056) | [119863286269066,147147092426093) | 33 | 32 |
| [23.5247169626056,27.228512609375226) | [147147092426093,170314332279771) | 32 | 31 |
| [27.228512609375226,30.51543280332421) | [170314332279771,190874016391806) | 31 | 30 |
| [30.51543280332421,33.50899730287358) | [190874016391806,209598760787195) | 30 | 29 |
| [33.50899730287358,36.28248037044658) | [209598760787195,226946895939473) | 29 | 28 |
| [36.28248037044658,38.883571527761575) | [226946895939473,243216719782307) | 28 | 27 |
| [38.883571527761575,41.34536944123708) | [243216719782307,258615264457015) | 27 | 26 |
| [41.34536944123708,43.691961273699334) | [258615264457015,273293195154609) | 26 | 25 |
| [43.691961273699334,45.941527811563425) | [273293195154609,287364232684706) | 25 | 24 |
| [45.941527811563425,48.10819571981785) | [287364232684706,300916739329498) | 24 | 23 |
| [48.10819571981785,50.20320392571675) | [300916739329498,314021014573143) | 23 | 22 |
| [50.20320392571675,52.23567067731592) | [314021014573143,326734093052511) | 22 | 21 |
| [52.23567067731592,54.213116139057256) | [326734093052511,339103013392294) | 21 | 20 |
| [54.213116139057256,56.14182888275907) | [339103013392294,351167110605961) | 20 | 19 |
| [56.14182888275907,58.02712896497076) | [351167110605961,362959661644475) | 19 | 18 |
| [58.02712896497076,59.87356014060077) | [362959661644475,374509087692437) | 18 | 17 |
| [59.87356014060077,61.68503184003544) | [374509087692437,385839842234890) | 17 | 16 |
| [61.68503184003544,63.46492412462716) | [385839842234890,396973067553844) | 16 | 15 |
| [63.46492412462716,65.2161639281094) | [396973067553844,407927071618287) | 15 | 14 |
| [65.2161639281094,66.9412773021877) | [407927071618287,418717654880330) | 14 | 13 |
| [66.9412773021877,68.6424192797632) | [418717654880330,429358297069654) | 13 | 12 |
| [68.6424192797632,70.32137954962614) | [429358297069654,439860192688716) | 12 | 11 |
| [70.32137954962614,71.97955727480327) | [439860192688716,450232093501524) | 11 | 10 |
| [71.97955727480327,73.61788995824008) | [450232093501524,460479863588517) | 10 | 9 |
| [73.61788995824008,75.23670452702919) | [460479863588517,470605547878490) | 9 | 8 |
| [75.23670452702919,76.83542194177753) | [470605547878490,480605524480339) | 8 | 7 |
| [76.83542194177753,78.41195676510516) | [480605524480339,490466748984332) | 7 | 6 |
| [78.41195676510516,79.9614066817654) | [490466748984332,500158557411138) | 6 | 5 |
| [79.9614066817654,81.47284075679195) | [500158557411138,509612576768200) | 5 | 4 |
| [81.47284075679195,82.91989876526003) | [509612576768200,518663923862256) | 4 | 3 |
| [82.91989876526003,84.22404437738102) | [518663923862256,526821353991124) | 3 | 2 |
| [84.22404437738102,84.99999999999986) | [526821353991124,531674956009016) | 2 | 1 |
| ( 84.99999999999986 | ( 531674956009016 | 1 | 1 |

Patch size functions

The size of a latitude and longitude patch shall be:

FIXED DATA FIELD POSITION ENCODING

General

Given an arbitrary position latitude and longitude and a desired type (odd or even), the lat, lon  and cprf sub-fields in the fixed data field of the synchronization burst shall be set to the value of enclat() and enclon() computed as defined below.

Input parameters

latitude = latitude to be encoded.

longitude = longitude to be encoded.

type = type of  encoding (odd or even).

Calculations

Latitiude

Longitude

Note.— clatdec = declat (latitude, lat, lat, type) as defined in Section 4.4.3.2.

FIXED DATA FIELD POSITION LOCAL DECODING

General

When the position report processing state machine (see Section 4.10.3.2) indicates that local decoding shall be performed, then the fixed data field position shall be decoded using a single position report and an unambiguous global reference location. The calculation shall return the latitude, longitude and type sub-fields.

Note.— Local decoding uses a single report from the target and a reference location which can be either the receiver’s position (if only one type of report has been received from a target) or the last decoded position for the target (if the target’s unambiguous global position is known).

Input parameters

clatref = reference latitude.

clonref = reference longitude.

lat = CPR encoded latitude to be decoded.

lon = CPR encoded longitude to be decoded.

cprf = CPR format even/odd.

Calculations

Supporting Function

Latitude

Note.—  is defined in Section 4.7.3.1.

Longitude

Note.—   is defined in Section 4.7.3.2.

FIXED DATA FIELD POSITION GLOBAL DECODING

General

When the position report processing state machine (see Section 4.10.3.2) indicates that global decoding shall be performed, then the fixed data field position shall be decoded using the most recently received odd and even fixed data field positions. The calculation shall return the latitude, longitude and type fields.

Note.— The global decoding is guaranteed to succeed if the target has travelled less than 8.4 nmi between the odd and even position report and if the target has not crossed any transition latitude between the reports.

Input parameters

lat0 = even CPR encoded latitude to be decoded.

lon0 = even CPR encoded longitude to be decoded.

lat1 = odd CPR encoded latitude to be decoded.

lon1 = odd CPR encoded longitude to be decoded.

cprf = type of encoding (odd or even) for the most recent of the two CPR reports.

Transition level straddling

If, nl(globalDeclat(lat0, lat1, 1, 0) ( nl(globalDeclat(lat0, lat1, 0),0) then decoding as defined in 4.10.3.3 shall be computed instead of a global decode.

Note.— This situation occurs when the target has straddled a transition latitude.

Calculations

Latitude

Longitude

INFORMATION FIELD OFFSET ENCODING

General

Given a position and its fixed data field encoding (see Section 4.3), a high resolution offset encoding of size bits together with an additional bit indicating the sign of the offset shall be computed as defined below. The offset shall be encoded in the sub-fields lat4, lon4 (for bits = 3), lat6, lon6 (for bits = 5) or lat8, lon8 (for bits = 7) dependent on which synchronization burst variable part is to be transmitted (see Section 3).

Input parameters

clatin = latitude to be encoded.

clonin = latitude to be encoded.

lat = the CPR encoded latitude (see Section 4.3).

lon = the CPR encoded longitude (see Section 4.3).

type = type of CPR (odd or even).

bits = number of bits in magnitude of the offset.

Calculations

Supporting functions

Latitude

Longitude

INFORMATION FIELD OFFSET DECODING

General

To decode the information field latitude and longitude offsets, the offset values defined below shall be added to the position from the fixed data field position decoding (either local or global) to determine the actual target position.

Input parameters

lat4, lat6, lat8 = received latitude offset.

lon4, lon6, lon8 = received longitude offset.

type = type of encoding (odd or even).

clatdec = the target’s decoded latitude (see Section 4.4.3.2)

Calculations

Latitude

Note.— tmp7 is defined in Section 4.6.3.2.

Longitude

Note.— tmp8 is defined in Section 4.6.3.3.

PATCH ID ENCODING

General

When a station sends an unambiguous global position in a single message, then it shall transmit the value of encpatch() as the patch ID (pid).

Input parameters

clatin = latitude to encode.

clonin = longitude to encode.

type = type of encoding (odd or even).

Calculations

PATCH ID DECODING

General

The patch ID decoding shall use the received patch ID , lat and lon subfields and decode this to a position in latitude and longitude, which is globally unambiguous.

Input parameters

lat = CPR latitude to decode.

lon = CPR longitude to be decode.

type = type of encoding (odd or even).

pid = encoded patch id

Calculations

Latitude

Longitude

POSITION REPORT PROCESSING

Services

The PECT (see Section 4.10.3.1) shall maintain sufficient history of received targets to enable unambiguous global position to be determined.

Position report parameters

The position report parameters shall be as defined in Table 4-6.

Table 4-6. Position report processing parameters

| Symbol | Parameter name | Minimum | Maximum | Default | Increment |
| --- | --- | --- | --- | --- | --- |
| TR1 | Maximum age for use in global decode | 1 sec | 60 sec | 30 sec | 1 sec |
| TR2 | Maximum time between global updates | 1 sec | 240 sec | 60 sec | 1 sec |

Parameter TR1 (maximum age for use in global decode)

The parameter TR1 shall be the maximum age of a report for its use in a global decode. The timer shall be started (or restarted) as defined in Table 4-7. If it expires the report shall not be valid for use in a global decode.

Parameter TR2 (maximum time between global updates)

The parameter TR2 shall be the maximum time between global updates. The timer shall be started (or restarted) as defined in Table 4-7.

Position report processing procedures

Position report processing state machine

For each station maintained in the PECT (see Section 1.5.6.2), the station shall maintain the record of the last received position report and a position report processing state machine with the following states:

a)	State 1 shall indicate that no position report has been received and represents the initial state of the position report processing state machine;

b)	State 2 shall indicate that a position report has been received but that no position has been decoded;

c)	State 3 shall indicate that a position report has been received and that a local position has been decoded;

d)	State 4 shall indicate that a position report has been received and that a global position has been decoded.

Position report processing state machine transitions

On receipt of a position report, the station shall update its state machine as defined in Table 4-7 and report target position quality to the application.

Note 1.— State transitions depend on:

a)	the initial state;

b)	the type (even or odd) of the last received position report;

c)	the type of received position report (even/odd/with patch ID/without patch ID);

d)	whether the station has knowledge of its own position;

e)	the state of timers TR1 and TR2.

Note 2.— The station carries out the actions defined as “C=” in Table 4-7:

a)	 C = GL: carry out global decoding as defined in Section 4.5 if there is no patch ID, or as defined in E9 if there is a patch ID;

b)	C = L1: carry out local decoding using own position as reference, as defined in Section 4.4;

c)	C = L2: carry out local decoding using the last known position of the transmitting station as reference, as defined in Section 4.4;

d)	C = NO: no decode is carried out.

Note 3.— The station restarts timers TR1 and TR2 as indicated in Table 4-7:

a)	resTR1: restart timer TR1;

b)	resTR2: restart timer TR2.

Note 4.— The state machine enters the state indicated as “N=” in Table 4-7 and reports the target position quality to the application:

a)	if the final state is 1 or 2, the station indicates a target position quality of “none”;

b)	if the final state is 3, the station indicates a target position quality of “local”;

c)	if the final state is 4, the station indicates a target position quality of “global”.

Table 4-7. State transitions for position report processing

| In State |  |  | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Last report |  |  | None | Even | Odd | Even | Odd | Even | Odd |
| Target position quality |  |  | None | None | None | Local | Local | Global | Global |
| Received position report type | Own Posi- tion | Timers (exp = expired) |  |  |  |  |  |  |  |
|  |  | TR1 | TR2 |  |  |  |  |  |  |  |
| Even or odd with patch ID | not appli-cable | not appli-cable | not appli-cable | N= 4 C= GL resTR1 resTR2 | N= 4, C= GL resTR1, resTR2 | N= 4, C= GL resTR1, resTR2 | N= 4, C= GL resTR1, resTR2 |
| Even | Yes | Not exp | Not exp | N= 3 C= L1 ResTR1 | N= 3 C= L1 resTR1 | N= 4 C= GL resTR1 resTR2 | N= 3 C= L1 resTR1 | N= 4 C= GL resTR1 resTR2 | N= 4 C= L2 resTR1 | N= 4 C= GL resTR1 resTR2 |
|  |  |  | Exp |  |  |  |  |  | N= 3 C= L1 resTR1 |  |
|  |  | Exp | Not exp |  |  | N= 3 C= L1 resTR1 |  | N= 3 C= L1 resTR1 | N= 4, C= L2, resTR1 |
|  |  |  | Exp |  |  |  |  |  | N= 3, C= L1, resTR1 |
|  | No | Not exp | Not exp | N= 2 C= NO ResTR1 | N= 2 C= NO resTR1 | N= 4 C= GL resTR1 resTR2 | N= 2 C= NO resTR1 | N= 4 C= GL resTR1 resTR2 | N= 4 C= L2 resTR1 | N= 4 C= GL resTR1 resTR2 |
|  |  |  | Exp |  |  |  |  |  | N= 2 C= NO resTR1 |  |
|  |  | Exp | Not exp |  |  | N= 2 C= NO resTR1 |  | N= 2 C= NO resTR1 | N= 4, C= L2, resTR1 |
|  |  |  | Exp |  |  |  |  |  | N= 2, C= NO, resTR1 |
| Odd | Yes | Not exp | Not exp | N= 3 C= L1 ResTR1 | N= 4 C= GL resTR1 resTR2 | N= 3 C= L1 resTR1 | N= 4 C= GL resTR1 resTR2 | N= 3 C= L1 resTR1 | N= 4 C= GL resTR1 resTR2 | N= 4 C= L2 resTR1 |
|  |  |  | Exp |  |  |  |  |  |  | N= 3 C= L1 resTR1 |
|  |  | Exp | Not exp |  | N= 3 C= L1 resTR1 |  | N= 3 C= L1 resTR1 |  | N= 4, C= L2, resTR1 |
|  |  |  | Exp |  |  |  |  |  | N= 3, C= L1, resTR1 |
|  | No | Not exp | Not exp | N= 2 C= NO ResTR1 | N= 4 C= GL resTR1 resTR2 | N= 2 C= NO resTR1 | N= 4 C= GL resTR1 resTR2 | N= 2 C= NO resTR1 | N= 4 C= GL resTR1 resTR2 | N= 4 C= L2 resTR1 |
|  |  |  | Exp |  |  |  |  |  |  | N= 2 C= NO resTR1 |
|  |  | Exp | Not exp |  | N= 2 C= NO resTR1 |  | N= 2 C= NO resTR1 |  | N= 4, C= L2, resTR1 |
|  |  |  | Exp |  |  |  |  |  | N= 2, C= NO, resTR1 |

State machine transitions for transition level straddling

When a position report is received from a station which fulfils:

a)	the conditions for the initial state, last received report type, received report type, own position and timer states defined in Table 4-8;

b)	the conditions defined in Section 4.5.3 are met (because the station has crossed a transition latitude),

the receiving station shall update its state machine as defined in Table 4-8 and report the target position quality to the application. Otherwise the station will process the report as defined in Section 4.10.3.2.

Table 4-8. State transitions for position report processing (transition level straddling)

| In State | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Last report | None | Even | Odd | Even | Odd | Even | Odd |
| Target position quality | None | None | None | Local | Local | Global | Global |
| Received position report type | Own Posi-tion | Timers (exp = expired) |  |  |  |  |  |  |  |
|  |  | TR1 | TR2 |  |  |  |  |  |  |  |
| Even | Yes | Not exp | Not exp | See Table 5-7 | See Table 5-7 | N= 3 C= L1 resTR1 | See Table 5-7 | N= 3 C= L1 resTR1 | See Table 5-7 | N= 4 C= L2 resTR1 |
|  |  |  | Exp |  |  |  |  |  |  | N=3 C= L1 res TR1 |
|  | No | Not exp | Not exp |  |  | N= 2 C= NO resTR1 |  | N= 2 C= NO resTR1 |  | N= 4 C= L2 resTR1 |
|  |  |  | Exp |  |  |  |  |  |  | N= 2 C= NO resTR1 |
| Odd | Yes | Not exp | Not exp | See Table 5-7 | N= 3 C= L1 resTR1 | See Table 5-7 | N= 3 C= L1 resTR1 | See Table 5-7 | N= 4 C= L2 resTR1 | See Table 5-17 |
|  |  |  | Exp |  |  |  |  |  | N=3 C=L1 resTR1 |  |
|  | No | Not exp | Not exp |  | N= 2 C= NO resTR1 |  | N= 2 C= NO resTR1 |  | N= 4 C= L2 resTR1 |  |
|  |  |  | Exp |  |  |  |  |  | N= 2 C= NO resTR1 |  |

— END —