## Slide 1: Aviation System Block Upgrades Module N° B0-84 Initial Capability for Ground-based Cooperative Surveillance
SIP/ASBU/2012-WP/24C
Workshop on preparations for ANConf/12 − ASBU methodology
(Bangkok, 14-18/Nadi, 21-25 May 2012)

## Slide 2: Module N° B0-84 Initial Capability for Ground-based Cooperative Surveillance
Summary | This module provides initial capability for lower cost ground surveillance supported by new technologies such as ADS-B OUT and wide area multilateration systems | 
Main Performance Impact | KPA- 02 Capacity, KPA-03 Efficiency, KPA-09 Predictability KPA-10 Safety | 
Operating Environment/Phases of Flight | All airborne flight phases in continental or subsets of oceanic airspace and on aerodrome surfaces | 
Applicability Considerations | This capability is characterized by being dependent and cooperative. The overall performance is affected by ADS-B out performance and equipage. | 
Global Concept Component(s) | CM – Conflict Management | 
Global Plan Initiatives () | -9 Situational awareness -16 Decision support and alerting systems | 
Main Dependencies |  | 
Global Readiness Checklist |  | Status (ready now or estimated date)
 | Standards Readiness | Ready now
 | Avionics Availability | Ready now
 | Ground Systems Availability | Ready now
 | Procedures Available | Ready now
 | Operations Approvals | Ready now

## Slide 3: Module N° B0-84 - Baseline
Air to ground aircraft position and surveillance is accomplished
  Primary Radar; and
  Secondary Radar

## Slide 4: Module N° B0-84 – Change Brought by the Module
ADS-B:
  advanced surveillance technology allowing avionics to broadcast an aircraft’s identification, position, altitude, velocity, etc
Multilateration :
  new technique providing independent cooperative surveillance.
  initially deployed on main airports to make the surveillance of aircraft on the surface. The technique is now used to provide surveillance over wide area (WAM).

## Slide 5: Module N° B0-84 – Intended Performance Operational Improvement
Safety | Reduction of the number of major incidents. Support to Search and Rescue
Capacity | Typical separation minima are 3 NM or 5 NM enabling a significant increase in traffic density compared to procedural minima.
CBA | either comparison between procedural minima and 5NM separation minima would allow an increase of traffic density in a given airspace -or comparison between installing/renewing SSR Mode S stations using Mode S transponders and installing ADS-B OUT (and /or Multilateration systems).

## Slide 6: Module N° B0-84 – Necessary Procedures (Air & Ground)
The relevant PANS-ATM (Doc 4444) provisions are available.

## Slide 7: Module N° B0-84 – Necessary System Capability
Avionics
  For ADS-B surveillance services, aircraft must be equipped with ADS-B OUT.
  For multilateration, aircraft need to be equipped with Mode S radar transponders
Ground Systems
  Units providing surveillance services must be equipped with a ground-based surveillance data processing system and flight data processing system
  Units may provide ADS-B surveillance in environments where there is full or partial avionics equipage depending on the capabilities and procedures of the ATC system.
  ATC Systems must also be designed to enable the delivery of separation services between ADS-B-to-ADS-B and ADS-B-to-radar and fused targets

## Slide 8: Module N° B0-84 – Training and Qualification Requirements
Controllers must receive specific training for separation provision, information service and search and rescue based on the ADS-B and WAM systems in use.
Training in the operational standards and procedures are required for this module
Qualifications requirements are identified in the regulatory requirements

## Slide 9: Module N° B0-84 –Regulatory/standardization needs and Approval Plan (Air & Ground)
Nil

## Slide 10: Module N° B0-84 – Reference Documents
Standards
  ICAO ANNEX 10 — Aeronautical Telecommunications, Volume IV  Aeronautical Radio Frequency Spectrum Utilization;
  ICAO DOC 9871, Technical Provisions for Mode S Services and Extended Squitter;
  RTCA MOPS DO260 and DO260A EUROCAE ED102 and ED102A.
Procedures
  ICAO Doc 4444, Procedures for Air Navigation Services — Air Traffic Management;
Guidance Material
  ICAO DOC 9924, Aeronautical Surveillance Manual;
  ICAO Assessment of ADS-B and Multilateration Surveillance to Support Air Traffic Services and Guidelines for Implementation (Circular 326);
  ICAO Asia Pacific: ADS-B implementation guidance document.

## Slide 11: Module N° B0-84 Implementation - Benefits and Elements
Initial Capability for Ground-based Cooperative Surveillance
Benefits: Capacity and safety
Elements:
  ADS-B
  Multilateration
  To be reflected in ANRF