## Slide 1: GNSS SURVEY OUTCOME
Secretariat
ICAO APAC Office
GNSS IMPLEMENTATION SEMINAR
26 MARCH 2012

## Slide 2: GNSS SURVEY
APANPIRG noted with concern slow progress of GNSS implementation in the region
Survey questionnaire developed with the active cooperation of HQ and some external agencies
Questionnaire circulated 30 November 2010
Reminder issued on 11 May 2011.
24 Responses received till July 2011 (40% response rate)
Notes: APANPIRG in its Twenty First Meeting held from 6 to 10 September 2010 noted with concern slow progress of GNSS implementation in the region. It was noted that implementation of some of the GNSS applications like PBN, ADS-B etc. were progressing slowly and it was agreed that implementation of GNSS is essential for the enhancement of safety and capacity of aircraft operation.
A survey questionnaire was developed to assess the level of GNSS implementation in the region, with the help of HQ and NSP members.
The questionnaire was circulated through ICAO APAC Office State Letter T 8/5.10:AP176/10(CNS) dated 30 November 2010 and a reminder was issued on 11 May 2011.
Till July 2011, 24 responses were received at a total response rate of 40%. No additional response since then has been received.

## Slide 3: GNSS SURVEY- 1
1. Has your State developed any plan to implement GNSS?
Out of the 24 States that responded to the survey questionnaire, 19 States informed that they had developed plans for the implementation of GNSS, but 5 States responded that they had not developed any such plan.
Recommendation: Workshop may consider developing a recommendation for the States, which have not developed their integrated GNSS implementation plan to consider developing one
SURVEY ITEM | YES | NO
Has your State developed any plan to implement GNSS (Yes, No) | 19 | 5
GNSS IMPLEMENTATION SEMINAR

## Slide 4: GNSS SURVEY - 2
Approval
Most of the Administrations provide on a Supplementary Basis for RNAV, SIDs/STARs, Non-Precision Approach, Approach with Vertical Guidance and Precision Approach. Many Administrations are also providing approval for Oceanic/Remote Area on a “Sole Means” basis.
SURVEY ITEM | SUPPLEMENTARY | ONLY MEANS | SUPP/OM
Oceanic/Remote Area | 10 | 6 | 3
RNAV | 14 | 2 | 4
SIDs/STARs | 13 | 4 | 3
Non Precision Approach | 13 | 5 | 2
Approach with Vert Guidance (Baro V-Nav, SBAS) | 6 | 2 | 2
Precision Approach (GBAS/GLS) | 2 | 2 | 1

## Slide 5: GNSS SURVEY - 3
Initiation of GNSS-based Services
Some States initiated GNSS implementation in their regions after receiving request for provision from the airline operators, some States took their own initiative for GNSS implementation
SURVEY ITEM | YES | NO
Has your Administration received requests from domestic/international aircraft operators to provide GNSS-based services? | 18 | 5

## Slide 6: GNSS SURVEY - 6
Aircraft Equipage
Many of the Administrations did not provide any information in respect of level of aircraft equipage. In some Administrations up to 97% of the domestic aircraft were reported to be equipped, but in one Administration the level of equipage was as low as 4%. The equipage for international operations varied between 12 and 100%. Level of aircraft equipage may be an important factor for promoting adoption of GNSS
SURVEY TASK |  | LEVEL
What percentage of aircraft, registered in your State is equipped with GNSS avionics? |  | 
A) Domestic with C129 or equivalent (or C145/146 etc.) |  | >10% - 13
B) Int’l C129 or equivalent (or C145/146) |  | >50% - 12

## Slide 7: GNSS SURVEY - 7
Instrument Approaches
SURVEY ITEMS | NO.
What is the number of runway in your State that meet instrument standards but do not have instrument approach or are served by a circling procedure only? | 
Japan | 81
PNG | 5
Philippines | 13
ROK | 9
Singapore | 1
USA | Very Few
French Polynesia | 23
North Caledonia | 3

## Slide 8: GNSS SURVEY - 8
Decommissioning of Conventional NAVAIDS
ICAO recommends transitioning from terrestrial navigation systems to the Global Navigation Satellite Systems. Transition is required to be planned and supported by development of regulatory and operational environment. States, may however opt to retain certain number of terrestrial systems to support operations in the event of failure of GNSS
SURVEY ITEM | YES | NO
Has your Administration planned the decommissioning of conventional nav-aids | 15 | 9

## Slide 9: GNSS SURVEY - 9
Decommissioning schedule
Decommissioning of terrestrial systems is required to be initiated after safety impact of this activity has been assessed. Similarly continued investment towards implementation of terrestrial systems will be based on assessment of the situation.
SURVEY ITEM | <=5 YRS | 5-10 YRS | =>10 YRS
If the answer to Item 8 is ‘Yes’, then when is the planned decommissioning scheduled to start | 7 | 3 | 2

## Slide 10: GNSS SURVEY - 11
GNSS Manual
GNSS Manual or Doc 9849 describes the concept of operation that uses the core satellite constellation and augmentation systems. In addition to providing basic explanation of satellite navigation technology including satellite system, augmentation systems and avionics, it discusses implementation considerations that will assist the States in planning for orderly introduction of service based on GNSS guidance. It also informs about future prospects for evolution of GNSS
SURVEY ITEM | YES | NO
Have you used GNSS Manual (Doc 9849) as a reference when considering the implementation of GNSS operations? | 22 | 1

## Slide 11: GNSS SURVEY - 13
Augmentation Systems
With MSAS, GAGAN and COMPASS (SBAS Augmentation) operating in the region, a considerable portion of the airspace is likely to be covered by SBAS. Some States have opted to enhance the navigation performance in their airspace by planning to have SBAS. GBAS is also being planned by many States to enhance approach and landing performance.
SURVEY ITEM | YES | NO
Does your State have any plans to implement augmentation systems? |  | 
SBAS | 6 | 17
GBAS | 14 | 9

## Slide 12: GNSS SURVEY - 15
GNSS as element for ILS
Some States have permitted the use of GPS based FMS to perform distance checks as a part of ILS let down procedures, where DME is not available. APANPIRG/22 agreed that GNSS should be considered for including as an ILS component.
Recommendation: Workshop invited to develop a recommendation on the issue for the consideration of CNS/MET SG/16
SURVEY ITEM | YES | NO
Do you have ILS systems with marker beacons only (no DME) for aircraft to perform altitude/distance cross checks? If yes, do you allow the use of FMS (GPS) based computed distance checks instead? | 4 | 20

## Slide 13: GNSS SURVEY - 15
ADS-C
Automatic Dependent Surveillance – Contract or ADS-C has been used by many States to support situation awareness at the Air Traffic Control position. ADS-C is normally complemented by Controller Pilot Data Communication or CPDLC another satellite based application.
SURVEY ITEM | YES | NO
Is your State using ADS-C | 13 | 11

## Slide 14: GNSS SURVEY - 16
ADS-B
SURVEY ITEM | YES | NO
Does your State have any plans to implement ADS-B based surveillance services | 22 | 2
a) If answer is ‘Yes’, then when will it be implemented | Implemented -- 5 2012-2015 – 11 After 2015 -- 1 | 
b) Will it be implemented in whole or partial airspace | Whole airspace -- 9 Partial airspace -- 10 | 
ADS-B implementation planned for enhanced surveillance in: |  | 
i) Non RADAR Area (NRA) | 16 | 
ii) RADAR Area (RDA) | 14 | 
iii) Aerodrome/Terminal Area (APT) | 13 | 
iv) Support surveillance data sharing | 9 | 

## Slide 15: GNSS SURVEY - 17
Help/Guidance
APANPIRG/22, based on the response from the States/Administrations agreed that a Seminar/Workshop be conducted in conjunction with the PBN Task Force meeting and adopted Conclusion 22/26.
SURVEY ITEM | YES | NO
Does your State need any help/guidance from ICAO in the development of GNSS plan and its implementation | 17 | 7
Notes: Conclusion 22/26 – Workshop on GNSS implementation
That, ICAO be invited to organize a Workshop on GNSS implementation to address issues identified through the GNSS implementation survey conducted in 2010.

## Slide 16: RECOMMENDATIONS
Recommendation 1: Workshop may consider developing a recommendation for the States, which have not developed their integrated GNSS implementation plan to consider developing one
Recommendation 2: Workshop may consider to recommend to ICAO, inclusion of GNSS as an element of ILS for the purpose of distance verification
Recommendation 3: Workshop may consider to develop a guidance on how to support GNSS implementation efforts in the region.
Notes: Meeting is invited to consider developing a recommendation in the form of a draft Conclusion urging the States which have not developed their integrated GNSS implementation plan to develop one to include various considerations like the regulatory environment, training and certification arrangements etc.
Some States have informed that they are permitting the use of FMS (GNSS) for distance verification in ILS, where colocated DME is not available. APANPIRG after reviewing this arrangement came to a conclusion that a recommendation should be made to ICAO to consider inclusion of GNSS as an elevement of ILS for the purpose of distance of verificaiton.
Workshop is also invited to develop a recommendation as to how the implementation of GNSS in the region can be supported. The recommendation may include seminar or training programmes on specific elements or requirements of GNSS or may be on the flight validation of various GNSS applications etc.

## Slide 17
THANK YOU